## Slide 1: Non CE12: Deblocking boundary strength and filtering process simplifications
Anand Kotra, Matthias Narroschke, Thomas Wedi
Panasonic Corporation
7th JCT-VC meeting, Geneva 21.-30. November 2011

## Slide 2: Summary
Proposed HM4.0 compliant WD and software cleanup
  Re-assignment of BS
  Clean Tc derivation
  Removal of processing steps for BS=0
Experiments and results
Conclusion
Notes: Jul 31, 2026
<number>
Give Numbering -> 3 separate items are being proposed

## Slide 3: Re-assignment of BS
HM-4.0
Proposal
Compliant with HM-4.0 since BS=3,4 as well as BS=1,2 are not further distinguished
Notes: Jul 31, 2026
<number>
1) Advantage software cleanup and reduction of cycles

## Slide 4: Clean Tc derivation
Current HM- 4.0
Tc (treshold) is derived as follows:
Step1: If (BS > 2) then tcoffset =2 else tcoffset = 0
Step2: indexTC = clip3(0, MAX_QP + 4, QP + tcoffset)
Proposal
Tc (treshold) is derived as follows:
Step1: indexTC = clip3(0, MAX_QP+ 4, QP+ bS-1)
Unnecessary step1 removed (Compliant with HM4.0)
Notes: Jul 31, 2026
<number>
Reassign BS values and then its possible to use the equation in the proposal
Compliant with G174, change this sentence

## Slide 5: Removal of unnecessary processing steps for BS=0
Current HM- 4.0 and WD
Tc, ß and other thresholds are calculated even when BS=0
Proposal
Do not calculate Tc, ß and other thresholds when BS=0
(Frequency: >50%)
Unnecessary processing removed (Compliant with HM4.0)
Notes: Jul 31, 2026
<number>
Advantage – software clean up

## Slide 6: Conclusion
Proposed WD and software cleanup
  Re-assignment of BS
  Clean Tc derivation
  Removal of processing steps for BS=0
Results:
  Cleanup of WD and Software
  Reduced operations in deblocking
  Compliant with HM4.0
  Combinable with parameter adjustment in slice level, e.g. JCTVC-G174
Cross checked by Qualcomm – JCTVC-G385
Proposal: Inclusion into next version of WD and HM