## Slide 1: Non CE12:Deblocking bug fix for CU-Varying QPs and IPCM blocks
Anand Kotra, Matthias Narroschke, Thomas Wedi
Panasonic Corporation
7th JCT-VC meeting, Geneva 21.-30. November 2011

## Slide 2: Outline
Deblocking for CU-Varying QPs
Deblocking for IPCM blocks
Conclusion
Notes: Jul 31, 2026
<number>

## Slide 3: Motivation
HM4.0: When CU-varying QPs are used, the QPs of two neighboring blocks may differ
Problem: Only one of the QPs is used for deblocking control
Approach: Control deblocking by both QPs as in H.264/MPEG-4 AVC
Notes: Jul 31, 2026
<number>

## Slide 4: Modifications
Deblocking On/Off-Decision
  Use of average QP to derive
Strong/Weak-Decision
  Use of average QP to derive and
Introduced tc-clipping in strong filter
  Individual based on the QP of each side
tc-clipping in weak filter (p0,q0)
  Use of average QP to derive
On/Off-Decisions and tc-clipping in weak filter (p1,q1)
  Individual and based on the QP of each side
Notes: Jul 31, 2026
<number>

## Slide 5: Objective Results – With class F
 | BD-Bit rate [%] |  |  |  | Encoder run time ratio [%] |  |  |  | Decoder run time ratio [%] |  |  | 
 | W-Rand | W-AVC-Rand | W+S-Rand |  | W-HM | W-AVC-HM | W+S-HM |  | W-HM | W-AVC-HM | W+S-HM | 
I HE | -0.1 | -0.1 | -0.2 |  | 105 | 104 | 100 |  | 100 | 98 | 102 | 
I LC | -0.1 | -0.1 | -0.2 |  | 109 | 106 | 100 |  | 101 | 96 | 102 | 
RA HE | -0.1 | 0.0 | -0.1 |  | 130 | 114 | 100 |  | 100 | 96 | 100 | 
RA LC | -0.1 | 0.0 | -0.1 |  | 101 | 94 | 100 |  | 99 | 94 | 101 | 
LDB HE | -0.1 | 0.0 | -0.1 |  | 92 | 100 | 100 |  | 99 | 94 | 100 | 
LDB LC | 0.0 | 0.0 | -0.1 |  | 96 | 81 | 100 |  | 99 | 95 | 100 | 
LDP HE | -0.1 | 0.0 | -0.1 |  | 106 | 96 | 100 |  | 99 | 96 | 101 | 
LDP LC | -0.1 | -0.1 | -0.1 |  | 97 | 93 | 101 |  | 109 | 97 | 101 | 
W-Rand : Weak filter modifications compared to HM-4.0 [ with Random QP assignment]
W-AVC-Rand : Weak filter modifications compared to AVC like deblocking [ with Random QP assignment]
W+S-Rand: Weak and strong filter modifications compared to HM-4.0 [ with Random QP assignment]
W-CE4 : Weak filter modifications compared to HM-4.0 [with CE4 subtest 1, psycho visual anchor)

## Slide 6: Motivation
HM4.0: QP=0 is used to deblock IPCM blocks
Problem: IPCM blocks may contain quantization noise and deblocking control by higher QP may be desirable
Approach: Transmit slice level QP_PCM, which is used for deblocking control of IPCM blocks
Notes: Jul 31, 2026
<number>

## Slide 7: Conclusion
Control of deblocking filter by both QPs
  Average bit rate reduction when QPs assigned randomly at CU level:
    Compared to HM4.0: 0.1%
    Compared to H.264/MPEG-4 AVC-like deblocking:
      0.1% in IHE,ILC, RALC
      0.0% else
  Average bit rate reduction when QPs assigned as in CE4 subtest 1:
      0.1% in LDHE
      0.0% else
Transmission of a seperate QP_PCM for IPCM blocks
  More efficient deblocking of IPCM coded blocks in case they contain quantization noise
Proposal: Inclusion into next version of HM/WD