## Slide 1: JCTVC-G643 AHG21: On reference picture list construction and reference picture marking
M. M. Hannuksela, S. R. Gopalakrishna (Nokia)
JCTVC-G643

## Slide 2: Summary of the Proposal
Reference picture list descriptions (list 0, 1, idle) instead of
  reference picture list initialization and modification and reference picture marking of HEVC WD4; or
  reference picture sets and reference picture list initialization and modification of JCTVC-G021
For reference picture list descriptions or reference picture sets:
Two-part coding of POC differences as a “short-term” part and a ue(v)-coded “long-term” part
Use of the two-part coding of POC differences for determining the marking “used for short-term reference” or “used for long-term reference”
temporal_id-based POC granularity for POC difference coding
JCTVC-G643

## Slide 3: Reference Picture List Description Motivation
Observation: reference picture sets (JCTVC-G021) resembled reference picture lists
Reference picture list initialization and modification are avoided if reference picture lists are described instead of reference picture sets
  Reduction of decoding process specification from >4 pages (HM WD4) or ~3 pages (JCTVC-G021) to ~2 pages
  Fewer processing steps: reference picture lists are described directly instead of two or three steps needed for reference picture set construction, reference picture list initialization, and (optional) reference picture list modification
Bitrate overhead is similar to that of reference picture sets, e.g. reported number of bits required in the PPS for the entire sequence:
JCTVC-G643
 | JCTVC-G021 (as reported in JCTVC-198r1) | JCTVC-G198r1 | JCTVC-G198r1 (with delta-POC coding) | JCTVC-G643r1
Random access | 288 | 177 | 144 | 157
Low delay | 201 | 143 | 106 | 132
Notes: <number>

## Slide 4: Reference Picture List Description Coding
Similar to reference picture sets
A number of pairs of reference picture list 0 and list 1 descriptions can exist in PPS
  Can be “fully” described; or
  Can be described as subsets from other descriptions (similarly to JCTVC-G198r1)
In slice header, an index to reference picture list pair in PPS can be given or reference picture list description can be included
ref_pic_list_copy_flag to avoid repetition of the head of list 0 and in the tail of list 1 or vice versa
Two ways to describe reference pictures not used as reference for the current picture but still kept marked as “used for reference”
  Include in reference picture list 0 or 1 with a higher index than the maximum active index
  Include in specific Idle reference picture list
  Depends on the referencing structure which way is more efficient
JCTVC-G643

## Slide 5: Long-Term Reference Pictures
Coding in reference picture list description
  Similar to JCTVC-G713
  Maximum short-term POC difference (maxPocDiff) relative to the POC of the current picture is specified in SPS
  For all reference pics, a “short-term” part (fgPocDiff) is in the range of 1 to maxPocDiff is in the syntax
  Number of and reference indexes for long-term pictures are in the syntax
  For each long-term picture, a POC cycle (pocCycle) in units of maxPocDiff is in the syntax
  The POC difference is pocCycle * maxPocDiff + fgPocDiff
Marking as “used for long-term reference” when pocCycle is present, otherwise “used for short-term reference”
JCTVC-G643

## Slide 6: temporal_id-based POC granularity
Motivation
  Encoders may use a regular GOP pattern and assign POC values proportional to a constant picture sampling interval
  POC granularity values given in SPS for each temporal_id are used to quantize the POC differences indicated in the reference picture list description syntax structures to improve compression efficiency
Constraint: POC granularity for temporal_id N = n * POC granularity for temporal_id N+1 (n=1,2,3,…)
POC granularity 1 can used for irregular POC assignment pattern
JCTVC-G643

## Slide 7: Summary of the Proposal
Reference picture list descriptions (list 0, 1, idle) instead of
  reference picture list initialization and modification and reference picture marking of HEVC WD4; or
  reference picture sets and reference picture list initialization and modification of JCTVC-G021
For reference picture list descriptions or reference picture sets:
Two-part coding of POC differences as a “short-term” part and a ue(v)-coded “long-term” part
Use of the two-part coding of POC differences for determining the marking “used for short-term reference” or “used for long-term reference”
temporal_id-based POC granularity for POC difference coding
JCTVC-G643