## Slide 1: Multiple Level Significance Maps for Large Transform Units
JCTVC-G644
Nguyen Nguyen, Tianying Ji, Dake He, Gaelle Martin-Cocher, and Lin Song

## Slide 2: Two-level significance map
Objective:
  Reduce the number of bins (significicant_coeff_flags) to be decoded in large transforms (16x16, 32x32).
Proposal
  Use two-level significance map
    Higher level: significant_coeffgroup_flag determines whether a group of coefficients has non-zero coefficients.
    Lower level: significant_coeff_flag

## Slide 3: Cost and Benefit
Cost: Introduce 4 contexts for decoding significant_coeffgroup_flag
  Two for luma and two chroma
    x a
    b
    ctx = max {a, b}
    if both a and b are 1, coding of the current significant_coeffgroup_flag is skipped as is the significant_coeffgroup_flag for the group including the DC position.
Benefit:
  No longer necessary to encode/decode significance flags in groups with significant_coeffgroup_flag = 0
  Overall reduction in bins to be decoded by BAC, with negligible impact on rate distortion performance

## Slide 4: Example
16x16 TU with 4x4 coefficient groups:
---------------------------------------------------------
| 5 2 0 1 | 1 0 0 0 | 1 1 1 0 | 0 0 0 0 |
| 5 0 2 1 | 2 0 1 1 | 0 2 1 0 | 0 0 0 0 |
| 0 1 0 0 | 1 0 1 1 | 0 1 1 1 | 0 0 0 0 |
| 0 0 0 1 | 1 1 1 1 | 0 0 1 0 | 0 0 0 0 |
---------------------------------------------------------
| 1 1 0 0 | 1 0 1 0 | 0 1 0 1 | 0 0 0 0 |
| 2 1 0 1 | 0 0 1 0 | 1 0 0 1 | 0 0 0 0 |
| 0 0 1 0 | 0 0 1 0 | 1 0 0 0 | 0 0 0 0 |
| 1 0 0 1 | 1 0 1 0 | 0 0 0 0 | 0 0 0 0 |
---------------------------------------------------------
| 0 1 1 1 | 0 1 0 1 | 1 1 1 0 | 0 1 0 0 |
| 0 0 1 0 | 0 1 1 1 | 0 0 0 1 | 0 0 0 0 |
| 1 0 0 1 | 0 0 0 0 | 1 1 0 0 | 1 0 0 0 |
| 0 0 1 0 | 0 0 0 0 | 1 1 0 0 | 0 0 0 0 |
---------------------------------------------------------
| 0 0 0 0 | 0 0 0 0 | 0 0 0 0 | 0 0 0 0 |
| 0 0 0 0 | 0 0 0 0 | 0 0 0 0 | 0 0 0 0 |
| 0 0 0 0 | 0 0 0 0 | 0 0 0 0 | 0 0 0 0 |
| 0 0 0 0 | 0 0 0 0 | 0 0 0 0 | 0 0 0 0 |
---------------------------------------------------------
Last

## Slide 5: Bin savings and BD-rate against HM4.0 anchor
 | All Intra HE |  |  | 
 | Total | Sig | 4,8 | 16, 32
Class A | -2.4% | -6.0% | -0.2% | -7.4%
Class B | -3.9% | -9.7% | -0.3% | -24.5%
Class C | -2.2% | -7.1% | -0.3% | -24.8%
Class D | -1.7% | -5.5% | -0.3% | -21.9%
Class E | -4.0% | -13.2% | -0.6% | -18.9%
Class F |  |  |  | 
Overall |  |  |  | 
 | -3.1% | -8.1% | -0.3% | -14.6%
Random Access HE |  |  | 
Total | Sig | 4,8 | 16, 32
-2.9% | -6.0% | -0.4% | -6.4%
-4.2% | -9.9% | 0.6% | -29.8%
-4.0% | -13.2% | -0.5% | -36.3%
-3.2% | -10.7% | 0.1% | -41.8%
-3.4% | -7.8% | 0.3% | -11.7%
Low delay B HE |  |  | 
Total | Sig | 4,8 | 16, 32
-4.2% | -9.3% | 0.7% | -28.9%
-4.8% | -14.2% | -0.4% | -36.8%
-2.5% | -7.7% | 0.2% | -36.3%
-4.7% | -14.0% | -2.7% | -20.1%
-4.2% | -10.1% | 0.4% | -29.6%
 | All Intra HE |  | 
 | Y | U | V
Class A | -0.1% | -0.5% | -0.3%
Class B | -0.1% | -0.6% | -0.6%
Class C | 0.0% | -0.2% | -0.3%
Class D | 0.0% | -0.3% | -0.4%
Class E | 0.0% | -0.5% | -0.4%
Class F | 0.0% | 0.0% | 0.0%
Overall | 0.0% | -0.4% | -0.4%
 | 0.0% | -0.4% | -0.4%
Enc Time[%] | 101% |  | 
Dec Time[%] | 99.79% |  | 
Random Access HE |  | 
Y | U | V
-0.1% | -0.1% | -0.4%
-0.1% | -0.3% | -0.3%
0.0% | -0.2% | -0.2%
0.0% | -0.2% | 0.0%
-0.1% | -0.2% | -0.3%
-0.1% | -0.2% | -0.3%
99% |  | 
99.73% |  | 
Low delay B HE |  | 
Y | U | V
0.0% | -0.5% | -0.5%
0.2% | -0.2% | -0.4%
0.1% | 0.3% | 0.1%
0.1% | -0.6% | -0.1%
0.1% | -0.2% | -0.3%
0.1% | -0.2% | -0.3%
101% |  | 
99.83% |  | 

## Slide 6: Integrated with Sub-block Scan in JCTVC-G323
Noticeable improvement in BD-rate
Crosschecked in JCTVC-G1001
 | All Intra HE |  |  | 
 | Total | Sig | 4,8 | 16, 32
Class A | -2.2% | -4.1% | -6.3% | -3.6%
Class B | -4.0% | -8.7% | -2.9% | -17.7%
Class C | -2.3% | -6.4% | -1.7% | -18.5%
Class D | -1.9% | -5.3% | -1.3% | -18.0%
Class E | -4.6% | -13.2% | -4.0% | -17.4%
Class F |  |  |  | 
Overall |  |  |  | 
 | -3.2% | -6.9% | -3.3% | -10.0%
Random Access HE |  |  | 
Total | Sig | 4,8 | 16, 32
-3.5% | -7.0% | -3.3% | -7.4%
-4.0% | -9.1% | -1.3% | -23.7%
-4.1% | -12.6% | -2.8% | -30.6%
-3.3% | -10.3% | -1.6% | -35.4%
-3.7% | -8.1% | -1.8% | -11.1%
Low delay B HE |  |  | 
Total | Sig | 4,8 | 16, 32
-4.0% | -8.6% | -1.4% | -22.6%
-4.9% | -13.9% | -3.2% | -31.3%
-2.5% | -7.1% | -1.1% | -28.8%
-4.5% | -11.6% | -9.2% | -12.8%
-4.1% | -9.3% | -1.8% | -23.3%
 | All Intra HE |  |  | Random Access HE |  |  | Low delay B HE |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.4% | -0.9% | -0.7% | -0.2% | -0.2% | 0.2% |  |  | 
Class B | -0.3% | -0.7% | -0.8% | -0.2% | -0.4% | -0.5% | -0.1% | -0.1% | -0.6%
Class C | -0.2% | -0.3% | -0.3% | -0.2% | -0.1% | -0.1% | -0.2% | -0.1% | -0.1%
Class D | -0.2% | -0.3% | -0.3% | -0.1% | 0.3% | -0.4% | -0.1% | 0.2% | 0.3%
Class E | -0.4% | -0.8% | -0.6% |  |  |  | -0.1% | -0.7% | 0.4%
Class F |  |  |  |  |  |  |  |  | 
Overall | -0.3% | -0.6% | -0.5% | -0.2% | -0.1% | -0.2% | -0.1% | -0.1% | 0.0%
 | -0.3% | -0.6% | -0.5% | -0.2% | -0.2% | -0.2% | -0.1% | -0.1% | -0.1%
Enc Time[%] | 102% |  |  | 100% |  |  | 101% |  | 
Dec Time[%] | 99.53% |  |  | 99.70% |  |  | 100.06% |  |