## Slide 1: JCTVC-G658: Quantization matrices in fragmented APS
Ying Chen, Ye-Kui Wang, Rajan Joshi, and Marta Karczewicz

## Slide 2: Introduction
Quantization matrices
  24 matrices might be needed for each full set of quantization matrix table
    intra/inter
    Y/U/V
    4×4, 8×8, 16×16 and 32×32 blocks
  The size can be large and larger than the MTU size
    System level framing may be needed, thus less error resilient, e.g., during in-band transmission
  Predictions are enabled for the coding of the coefficients of a quantization matrix
    Prediction inside a matrix
    Prediction between two matrices, even potentially for different block sizes

## Slide 3: Proposal
Do not put the quantization matrices table in SPS or PPS
Signal the quantization matrices in APS
Enable fragmenting one APS containing quantization matrices into multiple NAL units
  An APS may contain one or more quantization matrices, but not necessary the full set (24 ones)
  A quantization matrix can only refer to a previously signaled quantization matrix in the same APS NAL unit
  Any APS NAL unit can be independently decoded/parsed

## Slide 4: Proposal
Summary of the syntax elements
  Flag indicating the first NAL unit of an APS
    Only the first one contains the other parameters, such as SAO or ALF
  Flag indicating the last NAL unit of an APS
  ID of the starting quantization matrix in the APS NAL unit
  Number of the signaled quantization matrices in the NAL unit
  A flag indicating the prediction mode for each quantization matrix

## Slide 5: Proposal