## Slide 1
A Lossless Coding Solution for HEVC
Nov. 21,2011
Wen Gao, Minqiang, Ye He, Jin Song, Haoping Yu
Notes: <number>
<number>

## Slide 2
Motivation
MPEG-N11872 “Vision, Application and Requirements for HEVC” states
  Possible applications include “remote video presentation and remote computer graphics display”.
  Subjective visually lossless compression shall be supported. Lossless compression should be supported
Interactive video communications are becoming a major feature in many application scenarios
  E-Conference or web-conference: Screen/Desktop Sharing
  Virtual desktop infrastructure (VDI), and Online Gaming
Page <number>
Notes: <number>

## Slide 3
Current HEVC Architecture
Page <number>
Notes: <number>

## Slide 4
Lossless Coding
Page <number>
Transform and Quantization Modules are bypassed to achieve lossless coding
Notes: <number>

## Slide 5
Lossless coding tools
Intra Prediction
  DPCM: Extension of the unified directional Intra (UDI) prediction in current HEVC draft
  Use Local adaptive predictor to replace DC mode
CABAC modifications
  Binarization of Luma prediction residuals
  Context model of signs of Luma and Chroma prediction residuals
Prediction Residual Scanning
  Mode Dependent Residual Scanning (MDRS) for intra coding
  Multiple start scanning positions for inter coding, or equivalently multiple scanning patterns
Mechanism to indicate lossless coding mode
  QPY = 0
Page <number>
Notes: <number>

## Slide 6
DPCM Intra Prediction
No syntax modification to WD. The decoding process for intra prediction is modified
Page <number>
Notes: <number>

## Slide 7
Modified DC mode
Use local adaptive predictor to replace DC mode
  Used in JPEG-LS, so call “Median Edge Predictor
Page <number>
C | B | D
A | X | 
Notes: <number>

## Slide 8
Binarization of Intra Luma Residuals in HM4.0
Binarization consists of three parts
  Truncated Unary code for absolute values in {1,2,3}
  Truncated Golomb Rice code (TR) for (absolute value - 3) up to a limit, cTRMax for a given cRiceParam
  EG0 for (absolute value – 3 – cTRMax-1 )
Page <number>
cRiceParam | cTRMax | Prefix Length
0 | 7 | 8
1 | 20 | 10
2 | 42 | 11
3 | 70 | 8
Notes: <number>

## Slide 9
Modification of Binarization of Intra Luma Residuals (1)
Extend cRiceParam from (0-3) to (0-5)
Page <number>
cRiceParam | cTRMax | Prefix Length
0 | 7 | 8
1 | 20 | 10
2 | 42 | 10
3 | 70 | 8
4 | 142 | 8
5 | 252 | 7
Notes: <number>

## Slide 10
Modification of Binarization of Intra Luma Residuals (2)
cRiceParam adaptation method 1
Page <number>
 |  | min(valuet , 15) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
kt | 0 | 0 | 0 | 1 | 1 | 2 | 2 | 2 | 3 | 3 | 3 | 4 | 4 | 4 | 5 | 5 | 5
 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 3 | 3 | 3 | 4 | 4 | 4 | 5 | 5 | 5 | 5
 | 2 | 2 | 2 | 2 | 2 | 3 | 3 | 3 | 3 | 4 | 4 | 4 | 4 | 5 | 5 | 5 | 5
 | 3 | 3 | 3 | 3 | 3 | 3 | 4 | 4 | 4 | 4 | 4 | 4 | 5 | 5 | 5 | 5 | 5
 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 5 | 5 | 5 | 5 | 5 | 5
 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5
Notes: <number>

## Slide 11
Modification of Binarization of Intra Luma Residuals (3)
cRiceParam adaptation method 2:
  JPEG-LS adaptation method is used.
  Counter, N, is updated as the number of previous TR coded residuals including the current one in a block 16 residuals
  Accumulator, A, is updated as the summation of the previous TR coded including the current one in a block 16 residuals
  cRiceParam, is computed
  for(i = 0; (N << i) < A; i++);
  cRiceParam = min(i, 5);
Page <number>
Change EG0 to EG5 to encode (absolute value – 3 – cTRMax-1 )
Notes: <number>

## Slide 12
Context Model of Signs of Luma and Chroma Prediction Residuals
In HM4.0, signs of Luma and Chroma prediction residual are coded using bypass mode
A context model is created for sign of Luma, Chroma-U and Chroma-V prediction residuals, respectively.
  A single context for each context model.
  The conditional probability is only changed adaptively based on the encoded signs
Page <number>
Notes: <number>

## Slide 13
Mode Dependent Coefficient Scanning (MDCS) in HM4.0
Three Scanning methods in intra coding
  Horizontal Scan (1)
  Vertical Scan (2),
  Zig-Zag Scan (0)
Page <number>
Mode TU | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34
32x32 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
16x16 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
8x8 | 1 | 2 | 0 | 0 | 1 | 1 | 0 | 2 | 2 | 0 | 0 | 1 | 1 | 0 | 0 | 2 | 2 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 2 | 2 | 2 | 2 | 0 | 0
4x4 | 1 | 2 | 0 | 0 | 1 | 1 | 0 | 2 | 2 | 0 | 0 | 1 | 1 | 0 | 0 | 2 | 2 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 2 | 2 | 2 | 2 | 0 | 0
Notes: <number>

## Slide 14
Mode Dependent Residual Scanning for Intra Coding
Page <number>
In lossless coding, Mode dependent Residual scanning (MDRS) is proposed.
Mode TU | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34
32x32 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
16x16 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
8x8 | 2 | 1 | 0 | 0 | 2 | 2 | 0 | 1 | 1 | 0 | 0 | 2 | 2 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 2 | 2 | 2 | 2 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0
4x4 | 2 | 1 | 0 | 0 | 2 | 2 | 0 | 1 | 1 | 0 | 0 | 2 | 2 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 2 | 2 | 2 | 2 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0
Notes: <number>

## Slide 15
Multiple Start Scanning Positions in Inter Scanning (MSCAN)
In lossless coding, use RDO to choose different start position of residual scanning and send the index in the bit stream
  Index = 0: scan starting from the top left corner (as in current HEVC WD)
  Index =1: scan starting from the top right corner
  Index =2: scan starting from the lower left corner,
  Index =3: scan starting from the lower right corner
Page <number>
Notes: <number>

## Slide 16
Multiple Start Scanning Positions in Inter Scanning (MSCAN)
Equivalently, we define 4 types Zigzag scanning patterns
Page <number>
Notes: <number>

## Slide 17
  Mechanism to indicate lossless coding mode
Indicate lossless coding of a CU by setting its QPY = 0
  For those CUs using lossless coding mode, the internal bit depth is set to the input bit depth and the de-blocking filter, SAO and ALF are turned off
Example 1: lossless coding for a whole picture
  Set cu_qp_delta_enabled_flag=0 in SPS
  Set pic_init_qp_minus26=-26 in PPS
  Set slice_qp_delta=0 in all non-lightweight slice headers associated with the video picture
Example 2: Lossless coding for a CU
  Set cu_qp_delta_enabled_flag=1
  Set pic_init_qp_minus26 as usual for lossy coding
  Set slice_qp_delta as usual for lossy coding
  Set cu_qp_delta in a CU to a value such that the derived QPY equal to 0 thus indicating lossless coding for the CU.
Page <number>
Notes: <number>

## Slide 18
Test Results (1)
All coding tools are integrated in HM4.0 the SDIP software used in CE6.
Common test conditions are modified for lossless coding
  Set internal bit depth as input bit depth
  Disable De-block filter, SAO and ALF
  Set RDOQ=0
Anchors: HM4.0 and HM4.0 SDIP with QP=0 and RDOQ=0;
Compression ratio = raw data / compressed
An early skip method is used to speed up encoding process.
Thanks to Microsoft for cross-checking (G885)
Page <number>
Notes: <number>

## Slide 19
Test Results 2
Page <number>
Lossless coding outperforms HM4.0 and HM4.0 SDIP with QP=0
Lossless coding outperforms 7-Zip significantly in LB cases.
 | AI_HE |  |  | AI_HE_SDIP |  |  | 
 | compression ratio |  | bit-rate saving | compression ratio |  | bit-rate saving | 
 | anchor | proposed |  | anchor | proposed |  | 
Class A | 2.14 | 2.43 | -12.02% | 2.15 | 2.57 | -11.89% | 
Class B | 1.93 | 2.17 | -11.06% | 1.95 | 2.20 | -11.07% | 
Class C | 1.79 | 2.07 | -13.63% | 1.80 | 2.08 | -13.44% | 
Class D | 1.71 | 1.97 | -13.65% | 1.72 | 1.98 | -13.35% | 
Class E | 2.71 | 3.21 | -15.41% | 2.73 | 3.22 | -15.29% | 
Class F | 3.88 | 5.42 | -28.43% | 4.02 | 5.49 | -26.90% | 
Overall | 2.51 | 2.86 | -9.71% | 2.54 | 2.88 | -9.35% | 
Enc Time[%] | 84% |  |  | 84% |  |  | 
Dec Time[%] | 95% |  |  | 81% |  |  | 
 | LB_HE |  |  | LB_HE_SDIP |  |  | 7 Zip
 | compression ratio |  | bit-rate saving | compression ratio |  | bit-rate saving | Compression Ratio
 | anchor | proposed |  | anchor | proposed |  | 
Class A |  |  |  |  |  |  | 
Class B | 2.18 | 2.39 | -8.68% | 2.21 | 2.41 | -8.73% | 1.81
Class C | 2.32 | 2.58 | -10.19% | 2.32 | 2.58 | -10.19% | 1.69
Class D | 2.48 | 2.70 | -8.75% | 2.48 | 2.70 | -8.76% | 1.70
Class E | 3.78 | 4.17 | -9.40% | 3.78 | 4.17 | -9.40% | 2.49
Class F | 51.11 | 55.21 | -6.58% | 52.20 | 55.58 | -5.99% | 42.06
Overall | 12.29 | 13.32 | -7.24% | 12.52 | 13.40 | -7.15% | 8.62
Enc Time[%] | 126% |  |  | 123% |  |  | 
Dec Time[%] | 77% |  |  | 70% |  |  | 
Notes: <number>

## Slide 20
Page <number>
Conclusions
Create CE for further testing

## Slide 21
Page <number>
Thank You
www.huawei.com
Notes: <number>
<number>