## Slide 1: JCTVC-G666 1D DCT based frequency domain adaptive loop filter (FD-ALF)
Hae-Kwang Kim
Jeongyoen Lim, Ju Ock Lee, Joo-Hee Moon, Sungwon Lim
Notes: <number>
<number>

## Slide 2: Summary of 1D FD-ALF
Exactly same as existing ALF for adaptation of
  RA, BA adaptation
  CU unit control adaptation
  category filter merging
  predictive filter coefficient encoding, etc.
Except
  different filter type: 1D DCT block filtering (ALF: pixel based filtering)
  purpose: reducing complexity

## Slide 3: Summary of 1D FD-ALF (RA)
1xM
Mx1
M = 8 or 16
DCT
DCT

## Slide 4: Summary of 1D FD-ALF (BA)
MxM
MxM
Block size for variance is MxM (instead of 4x4 in ALF)
Filter coefficients are calculated as the same way for RA for
the same block variance category
1xM filter
Mx1 filter

## Slide 5: Summary of 1D FD-ALF
Experimental results for 1x16 and 16x1
 | All Intra HE |  |  | Random Access HE |  |  | Low delay P HE |  |  | Low delay B HE |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Class A | 2.2% | 1.2% | 0.8% | 3.3% | 4.6% | 4.2% |  |  |  |  |  | 
Class B | 1.3% | 1.8% | 1.3% | 2.6% | 3.1% | 2.0% | 4.0% | 3.2% | 2.8% | 2.0% | 2.5% | 1.8%
Class C | 1.1% | 2.6% | 2.7% | 1.6% | 1.3% | 1.6% | 2.1% | 1.3% | 1.5% | 1.4% | 1.6% | 1.8%
Class D | 0.5% | 2.4% | 2.7% | 1.6% | 1.2% | 1.5% | 1.0% | 1.0% | 1.3% | 0.8% | 2.2% | 2.1%
Class E | 1.9% | 2.8% | 4.3% |  |  |  | 4.8% | 3.9% | 4.4% | 3.0% | 2.3% | 2.8%
Class F | 0.6% | 1.7% | 1.4% | 1.0% | 1.4% | 1.1% | 1.5% | 1.4% | 0.8% | 1.1% | 1.5% | 1.1%
Overall | 1.2% | 2.0% | 2.1% | 2.1% | 2.3% | 2.1% | 2.6% | 2.1% | 2.1% | 1.6% | 2.0% | 1.9%
Enc Time[%] | 83% |  |  | 96% |  |  | 96% |  |  | 98% |  | 
Dec Time[%] | 99% |  |  | 91% |  |  | 93% |  |  | 94% |  | 

## Slide 6: Analysis complexity of filtering per one pixel
ALF in HM 4.0
FD-ALF
 | star 5x5 | cross 11x5
 | 8 | 9
 | 15 | 17
 | 4 | 8 | 16
 | 1.5 | 2.75 | 5.375
 | 3.5 | 5.25 | 8.125
Notes: <number>

## Slide 7: Simulation Results
ALF in HM 4.0 vs. FD-ALF for HE-AI
 | All Intra HE (M=16) |  |  | Random Access HE (M=16) |  | 
 | Y | U | V | Y | U | V
Class A | 2.2% | 1.2% | 0.8% | 3.3% | 4.6% | 4.2%
Class B | 1.3% | 1.8% | 1.3% | 2.6% | 3.1% | 2.0%
Class C | 1.1% | 2.6% | 2.7% | 1.6% | 1.3% | 1.6%
Class D | 0.5% | 2.4% | 2.7% | 1.6% | 1.2% | 1.5%
Class E | 1.9% | 2.8% | 4.3% |  |  | 
Class F | 0.6% | 1.7% | 1.4% | 1.0% | 1.4% | 1.1%
Overall | 1.2% | 2.0% | 2.1% | 2.1% | 2.3% | 2.1%
Enc Time[%] | 83% |  |  | 96% |  | 
Dec Time[%] | 99% |  |  | 91% |  | 
Notes: <number>

## Slide 8: Simulation Results
ALF in HM 4.0 vs. FD-ALF for HE-RA
 | Random Access HE (M=8) |  |  | Random Access HE (M=16) |  | 
 | Y | U | V | Y | U | V
Class A | 3.7% | 5.4% | 5.0% | 3.3% | 4.6% | 4.2%
Class B | 2.7% | 3.1% | 1.9% | 2.6% | 3.1% | 2.0%
Class C | 1.7% | 1.7% | 1.8% | 1.6% | 1.3% | 1.6%
Class D | 1.7% | 1.4% | 1.6% | 1.6% | 1.2% | 1.5%
Class F | 0.9% | 1.6% | 1.4% | 1.0% | 1.4% | 1.1%
Overall | 2.2% | 2.6% | 2.3% | 2.1% | 2.3% | 2.1%
Enc Time[%] | 97% |  |  | 96% |  | 
Dec Time[%] | 91% |  |  | 91% |  | 
Notes: <number>

## Slide 9: Simulation Results
ALF in HM 4.0 vs. FD-ALF for HE-LDB
 | Low delay P HE (M=16) |  |  | Low delay B HE (M=16) |  | 
 | Y | U | V | Y | U | V
Class B | 4.0% | 3.2% | 2.8% | 2.0% | 2.5% | 1.8%
Class C | 2.1% | 1.3% | 1.5% | 1.4% | 1.6% | 1.8%
Class D | 1.0% | 1.0% | 1.3% | 0.8% | 2.2% | 2.1%
Class E | 4.8% | 3.9% | 4.4% | 3.0% | 2.3% | 2.8%
Class F | 1.5% | 1.4% | 0.8% | 1.1% | 1.5% | 1.1%
Overall | 2.6% | 2.1% | 2.1% | 1.6% | 2.0% | 1.9%
Enc Time[%] | 96% |  |  | 98% |  | 
Dec Time[%] | 93% |  |  | 94% |  | 
Notes: <number>

## Slide 10: Simulation Results
ALF in HM 4.0 vs. FD-ALF for LDP
 | Low delay P HE (M=8) |  |  | Low delay P HE (M=16) |  | 
 | Y | U | V | Y | U | V
Class B | 4.5% | 3.4% | 3.1% | 4.0% | 3.2% | 2.8%
Class C | 2.2% | 1.7% | 2.0% | 2.1% | 1.3% | 1.5%
Class D | 1.0% | 1.5% | 1.2% | 1.0% | 1.0% | 1.3%
Class E | 5.1% | 3.7% | 4.0% | 4.8% | 3.9% | 4.4%
Class F | 1.4% | 1.5% | 1.0% | 1.5% | 1.4% | 0.8%
Overall | 2.8% | 2.4% | 2.2% | 2.6% | 2.1% | 2.1%
Enc Time[%] | 96% |  |  | 96% |  | 
Dec Time[%] | 92% |  |  | 93% |  | 
Notes: <number>

## Slide 11: Simulation Results
ALF in HM 4.0 vs. FD-ALF for HE-AI and HE-RA
 | All Intra HE (M=8 or M=16) |  |  | Random Access HE (M=8 or M=16) |  | 
 | Y | U | V | Y | U | V
Class A | 2.0% | 1.2% | 0.7% | 3.3% | 4.6% | 4.3%
Class B | 1.3% | 1.7% | 1.3% | 2.6% | 3.0% | 2.0%
Class C | 1.1% | 2.4% | 2.5% | 1.6% | 1.3% | 1.7%
Class D | 0.5% | 2.3% | 2.6% | 1.7% | 1.2% | 1.4%
Class E | 1.8% | 2.7% | 4.2% |  |  | 
Class F | 0.6% | 1.7% | 1.4% | 0.8% | 1.4% | 1.2%
Overall | 1.2% | 1.9% | 2.0% | 2.0% | 2.3% | 2.1%
Enc Time[%] | 84% |  |  | 97% |  | 
Dec Time[%] | 97% |  |  | 92% |  | 
Notes: <number>

## Slide 12: Simulation Results
ALF in HM 4.0 vs. FD-ALF for HE-LDB and HE-LDP
 | Low delay B HE (M=8 or M=16) |  |  | Low delay P HE (M=8 or M=16) |  | 
 | Y | U | V | Y | U | V
Class B | 2.0% | 2.5% | 1.8% | 4.0% | 3.3% | 2.8%
Class C | 1.5% | 1.9% | 2.1% | 2.1% | 1.5% | 1.6%
Class D | 0.8% | 1.6% | 2.0% | 1.0% | 1.1% | 1.7%
Class E | 3.0% | 1.9% | 3.3% | 4.7% | 3.8% | 4.9%
Class F | 1.1% | 1.5% | 1.3% | 1.3% | 1.6% | 1.3%
Overall | 1.6% | 1.9% | 2.0% | 2.6% | 2.2% | 2.3%
Enc Time[%] | 98% |  |  | 96% |  | 
Dec Time[%] | 96% |  |  | 93% |  | 
Notes: <number>

## Slide 13: Conclusions
The proposed method reduces decoding time complexity in average 5% while loss of coding efficiency by in average around 1.8%
It is recommend that this 1D FD-ALF be considered to be adopted in HEVC through CE for further improvement.
Notes: <number>