## Slide 1: JCTVC-G674 - CE5: Sub-block coding of transform coefficients with CAVLC

## Slide 2: Proposal
The 16x16 and 32x32 transform coefficients blocks are divided into 4x4 sub-blocks.
After the position of the last nonzero coefficient is sent, for each 4x4 sub-block two conditions are checked:
  The number of coded coefficients in this sub-block is larger than 4.
  The average number of non-zero coefficients in this sub-block in the previously coded blocks is smaller than 3.
If they are both true, coded-not-coded information (1 bit) is sent for this sub-block.

## Slide 3: Results – Sub-blocks
 | All Intra LC |  |  | Random Access LC |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.6% | 0.5% | 0.5% | -0.3% | -0.1% | 0.4% |  |  | 
Class B | -0.3% | 0.1% | 0.1% | -0.2% | 0.1% | 0.2% | 0.0% | 0.0% | 0.1%
Class C | -0.4% | 0.1% | 0.0% | -0.2% | -0.1% | 0.2% | -0.1% | 0.0% | -0.3%
Class D | -0.6% | -0.2% | -0.1% | -0.2% | -0.2% | 0.0% | 0.0% | 0.2% | 0.1%
Class E | -0.3% | 0.1% | 0.2% |  |  |  | -0.3% | -0.6% | -0.7%
Overall | -0.6% | 0.1% | 0.2% | -0.2% | -0.1% | 0.2% | -0.1% | -0.1% | -0.1%
Enc Time[%] | 100% |  |  | 101% |  |  | 100% |  | 
Dec Time[%] | 101% |  |  | 100% |  |  | 100% |  | 

## Slide 4: Results – Strong Scan and Sub-blocks
 | All Intra LC |  |  | Random Access LC |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -1.0% | -0.4% | -0.4% | -0.5% | -0.4% | 0.0% |  |  | 
Class B | -1.1% | -0.8% | -0.9% | -0.4% | -0.5% | -0.3% | -0.1% | -0.1% | 0.0%
Class C | -0.5% | -0.3% | -0.3% | -0.3% | -0.2% | -0.1% | -0.1% | 0.0% | -0.2%
Class D | -0.5% | -0.3% | -0.3% | -0.2% | -0.3% | 0.1% | -0.1% | 0.1% | -0.2%
Class E | -1.2% | -1.7% | -1.2% |  |  |  | -0.5% | 0.0% | -1.7%
Overall | -0.9% | -0.7% | -0.6% | -0.4% | -0.4% | -0.1% | -0.2% | 0.0% | -0.4%
Enc Time[%] | 101% |  |  | 103% |  |  | 101% |  | 
Dec Time[%] | 101% |  |  | 101% |  |  | 99% |  |