## Slide 1: JCTVC-G677 - CE5: Limitation on VLC codeword length

## Slide 2: Codewords Length
Codewords longer than 32 bits can be created when coding syntax element last_pos_level_one .
Set the value of the array lastPosVlcNumTable for blockType=0 and vlcNumIdx=7 to 2 insted of 7:
Modify VLC table for vlcNum=9, by concatenating Golomb codes with two different parameters k:
  Golomb code with k=4 used till value 266, is concatenated with Golomb code k=7.
 | vlcNumIdx |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
blockType | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
0 | 10 | 10 | 10 | 10 | 2 | 2 | 2 | 2 | 9 | 9 | 9 | 9 | 9 | 4 | 4 | 4 | 4
1 | 10 | 10 | 10 | 10 | 10 | 2 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 4 | 4 | 4 | 4
 | vlcNumIdx |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
blockType | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
0 | 10 | 10 | 10 | 10 | 2 | 2 | 2 | 7 | 9 | 9 | 9 | 9 | 9 | 4 | 4 | 4 | 4
1 | 10 | 10 | 10 | 10 | 10 | 2 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 4 | 4 | 4 | 4

## Slide 3
 | All Intra LC |  |  | Random Access LC |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | -0.1% |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | -0.1% | -0.2%
Class C | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class E | 0.0% | 0.0% | 0.0% |  |  |  | 0.0% | 0.0% | -0.1%
Class F | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | -0.1%
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1%
Enc Time[%] | 99% |  |  | 98% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 98% |  |  | 101% |  | 
Results