## Slide 1: JCTVC-G683: Simplification and Improvement of Additional Merge Candidate
Y. Zheng, X. Wang, W.-J. Chien, V. Seregin, M.Karczewicz

## Slide 2: Current Scheme in HM4.0
Combined bi-pred merge candidates
  Created by combining every two original candidates partially
Scaled bi-pred
  Invert the sign of a motion vector and check if it’s valid
Zero candidates
  mv=(0,0), refIdx=0
  mv=(0,0), refIdx=1
MV Pruning

## Slide 3: Proposed Changes
Limit the pruning operation to combined bi-pred candidates
Remove scaled bi-pred candidate
Adding motion offset candidates
  Possible offsets on motion vector: (4,0), (-4,0), (0,4), (0,-4)
  For a bi-pred mv, if two ref frames are from the same side of the current frame, offset value is added to the mv pointing to the frame farther away from the current frame
  If no original candidate available, add mv=(0,0) with refIdx=0, together with four of its mv offset version
  If mv(0,0), refIdx=0 is one of the original candidates, then add a candidate of mv(0,0), refIdx=1 before adding mv offset candidates

## Slide 4: Proposed Scheme vs. HM4.0
Additional merge candidates | HM4.0 | Proposed
Cand class 1 | Combined Bi-pred(with pruning) | Combined Bi-pred (with pruning)
Cand class 2 | Scaled Bi-pred(with pruning) | Contidional Zero candidates (with comparison on mv(0,0) with refidx=1 only)
Cand class 3 | Zero (with pruning) | Motion offset (without pruning)

## Slide 5: Simulation Results
 | Limit Pruning + Remove Scaled Bi-Pred |  |  |  | 
 | Y | U | V | Encoding | Decoding
RA_HE | 0.07% | 0.13% | 0.19% | 97% | 98%
LB_HE | 0.03% | 0.13% | -0.02% | 97% | 98%
LP_HE | 0.08% | 0.00% | 0.23% | 98% | 97%
RA_LC | 0.11% | 0.15% | 0.11% | 98% | 100%
LB_LC | 0.00% | 0.12% | 0.08% | 95% | 100%
LP_LC | 0.04% | 0.03% | 0.22% | 99% | 99%
Average | 0.06% | 0.09% | 0.14% |  | 

## Slide 6: Simulation Results (Cont.)
 | Limit Pruning + Remove Scaled Bi-Pred + Motion Offset Candidates |  |  |  | 
 | Y | U | V | Encoding | Decoding
RA_HE | -0.06% | -0.01% | 0.02% | 99% | 100%
LB_HE | -0.22% | -0.23% | -0.28% | 100% | 100%
LP_HE | -0.29% | 0.035 | -0.14% | 99% | 100%
RA_LC | -0.11% | -0.06% | -0.15% | 97% | 99%
LB_LC | -0.32% | -0.16% | -0.15% | 101% | 98%
LP_LC | -0.53% | -0.47% | -0.46% | 100% | 101%
Average | -0.26% | -0.15% | -0.19% |  | 

## Slide 7: Conclusions
No obvious coding performance drop with pruning operation reduced and scaled bi-pred removed
Motion offset candidates can be easily generated and are helpful to coding performance
Recommend to adopt the proposed changes into HM