## Slide 1: JCTVC-G700 On coeff_abs_level_minus3 coding
Jian Lou, Limin Wang, and Shuy Fang
Motorola Mobility

## Slide 2: Summary
Proposal consisting of two parts
  Truncated Rice (TR) code parameter updating and TR code generation
Part 1
  Remove resetting cRiceParam (TR parameter) value for each subset and a new updating table
Part 2
  Fix the problem of the TR code generation and WD description
Notes: <number>

## Slide 3: coeff_abs_level_minu3
Absolute value of a quantized transform coefficient level minus 3
Binarized with TR code with parameter cRiceParam and cTRMax (or with EG0 code)
  cRiceParam controls the flatness of the codeword distribution (small value is preferred for small symbols)
  cTRMax controls the truncation point for the rice code

## Slide 4: cRiceParam
Initialized as 0 for each subset (resetting)
Updated after each coeff_ab_level_minu3
HM2.0
HM4.0

## Slide 5: Remove cRiceParam resetting
Not needed assuming coeff_ab_level_minu3 getting larger statistically along the HM40 inverse scan
Save operations and hardware complexity, improve worst case performance (cRiceParam stay 3)
AIHE (Y/U/V): 0.0%/0.0%/0.0%
RAHE (Y/U/V): 0.0%/0.0%/0.0%
LBHE (Y/U/V): 0.0%/0.0%/0.1%

## Slide 6: Detailed performance of removing cRiceParam resetting
07/28/26
© 2011 Motorola Mobility, Inc.
 | All Intra HE |  | 
 | Y | U | V
Class A | 0.2% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0%
Class C | 0.0% | 0.1% | 0.1%
Class D | 0.0% | 0.0% | 0.0%
Class E | 0.0% | 0.0% | 0.0%
Overall | 0.0% | 0.0% | 0.0%
 | 0.0% | 0.0% | 0.0%
 | Random Access HE |  | 
 | Y | U | V
Class A | 0.2% | -0.2% | 0.0%
Class B | 0.0% | 0.0% | -0.1%
Class C | 0.0% | 0.0% | 0.1%
Class D | 0.0% | 0.2% | -0.1%
Class E |  |  | 
Overall | 0.0% | 0.0% | 0.0%
 | 0.1% | 0.0% | 0.0%
 | Low delay B HE |  | 
 | Y | U | V
Class A |  |  | 
Class B | 0.0% | 0.0% | -0.1%
Class C | 0.0% | 0.0% | -0.1%
Class D | 0.0% | 0.0% | 0.0%
Class E | 0.1% | 0.1% | 0.9%
Overall | 0.0% | 0.0% | 0.1%
 | 0.0% | -0.1% | 0.0%

## Slide 7: Current cRiceParam updating table
Trained from HM2.0 stats
Not changed since HM2.0
Irregular if jumping to cRiceParam = 3
07/28/26
© 2011 Motorola Mobility, Inc.
cRiceParam | 0 |  | 1 |  | 2 |  | 3 | 
Symbol | Codeword | Bits | Codeword | Bits | Codeword | Bits | Codeword | Bits
0 | 0 | 1 | 00 | 2 | 000 | 3 | 0000 | 4
1 | 10 | 2 | 01 | 2 | 001 | 3 | 0001 | 4
2 | 110 | 3 | 100 | 3 | 010 | 3 | 0010 | 4
3 | 1110 | 4 | 101 | 3 | 011 | 3 | 0011 | 4
4 | 11110 | 5 | 1100 | 4 | 1000 | 4 | 0100 | 4
5 | 111110 | 6 | 1101 | 4 | 1001 | 4 | 0101 | 4
6 | 1111110 | 7 | 11100 | 5 | 1010 | 4 | 0110 | 4
7 | 11111110 | 8 | 11101 | 5 | 1011 | 4 | 0111 | 4
8 | 11111111,EG0 | 9 | 111100 | 6 | 11000 | 5 | 10000 | 5
9 |  |  | 111101 | 6 | 11001 | 5 | 10001 | 5
10 |  |  | 1111100 | 7 | 11010 | 5 | 10010 | 5
11 |  |  | 1111101 | 7 | 11011 | 5 | 10011 | 5
12 |  |  | 11111100 | 8 | 111000 | 6 | 10100 | 5
13 |  |  | 11111101 | 8 | 111001 | 6 | 10101 | 5
HM4.0 table updating point

## Slide 8: New updating table without cRiceParam resetting
AIHE (Y/U/V):
0.0%/0.0%/0.0%
RAHE (Y/U/V):
0.0%/0.1%/0.0%
LBHE (Y/U/V):
0.0%/-0.2%/-0.2%
cRiceParam | 0 |  | 1 |  | 2 |  | 3 | 
Symbol | Codword | Bits | Codword | Bits | Codword | Bits | Codeword | Bits
0 | 0 | 1 | 00 | 2 | 000 | 3 | 0000 | 4
1 | 10 | 2 | 01 | 2 | 001 | 3 | 0001 | 4
2 | 110 | 3 | 100 | 3 | 010 | 3 | 0010 | 4
3 | 1110 | 4 | 101 | 3 | 011 | 3 | 0011 | 4
4 | 11110 | 5 | 1100 | 4 | 1000 | 4 | 0100 | 4
5 | 111110 | 6 | 1101 | 4 | 1001 | 4 | 0101 | 4
6 | 1111110 | 7 | 11100 | 5 | 1010 | 4 | 0110 | 4
7 | 11111110 | 8 | 11101 | 5 | 1011 | 4 | 0111 | 4
8 | 11111111,EG0 | 9 | 111100 | 6 | 11000 | 5 | 10000 | 5
9 |  |  | 111101 | 6 | 11001 | 5 | 10001 | 5
10 |  |  | 1111100 | 7 | 11010 | 5 | 10010 | 5
11 |  |  | 1111101 | 7 | 11011 | 5 | 10011 | 5
12 |  |  | 11111100 | 8 | 111000 | 6 | 10100 | 5
No loss
regular updating rule
No updating table with simplified logics
New table updating point

## Slide 9: Combination logic representation
1) Old Table
cRiceParam = cRiceParam
+ (coeff_abs_level_minus3[n-1] >= 2 && cRiceParam == 0)
+ (coeff_abs_level_minus3[n-1] >= 5 && cRiceParam <= 1)
+ (coeff_abs_level_minus3[n-1] >= 13 && cRiceParam == 0)
+ (coeff_abs_level_minus3[n-1] >= 11 && cRiceParam == 1)
+ (coeff_abs_level_minus3[n-1] >= 10 && cRiceParam == 2));
2) Proposed table
cRiceParam = cRiceParam
+ (coeff_abs_level_minus3[n-1] >= 2 && cRiceParam == 0)
+ (coeff_abs_level_minus3[n-1] >= 5 && cRiceParam <= 1)
+ (coeff_abs_level_minus3[n-1] >= 11 && cRiceParam <= 2);
07/28/26
© 2011 Motorola Mobility, Inc.

## Slide 10: Detailed performance of removing cRiceParam resetting with new updating table
07/28/26
© 2011 Motorola Mobility, Inc.
 | All Intra HE |  | 
 | Y | U | V
Class A | 0.1% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0%
Class C | 0.0% | 0.1% | 0.1%
Class D | 0.0% | 0.0% | 0.0%
Class E | 0.0% | 0.0% | 0.0%
Overall | 0.0% | 0.0% | 0.0%
 | 0.0% | 0.0% | 0.0%
 | Random Access HE |  | 
 | Y | U | V
Class A | 0.1% | 0.1% | -0.4%
Class B | 0.0% | 0.2% | 0.0%
Class C | 0.0% | 0.0% | 0.2%
Class D | 0.0% | 0.1% | 0.1%
Class E |  |  | 
Overall | 0.0% | 0.1% | 0.0%
 | 0.1% | 0.1% | 0.0%
 | Low delay B HE |  | 
 | Y | U | V
Class A |  |  | 
Class B | 0.0% | -0.2% | -0.5%
Class C | 0.0% | 0.0% | -0.2%
Class D | 0.0% | 0.2% | 0.1%
Class E | 0.1% | -0.8% | -0.2%
Overall | 0.0% | -0.2% | -0.2%
 | 0.0% | -0.3% | -0.2%

## Slide 11: Truncated Rice Codes for symbols greater than 39 with cRiceParam equal to 2
In HM 4.0, codeword redundancies caused by
  g_auiGoRicePrefixLen[4] = { 8, 10, 11, 8};
To remove codeword redundancies
  g_auiGoRicePrefixLen[4] = { 8, 10, 10, 8};
Symbol | HM4.0 |  | Fixed | 
 | Codeword | Bits | Codeword | Bits
39 | 111111111011 | 12 | 111111111011 | 12
40 | 1111111111000 | 13 | 111111111100 | 12
41 | 1111111111001 | 13 | 111111111101 | 12
42 | 1111111111010 | 13 | 111111111110 | 12
43 | 1111111111011,EG0 | 14 | 111111111111,EG0 | 13

## Slide 12: Fixing the problem of HM4.0 TR code
Specification of cTRMax depending on cRiceParam changed
Working draft modified with minimum changes
AIHE (Y/U/V): 0.0%/0.0%/0.0%
RAHE (Y/U/V): 0.0%/0.0%/0.0%
LBHE (Y/U/V): 0.0%/-0.1%/0.0%
cRiceParam | cTRMax
0 | (7) 8
1 | 20
2 | 42
3 | 70
Notes: <number>

## Slide 13: Detailed performance of fixing the problem of HM4.0 TR code
26/7/28
 | All Intra HE |  | 
 | Y | U | V
Class A | 0.0% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0%
Class C | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.0% | 0.0%
Class E | 0.0% | 0.0% | 0.0%
Overall | 0.0% | 0.0% | 0.0%
 | 0.0% | 0.0% | 0.0%
 | Random Access HE |  | 
 | Y | U | V
Class A | 0.0% | -0.1% | 0.0%
Class B | 0.0% | 0.0% | 0.0%
Class C | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.0% | 0.0%
Class E |  |  | 
Overall | 0.0% | 0.0% | 0.0%
 | 0.0% | 0.0% | 0.0%
 | Low delay B HE |  | 
 | Y | U | V
Class A |  |  | 
Class B | 0.0% | -0.1% | 0.0%
Class C | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.0% | 0.0%
Class E | 0.0% | -0.1% | 0.1%
Overall | 0.0% | -0.1% | 0.0%
 | 0.0% | -0.1% | 0.0%

## Slide 14: Conclusion
  Recommend adopt the Truncated Rice code fix
  Recommend adopt remove resetting cRiceParam (TR parameter) value and updating rule
  Thank You !
26/7/28