## Slide 1: JCTVC-G705: CABAC simplification for explicit signaling mode of AMVP
Kiran Misra, Andrew Segall
<number>
Notes: <number>

## Slide 2: Propose
We propose:
  Bypass CABAC mode for motion vector predictor index syntax elements:
    mvp_idx_lX i.e. mvp_idx_l0, mvp_idx_l1, mvp_idx_lc
Average BD bitrate for HM-4.0 common conditions:
  RA_HE Y:0.0% U:0.0% V:0.0%
  LB_HE Y:0.0% U:0.1% V:0.1%
  LP_HE Y:0.0% U:0.2% V:-0.1%
<number>
Notes: <number>

## Slide 3: Summary R-D results
<number>
 | Random Access HE |  |  |  |  |  |  | 
 | Y | U | V |  |  |  |  | 
Class A | 0.0% | 0.0% | 0.1% |  |  |  |  | 
Class B | 0.0% | 0.0% | 0.1% |  |  |  |  | 
Class C | 0.1% | 0.0% | -0.1% |  |  |  |  | 
Class D | 0.0% | 0.0% | 0.0% |  |  |  |  | 
Class E |  |  |  |  |  |  |  | 
Overall | 0.0% | 0.0% | 0.0% |  |  |  |  | 
 | 0.0% | 0.0% | 0.0% |  |  |  |  | 
Enc Time[%] | 97% |  |  |  |  |  |  | 
Dec Time[%] | 98% |  |  |  |  |  |  | 
 | Low delay B HE |  |  |  |  | Low delay P HE |  | 
 | Y | U | V |  |  | Y | U | V
Class A |  |  |  |  | Class A |  |  | 
Class B | 0.0% | 0.0% | 0.0% |  | Class B | 0.0% | 0.1% | 0.0%
Class C | 0.0% | 0.5% | -0.1% |  | Class C | 0.0% | 0.2% | -0.5%
Class D | 0.1% | 0.0% | 0.9% |  | Class D | 0.0% | 0.4% | 0.0%
Class E | -0.1% | 0.0% | 0.0% |  | Class E | -0.2% | 0.0% | 0.0%
Overall | 0.0% | 0.1% | 0.1% |  | Overall | 0.0% | 0.2% | -0.1%
 | 0.0% | 0.1% | 0.1% |  |  | 0.0% | 0.2% | -0.1%
Enc Time[%] | 98% |  |  |  | Enc Time[%] | #NUM! |  | 
Dec Time[%] | 99% |  |  |  | Dec Time[%] | #NUM! |  | 

## Slide 4: Proposed Working Draft Modification
<number>
Table 9‑20 – Association of ctxIdx and syntax elements for each slice type in the initialisation process

## Slide 5: Summary
Bypass CABAC mode for intra coding mode syntax elements:
  mvp_idx_lX
We recommend that this change be adopted in WD and HM.
Confidential
<number>