## Slide 1: JCTVC-G707: Using CABAC bypass mode for coding intra prediction mode
Kiran Misra, Andrew Segall
<number>
Notes: <number>

## Slide 2: Propose
We propose:
  Bypass CABAC mode for intra coding mode syntax elements:
    mpm_idx
    rem_intra_luma_pred_mode
No impact on coding efficiency for HM-4.0 common conditions:
  AI_HE Y:0.0% U:0.0% V:0.0%; RA_HE Y:0.0% U:0.0% V:0.0%;
  LB_HE Y:0.0% U:0.0% V:-0.5% LP_HE Y:0.0% U:-0.2% V:-0.3%
Changes identical to those proposed in JCTVC-G767
<number>
Notes: <number>

## Slide 3: Example CABAC bin distribution
BasketballDrill, all intra, QP=22 (21% increase in bypass bins)
BasketballDrill, all intra, QP=37 (81% increase in bypass bins)
<number>

## Slide 4: Summary R-D results
<number>
 | All Intra HE |  |  |  |  | Low delay B HE |  | 
 | Y | U | V |  |  | Y | U | V
Class A | 0.1% | 0.0% | 0.1% |  | Class A |  |  | 
Class B | 0.0% | 0.1% | 0.0% |  | Class B | 0.0% | -0.1% | -0.2%
Class C | 0.0% | 0.0% | -0.1% |  | Class C | 0.0% | 0.3% | -0.2%
Class D | 0.0% | -0.1% | 0.0% |  | Class D | 0.1% | -0.1% | -1.2%
Class E | 0.1% | 0.1% | 0.1% |  | Class E | 0.0% | -0.3% | -0.2%
Overall | 0.0% | 0.0% | 0.0% |  | Overall | 0.0% | 0.0% | -0.5%
 | 0.0% | 0.0% | 0.0% |  |  | 0.0% | -0.1% | -0.5%
Enc Time[%] | 99% |  |  |  | Enc Time[%] | 98% |  | 
Dec Time[%] | 99% |  |  |  | Dec Time[%] | 99% |  | 
 | Random Access HE |  |  |  |  | Low delay P HE |  | 
 | Y | U | V |  |  | Y | U | V
Class A | 0.0% | -0.1% | 0.0% |  | Class A |  |  | 
Class B | 0.0% | -0.1% | -0.1% |  | Class B | 0.0% | -0.1% | -0.1%
Class C | 0.0% | 0.0% | 0.0% |  | Class C | 0.0% | -0.4% | 0.0%
Class D | 0.0% | 0.0% | 0.0% |  | Class D | 0.1% | -0.5% | -1.3%
Class E |  |  |  |  | Class E | 0.1% | 0.0% | -0.1%
Overall | 0.0% | 0.0% | -0.1% |  | Overall | 0.0% | -0.2% | -0.4%
 | 0.0% | -0.1% | -0.1% |  |  | 0.0% | -0.2% | -0.4%
Enc Time[%] | 100% |  |  |  | Enc Time[%] | #NUM! |  | 
Dec Time[%] | 100% |  |  |  | Dec Time[%] | #NUM! |  | 

## Slide 5: Summary
Bypass CABAC mode for intra coding mode syntax elements:
  mpm_idx
  rem_intra_luma_pred_mode
We recommend that this change be adopted in WD and HM.
Confidential
<number>