## Slide 1: JCTVC-G714: On Picture Referencing
Kiran Misra, Sachin Deshpande, Andrew Segall
<number>
Notes: <number>

## Slide 2: Motivation
Background
  JCTVC-F493 Proposed absolute signaling of reference pictures which supports error robust management of reference pictures using Reference Picture Sets (RPS).
  AHG21 was formed at the 6th JCT-VC meeting. AHG21 has produced a candidate working draft specification for signaling reference pictures.
Drawbacks being addressed
  JCTV-F493 and the latest AHG21 WD* currently do not support long term pictures efficiently.
  Although, signaling RPS in PPS is an efficient signaling scheme, if the “desired RPS” differs from that defined in PPS a more expensive “explicit signaling” scheme is used.
<number>
* ftp://ftp.hhi.de/ahg21/JCTVC-F803_d5_RPS_r2.doc
Notes: <number>

## Slide 3: Proposal features
Features
  A method to replace, delete or append entries to a RPS defined in the PPS
  A method to signal long term pictures using absolute POC
  A method to define in PPS a RPS containing long term pictures
<number>

## Slide 4: Modification of RPS in PPS
<number>
Improved bit efficiency
Point to RPS in PPS
Explicit signaling in slice-header
We propose syntax for achieving intermediate bit efficiency points by allowing following operations on RPS defined in PPS:
  Replace:
    An efficient way of signaling delete and append together
  Delete:
    For pictures no longer providing R-D benefits
    For pictures prior to CRA point
  Append:
    For adding long term reference pictures

## Slide 5: Proposed Syntax: RPS Modification
Replace
Delete
Append

## Slide 6: Signal long term pictures using absolute POC
<number>
MSB (POC) + LSB (POC)

## Slide 7: RPS (defined in PPS) containing long term pictures
<number>
To enable long term pictures combining with locally varying deltaPOC referencing.
Example:

## Slide 8: Proposed Change 1, 2: Absolute POC, LTR in RPS
num_longterm_pics specifies the number of long term pictures specified in RPS.
longterm_pics_only_flag equals to 1 identifies that the reference picture set contains long term pictures only. longterm_pics_only_flag equals to 0 identifies that the reference picture set contains both short term and long term pictures.
longterm_poc [ i ] specifies the picture order count of the i-th long term picture being referenced. The longterm_poc [ i ] is the sum of POC MSB and POC LSB for the long term picture being referenced.
used_by_curr_pic_lt_flag[ i ] equal to 1 (0) specifies that the i-th long term picture is used (not used) for reference by the current picture.

## Slide 9: Conclusion
We propose:
  A method to replace, delete or append entries to a reference picture set defined in the picture parameter set.
  A method to signal long-term pictures using absolute POC
  A method to define in PPS a RPS containing long term pictures
Propose: Adoption of our proposed methods into HEVC
<number>