## Slide 1: JCTVC-G715: Absolute Signaling for Resolution Switching
Kiran Misra, Sachin Deshpande, Louis Kerofsky, Andrew Segall
<number>
Notes: <number>

## Slide 2: Motivation
JCTVC-F158:
  Proposed a method for changing the picture resolution without causing an instantaneous decoder refresh (IDR) or new sequence parameter set (SPS) to be sent was proposed.
  AHG18 was formed was formed at the 6th JCT-VC meeting to study and compare approaches for resolution switching.
JCTVC-F493:
  Proposed absolute signaling of reference pictures which supports error robust management of reference pictures using Reference Picture Sets.
  AHG21 was formed at the 6th JCT-VC meeting. AHG21 has produced a candidate working draft specification for signaling reference pictures.
We propose a method to enable signaling of different reference picture resolutions to be maintained in the decoded picture buffer.
  Proposed method is based on AHG21 candidate working draft
<number>
Notes: <number>

## Slide 3: Motivating example
<number>
P
P
P
P
P
I
P
P
P
P
P
P
P
(a)
P
P
P
P
P
I
P
P
P
P
P
P
(b)
P
P
P
P
P
P
I
P
P
P
P
P
P
(c)
P
P
P
Examples illustrating different picture resolutions to be maintained for motion prediction
Only a lower resolution picture should be stored in DPB
Only the higher resolution picture should be stored in DPB.
Both higher and lower resolution picture should be stored in DPB

## Slide 4: Proposal
If a stream switches to a lower resolution without an IDR or signaling a new SPS then the decoded picture buffer may contain pictures having different resolutions.
We propose signaling to the decoder that the reference pictures in the decoded picture buffer (DPB) are maintained at:
  The lower resolution only: useful if it is known that a reference picture will only be used for motion prediction at the lower resolution
  The higher resolution only: useful when the stream switches back to higher resolution and it is desired to use the long term picture stored in the DPB for motion prediction
  Both the higher and lower resolution: useful when a lower resolution version of the reference picture is used in motion prediction for lower resolution pictures. Additionally, the higher resolution version of the reference picture is used for motion prediction once the bitstream switches back to the original resolution
<number>

## Slide 5: Proposed Syntax
Description:
If reference picture and current picture resolution is different then signal which resolution the reference picture is to be maintained.
xxx_resolution_dx:
0 – keep reference at current pictures resolution
1 – keep reference at original resolution
2 – keep reference at both original resolution and at current pictures resolution

## Slide 6: Conclusion
We proposed a method to enable signaling of reference picture resolutions to be maintained in the decoded picture buffer.
Propose: Adoption of technique into HEVC
<number>