## Slide 1: On CABAC_init_idc JCTVC-G716 Kiran Misra and Andrew Segall
l
Notes: <number>

## Slide 2: Overview
We propose to clarify the meaning of cabac_init_idc
Our benefits
  Reduced number of tables compared to AVC
  Improvements in coding efficiency
  Clarification of the HEVC design

## Slide 3: Background
cabac_init_idc
  In AVC, cabac_init_idc is signaled to control the initialization of CABAC
  For P and B slices, cabac_init_idc allows selection between three initialization tables
  Total number of tables: 7
      (1-Intra, 3-P, 3-B)
HEVC
  cabac_init_idc syntax in the slice header
  Semantics indicate support for 7 tables
  No normative behavior for cabac_init_idc equal to 1 or 2 in WD
  Not present in software
cabac_init_idc specifies the index for determining the initialisation table used in the initialisation process for context variables. The value of cabac_init_idc shall be in the range of 0 to 2, inclusive.
HEVC WD4

## Slide 4: Further Motivation
Our findings
  We have not found evidence that multiple tables for P and B slices are beneficial for HEVC
  We observe that using the P slice table for B slices (and B slice tables for P slices) does provide coding benefit. This appears largely associated with the use of forward predicted B slices.

## Slide 5: Problem
Our proposal
  Maintain the number of tables for CABAC initialization to three. (As compared to the 7 anticipated with the WD semantics.) This is consistent with the HM software
  Define cabac_init_idc to be a one-bit flag to allow for P slice types to be initialized with either the “P slice type” table or “B slice type” table. Similarly, to allow for B slice types to be initialized with either the “P slice type” table or “B slice type” table.
  Signal the presence of cabac_init_idc in the PPS (or SPS if single entropy coder)
  Define the P slice table to be the default table for forward predicted B slices.
  Optionally, rename the syntax element to cabac_init_flag.

## Slide 6: Background
Synatax and semantics
cabac_init_idc specifies the index for determining the initialisation table used in the initialisation process for context variables. When cabac_init_idc is not present, it shall be inferred to be 0.
HEVC WD4
cabac_init_idc_enabled_flag equal to 0 specifies that cabac_init_idc is not present in the slice header. When cabac_init_idc_enabled_flag is not present, it shall be inferred to be 0.

## Slide 7: Result
Common test conditions
Average Impact on BD rate
  Random access: 0.0%
  LD-B: -0.1%
Benefit related to the number of initializations per coded bits…

## Slide 8: Result
Tiles test conditions
Average Impact on BD rate
  Random access: -0.1%
  LD-B: -0.3%

## Slide 9: Conclusions
Conclusions
  We propose clarification of the cabac_init_idc flag
  Three components
    Number of CABAC initialization tables defined to be 3
    cabac_init_idc is defined as a binary flag that allows selection of either the “P” or “B” table for all inter-predicted slices.
    Default table for a forward predicted B slice be the P slice table
  Benefits
    Clarification of the design
    Reduced number of number of tables
    Coding efficiency improvement
  Propose to adopt to WD.