## Slide 1: JCTVC-718:Context reduction for CABAC
Wei-Jung Chien, Joel Sole, Marta Karczewicz
Qualcomm

## Slide 2: Introduction
Context reduction related to coefficient coding
  Part1: chroma cbf
  Part2: level coding
Simulation results are provided for normal QP and low QP range.

## Slide 3: Chroma cbf coding
Contexts for luma component is less than contexts for chroma components on cbf coding.
Luma cbf
  HM4.0 : one context set (5 contexts).
Chroma cbf
  HM4.0 : one context set (5 contexts) for each of chroma cbf (cbf_cb, cbf_cr).
  Proposal : one shared context set (5 contexts) for chroma cbf (cbf_cb, cbf_cr).

## Slide 4
BD-rate | All Intra HE |  |  | Random access HE |  |  | Low delay B HE |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | 0.0% | 0.6% | -1.1% | 0.0% | 0.6% | -1.7% |  |  | 
Class B | 0.0% | 0.6% | -1.1% | 0.0% | 0.7% | -1.3% | 0.0% | 1.1% | -1.9%
Class C | 0.0% | 0.2% | -0.7% | 0.0% | 0.1% | -0.6% | 0.0% | 0.2% | -1.0%
Class D | 0.0% | -0.2% | -0.5% | 0.0% | -0.2% | -0.8% | 0.0% | -0.4% | -0.4%
Class E | 0.0% | -0.4% | 0.2% |  |  |  | 0.0% | 0.4% | 0.4%
All | 0.0% | 0.2% | -0.7% | 0.0% | 0.3% | -1.1% | 0.0% | 0.4% | -0.9%
BD-rate | All Intra HE |  |  | Random access HE |  |  | Low delay B HE |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | 0.0% | 0.2% | -0.3% | 0.0% | 0.4% | -0.8% |  |  | 
Class B | 0.0% | 0.5% | -0.7% | 0.0% | 1.3% | -2.0% | 0.0% | 1.3% | -2.2%
Class C | 0.0% | 0.2% | -0.3% | 0.0% | 0.3% | -0.4% | 0.0% | 0.4% | -0.5%
Class D | 0.0% | 0.0% | -0.2% | 0.0% | 0.1% | -0.4% | 0.0% | -0.1% | -0.1%
Class E | 0.0% | 0.1% | 0.0% |  |  |  | -0.1% | 0.7% | -0.4%
All | 0.0% | 0.2% | -0.3% | 0.0% | 0.5% | -0.9% | 0.0% | 0.6% | -0.9%
QP = 12, 17, 22, 27
QP = 22, 27, 32, 37

## Slide 5: Proposed changes for level coding
Coefficient level coding
  HM4.0 : Total 120 contexts
    coeff_abs_level_greater1_flag: 6 context sets (5 contexts in each context set)
    coeff_abs_level_greater2_flag: 6 context sets (5 contexts in each context set)
  Proposal: Total 78 contexts
    coeff_abs_level_greater1_flag
      If context set index is equal to 0 or 3, 5 contexts are used.
      Otherwise, 2 contexts are used.
    coeff_abs_level_greater2_flag
      If context set index is greater than 2, 5 contexts are used.
      Otherwise, 2 contexts are used.

## Slide 6: Proposed method
HM4.0
  ctxIdxInc = ( ctxSet * 5 ) + Min( 4, greater1Ctx )
  ctxIdxInc = ( ctxSet * 5 ) + Min( 4, greater2Ctx )
Proposed method
  ctxIdxInc = ( ctxSet * 5 ) + Min( Threhold1, greater1Ctx )
  ctxIdxInc = ( ctxSet * 5 ) + Min( Threhold2, greater2Ctx )
 | 0 | 1 | 2 | 3 | 4 | 5
Threhold1 | 4 | 1 | 1 | 4 | 1 | 1
Threhold2 | 4 | 4 | 4 | 1 | 1 | 1

## Slide 7
BD-rate | All Intra HE |  |  | Random access HE |  |  | Low delay B HE |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | 0.0% | 0.0% | 0.0% | 0.1% | -0.4% | 0.0% |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | -0.1% | 0.0% | 0.0% | -0.1%
Class C | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.1% | -0.1%
Class D | 0.0% | 0.0% | 0.0% | 0.1% | 0.3% | -0.1% | 0.0% | -0.4% | -0.1%
Class E | 0.0% | 0.0% | 0.0% |  |  |  | 0.1% | -0.7% | 0.5%
All | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.2% | 0.0%
BD-rate | All Intra HE |  |  | Random access HE |  |  | Low delay B HE |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.1% |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0%
Class C | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | -0.2% | 0.0% | -0.1% | -0.1%
Class E | 0.0% | -0.1% | 0.0% |  |  |  | 0.0% | -0.4% | -0.2%
All | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | -0.1%
QP = 12, 17, 22, 27
QP = 22, 27, 32, 37

## Slide 8: Conclusions
The proposal reduces 5+42 contexts with coding performance changes.
Recommend the adoption of the proposed changes

## Slide 9: Coefficient level coding
  G121: Total 84 contexts
    coeff_abs_level_greater1_flag: 6 context sets (4 contexts in each context set)
    coeff_abs_level_greater2_flag: 6 context sets (3 contexts in each context set)
  Proposal: Total 78 contexts
    coeff_abs_level_greater1_flag
      If context set index is equal to 0 or 3, 5 contexts are used.
      Otherwise, 2 contexts are used.
    coeff_abs_level_greater2_flag
      If context set index is greater than 2, 5 contexts are used.
      Otherwise, 2 contexts are used.

## Slide 10: Comparison with G121
 | All Intra | Random Access | Low Delay
G121 | 0.1% | 0.0% | 0.0%
G718 | 0.0% | 0.0% | 0.0%
 | All Intra | Random Access | Low Delay
G121 | 0.1% | 0.0% | 0.0%
G718 | 0.0% | 0.0% | 0.0%
QP = 22, 27, 32, 37
QP = 12, 17, 22, 27