## Slide 1: JCTVC-G719: Structured Level Limits
Louis Kerofsky1, Kiran Misra1, Andrew Segall1
Elena Alshina2, Alexander Alshin2
1Sharp Labs of America
2Samsung Electronics Ltd.
<number>
Notes: <number>

## Slide 2: Motivation
Limitation needed on coefficients immediately following dequantization
  JCTVC-E243 Clipping following dequant: Clipping is necessary even for ‘typical’ operation such as nearest neighbor quantization of result of extreme residual. Normative solution to ensure 16-bit coefficient data.
  JCTVC-F257 Encoder level limits defined which ensure the clip following dequant is unneeded when levels are limited. No impact on coding performance. Derivation of limits requires division. No normative behavior required.
  Limitation needed on maximum level needed: Largest level occurs for 32x32 transform size and QP=0, source bit-depth of 10.
Limitation needed on bits required for dequantization
  Bits needed for Dequant depend on largest level and largest dequantization parameters i.e. QP=51.
<number>

## Slide 3: Proposal
Place upper limit on maximum absolute value of level independent of QP, block size, bit-depth i.e. |level|<2^16 (largest level with QP=0, 32x32, B=10 is 52424)
Describe formula for level bound depending on QP, block size, bit-depth
  Basic level bounds
    LB(x) = {13106,11650,10279,9197,8191,7281} for x=0,1,2,3,4,5
  General formula:
    LevelBound(QP,M,B) = (LB [QP%6]<<( B-8))>>(5-M+QP/6)
    where QP is the quantization parameter and M=log2(N) where N is the transform size and B is the bit-depth parameter.
  For NSQT, M=(log2(N1)+log2(N2))/2 in a transform size N1xN2.
Clip absolute levels based on level bound prior to dequantization
  level = sign(level)*clip(abs(level),LevelBound(QP,M,B))
Remove clipping following dequantization
Note as QP increases by 6 so bin size doubles, level limit is halved
<number>

## Slide 4: Benefits
Normative bounds of dynamic range of levels, dequantization, and coefficients ensured.
Division free formula for level limits depending on 6 constants and shift operations using QP, M, B.
Bounds allow all 16-bit coefficients to be signaled.
Reduces bits needed for dequantization. (Fewer bits needed during dequantization process since maximum level decreases as QP increases. MaxLevel*40 compared to MaxLevel*72<<(51/6) is a 9-bit difference)
Clipping following dequant removed. Clip of positive portion of absolute value only needed in implementation.
Coefficients still limited to 16-bits following dequantization.
Compatible with different transform elements i.e. core, NSQT, SDT
<number>

## Slide 5: Conclusion
We proposed a method to limit the dynamic range of levels, bits for dequantization, and ensure 16-bit coefficient data.
Propose: Adoption of technique into HEVC
<number>