## Slide 1: JCTVC-G720: Dequantization with symmetric reconstruction points
Louis Kerofsky, Kiran Misra, Andrew Segall
Sharp Labs of America
<number>
Notes: <number>

## Slide 2: Motivation
JCTVC-E243: Dequantization is based on integer multiplication, offset, and right shift.
  coeffQ = ((level*IQ << (QP/6)) + offset)>>(M-1+DB), offset = 1<<(M-2+DB)
  Reconstruction points are not always symmetrically distributed i.e. DQ(-level)!=-DQ(level) for some situations but nearly so.
  Worst case Dquant calculation uses 17 signed bits for signed level value implying multiplication in Dequant can’t use 16-bit multiply
Dequant offset proposals i.e. JCTVC-G728, JCTVC-G382
  Use |level| during dequantization in motivation i.e. JVT-N011.
  Compared to E243, larger offset values used in dequantization increasing lack of symmetry of reconstruction points
  Signed level and right shift implementation differs from theory and introduces bias in reconstruction points
<number>

## Slide 3: Proposal
Dequantization process described using absolute value of level and sign of level separately
coeffQ = Sgn(level)((|level|*IQ << (QP/6)) + offset)>>(M-1+DB), offset = 1<<(M-2+DB)
Note this definition of Sgn(x) differs from the definition of Sign(x) used in WD text in that Sgn(0)=0 but Sign(0) = 1
<number>

## Slide 4: Benefits
Reconstruction points clearly symmetric about zero i.e. DQ(-|level|) = -DQ(|level|)
Allows use of 16-bit unsigned multiplier for dequantization in all cases avoiding the need for 17-bit signed multiply for low QP, 32x32 block, and 10-bit source
Desired handling of dequantization offset modifications if adopted.
Note: Proposed dequantization formula is identical to existing HM4.0 design on common conditions QP=22, 27, 32, 37 since the right shift is by at most 4 bits and the term IQ<<(QP/6) is divisible by 2^4 for this range of QP.
Note: Computation of |level| unneeded in implementation since sign and magnitude signaled individually
<number>

## Slide 5: Conclusion
We proposed a produce reconstruction points symmetrically located about zero even when an offset is used in dequantization. Dequantization can be achieved with 16-bit unsigned multiplication.
Propose: Adoption of technique into HEVC
<number>