## Slide 1: JCTVC-G737 “CE10: Full Factorization Core Transforms for HEVC”
Elena Alshina, Alexander Alshin,
Wonjae Lee, JeongHoon Park, Kulbhushan Pachauri (Samsung)
Pankaj Topiwala (FastVDO)

## Slide 2: Partial butterfly flow graph == HM3.0
EEEO[0] = g_aiT32[8][0]*tmp[8] + g_aiT32[24][0]*tmp[24];
EEEO[1] = g_aiT32[8][1]*tmp[8] + g_aiT32[24][1]*tmp[24];
EEEE[0] = g_aiT32[0][0]*tmp[0] + g_aiT32[16][0]*tmp[16];
EEEE[1] = g_aiT32[0][1]*tmp[0] + g_aiT32[16][1]*tmp[16]
for (k=0;k<4;k++) {
EEO[k] = g_aiT32[4][k]*tmp[4]+g_aiT32[12][k]*tmp[12]
+g_aiT32[20][k]*tmp[20] + _aiT32[28][k]*tmp[28]; }
for (k=0;k<8;k++) {
EO[k] = g_aiT32[ 2][k]*tmp[ 2]+ g_aiT32[ 6][k]*tmp[ 6]+ g_aiT32[10][k]*tmp[10]+
g_aiT32[14][k]*tmp[14]+ g_aiT32[18][k]*tmp[18]+ g_aiT32[22][k]*tmp[22]+
g_aiT32[26][k]*tmp[26]+ g_aiT32[30][k]*tmp[30]; }
for (k=0;k<16;k++) {
O[k] = g_aiT32[ 1][k]*tmp[ 1] + g_aiT32[ 3][k]*tmp[ 3] + g_aiT32[ 5][k]*tmp[ 5] + g_aiT32[ 7][k]*tmp[ 7] +
g_aiT32[ 9][k]*tmp[ 9] + g_aiT32[11][k]*tmp[11] + g_aiT32[13][k]*tmp[13] + g_aiT32[15][k]*tmp[15] +
g_aiT32[17][k]*tmp[17] + g_aiT32[19][k]*tmp[19] + g_aiT32[21][k]*tmp[21] + g_aiT32[23][k]*tmp[23] +
g_aiT32[25][k]*tmp[25] + g_aiT32[27][k]*tmp[27] + g_aiT32[29][k]*tmp[29] + g_aiT32[31][k]*tmp[31]; }
JCTVC-G737 “CE10: Full Factorization Core Transforms for HEVC”

## Slide 3: Full-factorized flow graph
JCTVC-G737 “CE10: Full Factorization Core Transforms for HEVC

## Slide 4: H/w test G737 vs HM4.0 core transform
JCTVC-G737 “CE10: Full Factorization Core Transforms for HEVC
h/w test materials are disclosed for cross-check |  |  | 
Test | 1 | 2 | 3
RTL generator | SynphonyCC | SynphonyCC | CATAPULT C
Design Compiler test | STMicro | Samsung | Samsung
Relative G/C, % | 39...67% | 43...72% | 63...78%
32pt 1D inverse transform test

## Slide 5: Possibility of sharing area between forward and inverse transforms
Total number of multipliers modules |  | 
Size | HM-4.0 (*) | G737
4 | 3 | 2
8 | 7 | 6
16 | 15 | 13
32 | 29 | 30
(*) M. Tikekar, C.-T. Huang, C. Juvekar, A. Chandrakasan (MIT)
“Core Transform Property for Practical Throughput Hardware Design” ,
JCTVC-G265, 7th JCT-VC Meeting, Geneva, Switzerland, November, 2011
JCTVC-G737 “CE10: Full Factorization Core Transforms for HEVC

## Slide 6: Multipliers
/// 32x32 /// constants
64 = cos(1 *p/64)*64
63 = cos(3 *p/64)*64
62 = cos(5 *p/64)*64
60 = cos(7 *p/64)*64
58 = cos(9 *p/64)*64
55 = cos(11*p/64)*64
51 = cos(13*p/64)*64
47 = cos(15*p/64)*64
43 = cos(17*p/64)*64
38 = cos(19*p/64)*64
33 = cos(21*p/64)*64
27 = cos(23*p/64)*64
22 = cos(25*p/64)*64
16 = cos(27*p/64)*64
9 = cos(29*p/64)*64
3 = cos(31*p/64)*64
89 = cos( 4*p/64)*64*sqrt(2.0)
75 = cos(12*p/64)*64*sqrt(2.0)
50 = cos(20*p/64)*64*sqrt(2.0)
18 = cos(28*p/64)*64*sqrt(2.0)
/// 4x4 /// constants
83 = cos( 8*p/32)*64*sqrt(2.0)
64 = cos(16*p/32)*64*sqrt(2.0)
36 = cos(24*p/32)*64*sqrt(2.0)
/// 8x8 /// constants
90 = sqrt(2.0) * 64
63 = cos( 4*p/64)*64
53 = cos(12*p/64)*64
36 = cos(20*p/64)*64
12 = cos(28*p/64)*64
/// 16x16 /// constants
64 = cos(2 *p/64)*64
61 = cos(6 *p/64)*64
56 = cos(10*p/64)*64
49 = cos(14*p/64)*64
41 = cos(18*p/64)*64
30 = cos(22*p/64)*64
19 = cos(26*p/64)*64
6 = cos(30*p/64)*64

## Slide 7: Bits accumulation (JCTVC-G782)
Size | L1Norm | MaxAbs coeff | Reg. bits | De-scale bits | MaxAbs Temp | Temp bits | Reg. bits | De-scale bits | rec res | rec res bits
8 | 30622 | 32767 | 31 | 13 | 32767 | 16 | 31 | 18 | 3828 | 13
16 | 60326 | 32767 | 32 | 13 | 32767 | 16 | 32 | 18 | 7541 | 14
32 | 119262 | 18006 | 32 | 13 | 18006 | 16 | 32 | 18 | 8192 | 15
JCTVC-G737 “CE10: Full Factorization Core Transforms for HEVC
DeQuant  Clip3  1st Inv Transform  Clip3  2nd Inv Transform

## Slide 8: SIMD test for core transform
JCTVC-G737 “CE10: Full Factorization Core Transforms for HEVC
Code Proponent |  | Samsung |  |  |  |  | Cisco | 
Tester |  | Samsung |  |  |  | Cisco | Cisco | Samsung
System |  | 3.4GHz, 4GB |  |  |  | ?? GHz, ?GB | 3.53GHz,16GB | 3.4GHz, 4GB
8pt |  |  |  |  |  |  |  | 
Partial butterfly |  |  |  |  | 144 | 146 | 138 | 142
Full butterfly |  |  |  |  | 167 | 168 |  | 
16pt |  |  |  |  |  |  |  | 
Partial butterfly |  |  |  | 848 |  | 859 | 836 | 918
Full butterfly |  |  |  | 890 |  | 901 |  | 
32pt |  |  |  |  |  |  |  | 
Partial butterfly |  |  | 5900 |  |  | 5990 | 5329 | 5643
Full butterfly |  |  | 4902 |  |  | 4937 |  | 
Intel Processor Type |  | i7(Sandybridge)
OS |  | Ubuntu 11.10
 |  | 64 bit
SIMD |  | SSE4
turbo boost |  | disabled

## Slide 9: Performance in HM4.0 (normal QP)
JCTVC-G737 “CE10: Full Factorization Core Transforms for HEVC
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | 0,2% | -0,1% | -0,1% | 0,3% | 0,0% | -0,1%
Class B | 0,1% | -0,1% | -0,1% | 0,1% | -0,1% | -0,1%
Class C | 0,0% | 0,0% | -0,1% | 0,0% | 0,0% | -0,1%
Class D | 0,0% | -0,1% | 0,0% | 0,0% | 0,0% | 0,0%
Class E | 0,1% | -0,1% | -0,1% | 0,1% | -0,1% | 0,0%
Class F | 0,1% | -0,1% | 0,0% | 0,0% | 0,0% | 0,0%
Overall | 0,1% | -0,1% | -0,1% | 0,1% | 0,0% | 0,0%
Enc T.[%] | 99% |  |  | 96% |  | 
Dec T.[%] | 97% |  |  | 96% |  | 
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A | 0,1% | -0,2% | -0,3% | 0,1% | 0,2% | 0,0%
Class B | 0,0% | -0,1% | 0,0% | 0,0% | -0,2% | -0,2%
Class C | 0,0% | 0,0% | -0,1% | 0,0% | 0,0% | 0,0%
Class D | 0,1% | -0,1% | 0,0% | 0,0% | -0,1% | 0,1%
Class E |  |  |  |  |  | 
Class F | 0,0% | 0,0% | -0,1% | 0,1% | 0,0% | 0,0%
Overall | 0,0% | -0,1% | -0,1% | 0,0% | 0,0% | 0,0%
Enc T.[%] | 99% |  |  | 99% |  | 
Dec T.[%] | 99% |  |  | 100% |  | 
Low delay B HE |  |  | Low delay B LC |  | 
Y | U | V | Y | U | V
0,0% | -0,1% | -0,4% | 0,0% | -0,1% | 0,1%
0,1% | 0,0% | -0,2% | 0,0% | 0,1% | -0,1%
0,0% | -0,1% | -0,1% | 0,0% | 0,4% | -0,3%
0,1% | 0,5% | 0,4% | 0,0% | -0,1% | -0,3%
-0,1% | -0,4% | -0,3% | 0,1% | 0,2% | 0,1%
0,0% | -0,1% | -0,1% | 0,0% | 0,1% | -0,1%
99% |  |  | 99% |  | 
99% |  |  | 100% |  | 
Low delay P HE |  |  | Low delay P LC |  | 
Y | U | V | Y | U | V
0,0% | 0,1% | -0,2% | 0,0% | 0,0% | -0,1%
0,0% | 0,2% | -0,1% | 0,0% | -0,1% | 0,1%
0,0% | -0,4% | -0,8% | 0,0% | -0,1% | -0,4%
0,0% | 1,1% | -0,5% | 0,0% | -0,5% | -0,5%
0,0% | -0,2% | -0,3% | 0,0% | 0,3% | 0,1%
0,0% | 0,1% | -0,4% | 0,0% | -0,1% | -0,1%
99% |  |  | 98% |  | 
100% |  |  | 99% |  | 
Avg. across 8 test cases 0.0%(Y), 0.0%(U), -0.1%(V)

## Slide 10: Conclusion
Based on test results:
0.0%(Y) 0.0% (U) -0.1%(V)
(average performance across all 8 test cases in normal QP tests)
we would like to recommend adoption for proposed core transform modification for HM5.0 and WD.
This will keep possibility of 2 equivalent implementations:
matrix multiplication
partial butterfly
which are available in HM4.0 and add one more equivalent implementation
full-factorized form
which uses 4 times smaller number of multiplications in 32 pt transform compare to default partial butterfly and so 20% faster in SIMD implementation (by Samsung’s measurement) and requires 2 less G/C in h/w implementation (according to ST Micro’s independent analysis).
JCTVC-G737 “CE10: Full Factorization Core Transforms for HEVC