## Slide 1: Non-CE2: Harmonization of HE residual coding and NSQT
J. Sole, X. Wang, M. Karczewicz Qualcomm
J. Kim, B. Jeon LGE
JCTVC-G750

## Slide 2: Motivation
NSQT uses non-square transforms
  Block sizes: 32×8, 8×32, 16×4, 4×16
Issue: entropy coder only handles square blocks
  NSQT introduces mappings between non-square transforms and ‘square-based’ entropy coder
    Extra computational complexity
    Neighborhood relation between coefficients is ‘broken’
Harmonization: modify entropy coding in HE to handle similarly square and non-square blocks (without intermediate mappings)
  Contexts for significance map
  Scans for NSQT blocks
  Last coefficient coding
JCT-VC, Geneva, November 2011
<number>

## Slide 3: NSQT harmonization with CABAC
Significance map coding
  Context derivation for the non-square blocks similar to square blocks
    Blocks with same sizes share (transposed) contexts
  Blocks 16×4 and 4×16 use contexts based on position
  Blocks 32×8 and 8×32 use the method for blocks 16×16 and 32×32
  No increase in the number of ocntexts
Last significant position coding
  Context depends on the length of the side of the block
JCT-VC, Geneva, November 2011
<number>
15 | 15 | 16 | 16 | 17 | 17 | 18 | 18 | 23 | 23 | 24 | 24 | 25 | 25 | 26 | 26
15 | 15 | 16 | 16 | 17 | 17 | 18 | 18 | 23 | 23 | 24 | 24 | 25 | 25 | 26 | 26
19 | 19 | 20 | 20 | 21 | 21 | 22 | 22 | 27 | 27 | 28 | 28 | 29 | 29 | 30 | 30
19 | 19 | 20 | 20 | 21 | 21 | 22 | 22 | 27 | 27 | 28 | 28 | 29 | 29 | 30 | 30
16×4 block
15 | 15 | 19 | 19
15 | 15 | 19 | 19
16 | 16 | 20 | 20
16 | 16 | 20 | 20
17 | 17 | 21 | 21
17 | 17 | 21 | 21
18 | 18 | 22 | 22
18 | 18 | 22 | 22
23 | 23 | 27 | 27
23 | 23 | 27 | 27
24 | 24 | 28 | 28
24 | 24 | 28 | 28
25 | 25 | 29 | 29
25 | 25 | 29 | 29
26 | 26 | 30 | 30
26 | 26 | 30 | 30
4×16 block

## Slide 4: NSQT harmonization with CABAC
Scan harmonization
  Removal of the mapping between non-square and square blocks
  Diagonal scan starting from left-bottom side for non-square blocks
    Simple extension of the square block case
JCT-VC, Geneva, November 2011
<number>
0 | 2 | 5 | 9 | 13 | 17 | 21 | 25 | 29 | 33 | 37 | 41 | 45 | 49 | 53 | 57
1 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32 | 36 | 40 | 44 | 48 | 52 | 56 | 60
3 | 7 | 11 | 15 | 19 | 23 | 27 | 31 | 35 | 39 | 43 | 47 | 51 | 55 | 59 | 62
6 | 10 | 14 | 18 | 22 | 26 | 30 | 34 | 38 | 42 | 46 | 50 | 54 | 58 | 61 | 63
16×4 block
0 | 2 | 5 | 9
1 | 4 | 8 | 13
3 | 7 | 12 | 17
6 | 11 | 16 | 21
10 | 15 | 20 | 25
14 | 19 | 24 | 29
18 | 23 | 28 | 33
22 | 27 | 32 | 37
26 | 31 | 36 | 41
30 | 35 | 40 | 45
34 | 39 | 44 | 49
38 | 43 | 48 | 53
42 | 47 | 52 | 57
46 | 51 | 56 | 60
50 | 55 | 59 | 62
54 | 58 | 61 | 63
4×16 block

## Slide 5: Results
Common conditions, HE configuration
  Cross-check: KAIST (JCTVC-G596)
JCT-VC, Geneva, November 2011
<number>
BD-rate | Random access HE |  |  | Low delay B HE |  | 
 | Y | U | V | Y | U | V
Class A | 0.03% | -0.12% | -0.31% |  |  | 
Class B | -0.05% | -0.06% | 0.00% | -0.05% | -0.19% | -0.20%
Class C | -0.04% | -0.04% | 0.05% | -0.07% | -0.19% | -0.15%
Class D | 0.00% | -0.02% | -0.19% | -0.08% | -0.23% | -0.17%
Class E |  |  |  | -0.01% | -0.66% | 0.77%
All | -0.02% | -0.06% | -0.10% | -0.06% | -0.29% | 0.00%
Enc T[%] | 100% |  |  | 101% |  | 
Dec T[%] | 100% |  |  | 100% |  | 

## Slide 6: Conclusions
Straightforward extension of HE entropy coding to non-square blocks
  Diagonal scans and similar contexts for significance map
  Same number of contexts
Complexity reduction
  Removal of the intermediate mapping between block shapes
Slightly better BD-rate
JCT-VC, Geneva, November 2011
<number>
YUV avg | RA– HE | LB – HE | LP – HE
With class F | -0.03% | -0.12% | -0.10%
No class F | -0.03% | -0.08% | -0.09%

## Slide 7: Thank you!
JCT-VC, Geneva, November 2011
<number>

## Slide 8: BD-rate (with class F and low delay P)
Common conditions, HE configuration
JCT-VC, Geneva, November 2011
<number>
 | All Intra HE |  |  | Random Access HE |  |  | Low delay B HE |  |  | Low delay P HE |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Class A | 0.00% | 0.00% | 0.00% | 0.03% | -0.12% | -0.31% |  |  |  |  |  | 
Class B | 0.00% | 0.00% | 0.00% | -0.05% | -0.06% | 0.00% | -0.05% | -0.19% | -0.20% | -0.07% | -0.13% | -0.27%
Class C | 0.00% | 0.00% | 0.00% | -0.04% | -0.04% | 0.05% | -0.07% | -0.19% | -0.15% | -0.06% | 0.01% | -0.03%
Class D | 0.00% | 0.00% | 0.00% | 0.00% | -0.02% | -0.19% | -0.08% | -0.23% | -0.17% | -0.04% | -0.25% | -0.26%
Class E | 0.00% | 0.00% | 0.00% |  |  |  | -0.01% | -0.66% | 0.77% | -0.09% | -0.07% | -0.14%
Class F | 0.00% | 0.00% | 0.00% | 0.00% | -0.08% | -0.08% | -0.33% | -0.34% | 0.03% | -0.12% | -0.08% | -0.29%
Overall | 0.00% | 0.00% | 0.00% | -0.01% | -0.06% | -0.10% | -0.11% | -0.30% | 0.00% | -0.08% | -0.11% | -0.21%
 | 0.00% | 0.00% | 0.00% | -0.01% | -0.08% | -0.10% | -0.11% | -0.31% | -0.02% | -0.08% | -0.09% | -0.21%