## Slide 1: The Art of Writing Standards: Some “Shalls” and “Shoulds” for Better Quality Interop Specs
Gary J. Sullivan
Microsoft Corp.
Joint Collaborative Team on Video Coding (JCT-VC) of ITU-T SG16 WP3 and ISO/IEC JTC1/SC29/WG11 7th Meeting: Geneva, CH, 21-30 Nov., 2011 | Document: JCTVC-G777
(Only minor updates relative to JCTVC-F333)

## Slide 2: First thoughts: Channeling Aharon Gill
Once the spec is written, whatever was in your head is gone. Only what was put in the document survives.
The interpretation of the spec must not depend on assumed background knowledge
  The reader must not be assumed to share your point of view
  Provide all of the information that is necessary.
Lack of ambiguity is key
A standard is not a tutorial
  Don't put in any "salesmanship" opinionated commentary
  Don't waste time, energy and space trying to summarize
  Don't oversimplify
  It's better to just leave it out, and publish some overview articles
It is better if you approach the problem of writing the spec from the point of view of technical neutrality, as if you have no technical intentions whatsoever.

## Slide 3: How Your Spec Will be Used
If you are lucky, people will use your spec in ways you do not anticipate.
  You should plan for this and to some extent you should encourage it.
  However, you must establish clear limits on such freedom
    Ensure that interoperability is achieved
    But avoid unnecessary burdens on implementations
In fact, if you are lucky, many people will use your spec incorrectly and even clearly violate it.
If you are not lucky, they will simply not use your spec.

## Slide 4: The Scope of an Interop Standard
Only the Syntax and Decoder are standardized:
  Enables interoperability
  Permits optimization beyond the obvious
  Permits complexity reduction for implementability
  Allows quality to improve over time
  Provides no guarantees of Quality
Keep that in the front of your mind – don't violate it for conceptual convenience
Don't pretend the scope is different than what it really is
Pre-Processing
Encoding
Source
Destination
Post-Processing
& Error Recovery
Decoding
Scope of Standard

## Slide 5: Your Starting Basis
When working on an amendment or corrigendum, do not start from a prior committee editor's draft – get the starting basis text from the secretariat
For editing work, it is always best to work from a complete integrated text rather than attempting to directly prepare a list of revisions.
  From the ITU-T perspective, it is also generally considered better to publish a complete integrated new edition
  For texts that have already become substantially fragmented, make the effort to produce and publish an integrated new edition
  Generally do not discuss or refer to an amendment as being an amendment within its own text; conceptually an amendment is not a stand-alone document – it is a list of instructions for editing another document

## Slide 6: The Difference Between Informative and Normative Text
Be very careful to make it clear whether what you are writing is normative or informative.
Don't use the word "shall" in informative text. Use it sparingly when you do use it. Mean it when you use it.
Avoid using the word "note" in normative text.
To clearly separate an informative remark from normative text: put it in a NOTE.
A "NOTE" should be formatted properly as a "NOTE".
Phrase informative text in a way that makes it clear that any statements describing mandatory conformance requirements are only observations about requirements that are established somewhere else in a normative fashion – as informative text must not contain statements that establish normative conformance requirements.
Any normative expression of a requirement for conformance to the standard (e.g., statements using the term "shall") must express a requirement that is completely unambiguous.
Vagueness or even incorrect information is not so much of a tragedy if it is clearly within an informative context.
Informative references go in the Bibliography at the end of the specification. (Do not forget to list all of them.)

## Slide 7: Normative Referencing (Clause 2)
Normative references go in clause 2.
Don't list things as normative references unless absolutely necessary to the spec.
Don't forget to list all of the normative references.
Don't just vaguely refer to some specification. That spec has a formal specification name and number. Figure out what it is, and put it in clause 2.
Normative referencing to specifications other than those produced by ITU-T, ISO, and IEC require following special practices – in both ISO/IEC and ITU-T. The rules on this subject in ITU-T are especially strict, and the rules in ISO/IEC are no joke either. The procedures for normative referencing can delay or block the approval of your text.
Avoid using excessive use of normative referencing. Don't make someone go find, buy and dig through another specification just to find one or two numbers (or to later learn that they didn't really need anything in it).
When using normative referencing, be very precise about what aspect(s) of the other specification you are referencing normatively. Don't give the impression that conforming to the whole specification is necessary if you only need some small piece of it.

## Slide 8: Definitions and Abbreviations (Clauses 3 and 4)
Don't ignore clause 3 (the Definitions). Write good definitions there, depend on them, use them, and follow them.
Unfortunately, the ISO editor prohibits all definitions longer than one sentence.
  As a result, you may need to put some vagueness in the definition and specify the full details elsewhere
In clause 4, list all of the abbreviations that you use in the spec.

## Slide 9: Establish Strong Editorial Conventions
The reader should be able to see at a glance the difference between a word, a variable name, a syntax element name, an enumeration value, a function name, etc.
Try to follow the same conventions used in other (good) documents.
Avoid using a variety of slightly different phrases (and spellings) to mean the same thing. It is unprofessional, ambiguous, confusing, and unfriendly to document searching.
Pick names for things (syntax elements and special terms) that can be used conveniently as unique search strings.
Avoid using a name that is a subset of another name, because this means that you will have to step through many irrelevant distractions before you find what you are looking for.
Avoid using a variable name or syntax element name that is also a word.
Don't confuse the name of something with its meaning. The meaning still needs to be defined separately (and clearly). In principle, the name is just a label, and could it be any arbitrary string of characters.

## Slide 10: Coordination, Uniformity, and Stability
When referring to ITU-T and ISO/IEC common text standards in the text, do not exclusively refer to just the ISO or ISO/IEC publication and organization. Do not ignore the ITU-T (or the IEC either, for that matter).
Use the correct document template and editorial formatting. This particularly applies to ITU-T/ISO/IEC common and twin text. This can prevent a large quantity of annoying little problems with paragraph spacing, fonts, figure titles, table titles, etc.
Avoid renumbering existing annexes (even if there is a deleted one). New Annexes should get the next available letter, deleted ones should be kept as a placeholder saying "This Annex has been deleted").

## Slide 11: Some Formatting Rules
In the title of a section of a specification, and in the title of the specification itself, generally only the first word should be capitalized.
Don't capitalize things arbitrarily or (especially) inconsistently.
When in doubt, don't capitalize it.
Just because it means something special is not a sufficiently good reason to capitalize it.
A clause or subclause should contain either some text (e.g., a few paragraph) or some subordinate subclauses, not both.
Generally do not refer to the committee within the text (except perhaps in a Foreword). Generally do not discuss the history of the development of the text within the text. The text should be a technical specification without extraneous remarks such as "the MPEG committee provided ..."

## Slide 12: Basic Editing Tips
Avoid informal language, such as the use of contractions and the word "too".
Do not use colour in figures in a way that will make the result unreadable when printed on a monochrome printer.
Add special strings, such as variable names, to your spelling dictionary. Then when you misspell a variable name, the spelling checker will flag it. (Of course, try to be very careful to avoid letting misspellings creep into your spelling dictionary.)
Be very careful about using the "find and replace" feature. Never (or almost never) use "replace all". You can probably guess how the string "selecTable" ended up in a draft standard.

## Slide 13: Microsoft Word Basics
In general, Microsoft Word is really excellent software
But you should need to learn how to customize it somewhat. (It is generally best to use it on Windows 7.)
Disable the following features of Microsoft Word (if you don't know how to disable them, take the time to figure it out)
  Automatic language detection
  Automatic capitalization of the first letter of sentences
  Automatic capitalization of the first letter of table cells
  Automatic use of suggestions from the spelling checker
  Automatic field updating when opening a document
  Automatic field updating when printing (sometimes difficult)
  Automatic conversion to "Smart quotes"
  Automatic capitalization of "i".

## Slide 14: Microsoft Word Tips
Learn how to use the "Keep with next" paragraph property in Microsoft Word. It can be useful.
The "Keep lines together" property can also come in handy once in a while.

## Slide 15: About Character Codes (including dashes and minuses)
To toggle between a character code and the character itself, use Alt-X.
An ordinary hyphen is character code 002D.
The dash character that results from automatic conversion if you type something like "x – x y" is character code 2013 (an "en dash").
A minus sign (−) is character code 2212. It is not the same thing as a dash.
The dash character that the ITU uses to follow the word "NOTE" doesn't actually seem to have a character code. It is the non-breaking dash "". To produce a non-breaking dash, use Shift-Control-<dash>.
A non-breaking dash often will not survive a cut-paste operation (unless you use the "keep source formatting option, which I don't recommend). Watch out for that.
A non-breaking dash looks different than a regular dash on your computer display. But on paper, it doesn't.

## Slide 16: Hyphenation and Numbers
Use hyphens and dashes correctly
  Don't hyphenate a term inconsistently. Don't write a spec that has "bit rate", "bit-rate", and "bitrate" scattered around in it for no reason.
  When in doubt, don't hyphenate it.
  Hyphenation can sometimes be used to construct a compound modifier (i.e., an adjective or adverb) from multiple words.
  It may be OK to have "the bit rate is" in one place in a document and "bit-rate relationship" somewhere else if it is for that reason.
  Do not try to construct a noun that way. "Bit-rate" is not a noun.
  Some useful guidelines about the use of hyphens and dashes can be found at http://en.wikipedia.org/wiki/Wikipedia:HYPHEN and http://en.wikipedia.org/wiki/Wikipedia:DASH.
Learn when to say "3" and when to say "three". See http://en.wikipedia.org/wiki/Wikipedia:Manual_of_Style#Numbers.

## Slide 17: About Microsoft Word Fields
Set the "field shading" option in Microsoft Word to "always". If you don't do that, you may not be able to see the difference between text and a linked field, and strange things can happen.
F9 will update a field (unless it is locked – see below).
Control-F9 will insert a new field.
Shift-F9 will toggle between the field code and its value.
Shift-Control-F9 will change a field to text (be very careful about this one).
Control-F11 will lock a field.
Shift-Control-F11 will unlock a field.

## Slide 18: More Microsoft Word Tips
Sometimes when Microsoft Word gets confused, it will change a link to a section number to produce the number 0. If you prefix each cross-reference with "clause" or "subclause", you can search for "clause 0" (although ITU and ISO/IEC prefer to omit the word).
Once in a while, search the document for the string "not found", since broken links in Microsoft Word will ordinarily evaluate to something like "Error! Reference not found".
Microsoft Word has a feature called the "document map" (in older versions) or "navigation pane" (in the 2010 version). It can be useful.
Set your default paste option, for copying things from one file to another, to "text only". Otherwise, you may end up "polluting" the style content of the file you're pasting into with styles from the other file.

## Slide 19: Cross-references
Bookmarks are a good way to do cross-referencing. In particular, they can survive cut-paste operations.
Cross-referencing to clause numbers and subclause numbers and table numbers and figure numbers (unless sequence number tricks or bookmarks are used) seems to break when you cut something from one file and splice it into another.
  The broken cross-references tend to look OK when they are copied in, but then they show up as broken links when the file is saved and the links are updated later by a print or print preview operation.
  Bookmarks seem more portable.
Learn how to insert a new clause or list item without breaking cross-references to the existing one.
The publication process sometimes "flattens" cross-references (i.e. converts them to text). Watch for it, and try to stop them.

## Slide 20: Spelling – General
ITU (and general UN) guidelines say to use the current edition of the Concise Oxford Dictionary (COD).
Where alternative forms are given in the COD, the preferred spelling should be used. The preferred spelling is the one which is presented first (e.g. for "judgement, judgment": use "judgement"; "adviser (also disp. advisor)": use "adviser") or to which the reader is referred (e.g. "tire, US variant of "tyre": use "tyre").
Free web site using the COD: http://www.wordreference.com/definition/
ISO/IEC guidelines are essentially the same
There seems to be no Microsoft Word language dictionary that corresponds exactly to the COD; the closest may be Canadian English

## Slide 21: Spelling: -ize, -ise and -yse
Words ending in -ize, -ise and -yse
  Where there is a choice between using the suffix -ize or -ise (e.g. organize, liberalization, standardization, harmonize), -ize, derived from the Greek -izo, is preferred, in accordance with the first spelling of such words given in the COD.
  For some words, the -ise is not a suffix but part of the root of the word; in these cases there is no choice and -ise must be used (e.g. surprise, comprise, enterprise, improvise, advertise, franchise). Similarly, ‑yse must be used for words derived from the Greek lusis (as in analyse, dialyse and hydrolyse).

## Slide 22: Spelling – Particular Words
ad hoc (no italics)
ad hoc group (when capitalized: Ad hoc Group)
analogue
analyse
audiovisual
bandwidth
baseline
behaviour
bit rate (noun); bit-rate (adj.)
bits per second; bit/s; kbit/s; Mbit/s; Gbit/s
broadband
bypass
cancel; cancelled; cancelling
cannot
centre; centred; centring
coefficient
collocate; collocation
comprise
colour dependant (noun); dependent (adj.)
data (a plural word)
de facto (italic)
dependent (adj.)
disk (computer)
e.g. (not followed by a comma)
formulae (mathematical)

## Slide 23: Spelling – Particular Words
fulfil, fulfilled
grey
highpass (adj.)
implementer (not implementor)
i.e. (not followed by a comma)
index (pl. indices [maths] ; indexes [books])
Internet
label; labelled; labelling
laptop
lowpass (adj.)
meter (instrument); metre (unit of length)
microprocessor
multiband; multichannel; multidimensional; multiframe; multimedia; multinational; multipoint
neighbour
non‑existent
non-linear
occur; occurred; occurrence
offset
organization; organize
principal (adj.); principal (head person); principle (noun)
quantization; quantize
separate
signal; signalled; signalling
standardization; standardize

## Slide 24: Spelling – Particular Words
sub-band
subcommittee
subdivision
subgroup
subheading
sub-item
supersede
supervise; supervisor
synchronize
synthesis; synthesize
telecommunication (adj.); telecommunications (noun)
teleconference
videoconference
videotelephony
webpage
website
weekday
weekend
wideband
worldwide

## Slide 25: Formal English Style Guidelines
The ITU English language style guide
    http://www.itu.int/SG-CP/docs/styleguide.doc
ISO/IEC Directives Part 2 “Rules for the structure and drafting of International Standards” (6th Edition, 2011) http://www.itscj.ipsj.or.jp/sc29/29w7d2.zip
ITU-T Rec. A.23 Annex A | ISO/IEC Standing Document 3 “Guide for ITU-T and ISO/IEC JTC 1 Cooperation” http://www.itu.int/rec/T-REC-A.23
UN Editorial manual
http://69.94.137.26/editorialcontrol/
Writing for the United Nations: an online learning programme
http://69.94.137.26/editorialcontrol/training/Index.htm

## Slide 26: General English Style Guidance (encouraged by ITU English language style guide)
EU Clear writing campaign
http://ec.europa.eu/translation/writing/clear_writing/how_to_write_clearly_en.pdf
General guidance
  H.W. FOWLER: A dictionary of modern English usage
  Sir Ernest GOWERS: The complete plain words
  The Economist pocket style book
  E. PARTRIDGE: Usage and abusage