## Slide 1: AhG7: Overflow Prevention in HEVC inverse transform
JCTVC-G782
Elena Alshina Alexander Alshin
JeongHoon Park

## Slide 2: Inverse transform implementation in HM
De facto we have clipping both after 1st and 2nd inverse transforms
DeQuantizer
1st INV
transform
2nd INV
transform
Clip3(-32768,32767, X)
int  short
int  short

## Slide 3: Dynamic range for matrix product
If
  A = B  C (X = Maxij |Cij|)
then
Maxij |Aij| = N * X (***)
Here
N = NormL1(B) = Maxi(j|Bij|)
(Sum along rows; Maximum across all rows)
This is always possible to find C which will realize (***)
sum abs
sum abs
sum abs
sum abs
NormL1 =maximum

## Slide 4: Dynamic range in inverse transform
JVTCV E243 Inverse transform |  |  |  |  |  |  | 
HM | Size | L1Norm | MaxAbs coeff | reg1 bits | temp2 bits | reg2 bits | rec res bits
DST | 4 | 242 | 32767 | 24 | 17 | 25 | 13
DCT | 4 | 247 | 32767 | 24 | 17 | 25 | 13
 | 8 | 479 | 32767 | 25 | 18 | 27 | 15
 | 16 | 940 | 32767 | 26 | 19 | 29 | 17
 | 32 | 1862 | 32767 | 27 | 20 | 31 | 19
Internal Bit-Depth 8

## Slide 5: 4pt example of 16 bits overflow(1/2)
register2
=

=
Clip(coeff, Min, Max)
X | X | X | X
X | X | X | X
X | X | X | X
X | X | X | X
=
Min = -32768
Max = 32767
X = 32767 (within 16 bits!)
X | X | X | X
X | X | X | X
X | X | X | X
X | X | X | X
64 | 83 | 64 | 36
64 | 36 | -64 | -83
64 | -36 | -64 | 83
64 | -83 | 64 | -36
247X | 247X | 247X | 247X
-47X | -47X | -47X | -47X
47X | 47X | 47X | 47X
-119X | -119X | -119X | -119X
temp2
=
register2 /128
=
1.9X | 1.9X | 1.9X | 1.9X
-0.4X | -0.4X | -0.4X | -0.4X
0.4X | 0.4X | 0.4X | 0.4X
-0.9X | -0.9X | -0.9X | -0.9X
63230 | 63230 | 63230 | 63230
-12032 | -12032 | -12032 | -12032
12032 | 12032 | 12032 | 12032
-30463 | -30463 | -30463 | -30463
=
X | X | X | X
X | X | X | X
X | X | X | X
X | X | X | X
X= 32767
Cannot be output of forward 4pt transform,
but can come from “non –confirmed” bit-stream

## Slide 6: 4pt example of 16 bits overflow(2/2)
Register3
=

=
64 | 64 | 64 | 64
84 | 36 | -36 | -83
64 | -64 | -64 | 64
36 | -83 | 83 | -36
Rec_res
=
register3 /256
=
61007 | … | … | …
… | … | … | …
… | … | … | …
… | … | … | …
De-scaling factor ‘256” corresponds “internal bit depth” 12
63230 | 63230 | 63230 | 63230
… | … | … | …
… | … | … | …
… | … | … | …
15617810 | … | … | …
… | … | … | …
… | … | … | …
… | … | … | …
=

## Slide 7: Hypothetical implementation
Overflow after 2nd transform may be resolved by implementation
DeQuantizer
1st INV
transform
2nd INV
Transform
+ prediction
Clip3(0,255)
?
?
No need to clip

## Slide 8: Proposed design (1)
Need to put to the specification:
Clip to Min1…Max1 range after de-Quantization
Clip to Min2…Max2 range after 1st INV transform
No clipping or “intshort” conversion
DeQuantizer
1st INV
transform
2nd INV
transform
Clip3(Min1,Max1, X)
No CLIP!!!
or “intshort”
conversion
Clip3(Min2,Max2, X)

## Slide 9: Proposed design (2)
Need to put to the specification:
Clip to Min1…Max1 range after de-Quantization*
Clip to Min2…Max2 range after 1st INV transform
Add residual and clip to original signal range before output of 2nd transform
(*)Preferable to move clipping from De-Quantizer to earlier stage (JCTVC-G719)
DeQuantizer
1st INV
transform
Clip3(Min1,Max1, X)
Clip3(Min2,Max2, X)
2nd INV
Transform
+ prediction
Clip3(0,255)

## Slide 10: Min1, Max1? Min2, Max2?
JVTCV E243 Inverse transform |  |  |  |  |  | internal bit-depth |  | 10
 | Size | L1Norm | ¦coeff¦<=Max1 | reg2 bits | ¦temp2¦ <=Max2 | temp2 bits | reg3 bits | rec res bits
DST | 4 | 242 | 32767 | 24 | 32767 | 16 | 24 | 14
DCT | 4 | 247 | 32767 | 24 | 32767 | 16 | 24 | 14
 | 8 | 479 | 32767 | 25 | 32767 | 16 | 25 | 15
 | 16 | 940 | 32767 | 26 | 32767 | 16 | 26 | 16
 | 32 | 1862 | 32767 | 27 | 32767 | 16 | 27 | 17
Min1=-32767; Max1= 32767
Min2=-32767; Max2= 32767
Min1=Min2 = -32768 (if it is preferable somehow)

## Slide 11: Min1, Max1? Min2, Max2?
Min1=-32767; Max1= 32767
Min2=-32767; Max2= 32767
Min1=Min2 = -32768 (if it is preferable somehow)
JVTCV F251 Inverse transform |  |  |  |  | internal bit-depth |  |  | 8
 | Size | L1Norm | coeff | reg2 bits | temp2 | temp2 bits | reg3 bits | rec res bits
DST | 4 | 15488 | 32767 | 30 | 32767 | 16 | 30 | 12
DCT | 4 | 15808 | 32767 | 30 | 32767 | 16 | 30 | 12
 | 8 | 30622 | 32767 | 31 | 32767 | 16 | 31 | 13
 | 16 | 60326 | 32767 | 32 | 32767 | 16 | 32 | 14
 | 32 | 119262 | 18006 | 32 | 18006 | 16 | 32 | 15
Size < 32
Min1=Min2 = -18006
Min1=Max2 = 18006
Size = 32

## Slide 12: Conclusions:
We would like to suggest following inverse transform framework for HEVC:
  Restrict dynamic range of de-quantized coefficients (preferably move restriction prior de-quantizer JCTVC-G719)
  Restrict dynamic range of the out-put of 1st inverse transform
  Add residual and clip to out-put signal range before output of 2nd transform