## Slide 1: JCTVC-G812: Intra Padding Simplification
X. Wang, W.-J. Chien, M.Karczewicz

## Slide 2: Current Padding Process in HM4.0
If both Ppre and Pnext are available
  Ppad = (Ppre + Pnext) / 2
If only Pnext is available (i.e. Pcur is the first pixel starting from A)
  Ppad = Pnext
If only Ppre is available (i.e. no border pixel available from Pcur to the end point of B)
  Ppad = Ppre
Problem
  A two pass process is needed

## Slide 3: Scheme A: Copying Previous Pixel
Start from A. If A is not available, set Ppad equal to Pnext, as in HM4.0
Padding is performed by copying its previous pixel. No “look ahead” search is needed.

## Slide 4: Scheme B: Pick a Start Point
Identify a start point from PL and PA. If neither is available, start from PA and set its value to (1 << ( BitDepthY ‑1))
Padding from the start point towards both A and B.
Padding is performed by copying its previous pixel.
Current block
w
h
A
B
P
A
P
L

## Slide 5: Simulation Results (Cont.)
 | Proposed Scheme A |  |  |  | 
 | Y | U | V | Encoding | Decoding
AI_HE | 0.00% | 0.00% | 0.00% | 100% | 100%
RA_HE | 0.01% | 0.05% | 0.02% | 99% | 98%
LB_HE | 0.02% | -0.10% | 0.15% | 99% | 98%
AI_LC | 0.00% | 0.01% | 0.00% | 100% | 99%
RA_LC | 0.00% | 0.00% | 0.03% | 98% | 98%
LB_LC | 0.02% | 0.30% | 0.01% | 98% | 98%
Based on common test conditions, with 1500bytes/slice, constrained intra prediction enabled

## Slide 6: Simulation Results
 | Proposed Scheme B |  |  |  | 
 | Y | U | V | Encoding | Decoding
AI_HE | 0.00% | 0.00% | 0.00% | 100% | 100%
RA_HE | 0.04% | 0.06% | 0.01% | 99% | 97%
LB_HE | 0.01% | -0.09% | 0.16% | 100% | 97%
AI_LC | 0.01% | 0.01% | 0.00% | 101% | 99%
RA_LC | 0.06% | 0.09% | 0.11% | 99% | 98%
LB_LC | 0.01% | 0.16% | -0.06% | 99% | 98%
Based on common test conditions, with 1500bytes/slice, constrained intra prediction enabled

## Slide 7: Conclusions
With proposed padding schemes, search for a next available pixel is completely removed or significantly reduced
Memory access is improved compared with the current one in HM4.0
Very little impact on coding performance
Recommend to adopt one of the proposed schemes into HM