## Slide 1: Non-CE1: 8-bit Initialization for CABAC (JCTVC-G837)
Liwei Guo, Rajan Joshi, Joel Sole, Xianglin Wang, Marta Karczewicz
Nov. 2011

## Slide 2: Introduction
CABAC contexts initialization in HM
iInitState = Clip(1,126, (m*QP>>4) + n)
  m: “short-int” type slope parameter
  n: “short-int” type intersection parameter
  Current values of m/n can be stored using 8-bits (with an offset)
    At least,16 bits storage for each context
Proposed 8-bit CABAC initialization
  An 8-bit InitIdx is stored for each context
  InitIdx is converted to m and n based on SlopeTable and IntersecTable
  Two sets of tables are provided
    Table look-up operations can be replaced by simple computations and thus storage of tables is not necessary

## Slide 3: InitIdx
8-bit InitIdx consists of two parts
  4-bit SlopeIdx
  4-bit IntersecIdx
Converting InitIdx to m and n
  16-element tables SlopeTable and IntersecTable
    m = SlopeTable[SlopeIdx]
    n = IntersecTable[IntersecIdx]
iInitState = Clip(1,126, (m*QP>>4) + n)

## Slide 4: First set of tables
Tables
  SlopeTable[16] = { -44, -39, -33, -28, -22, -17, -11, -5,
  0, 6, 11, 17, 22, 28, 33, 39}
  IntersecTable[16] = {-13, -5, 3, 11, 19, 27, 35, 43,
51, 59, 67, 75, 83, 91, 99, 107}
Tables can be replaced by computing
  m = ( SlopeIdx * 89 – 703 ) >> 4
  n = ( IntersecIdx << 3 ) – 13
  Value m can be pre-calculated for every SlopeIdx at the beginning of the encoding process

## Slide 5: Second set of tables
Tables
  SlopeTable[16] = { -32, -28, -24, -20, -16, -12, -8, -4
  0, 4, 8, 12, 16, 20, 24, 28}
  IntersecTable[16] = {-13, -5, 3, 11, 19, 27, 35, 43,
51, 59, 67, 75, 83, 91, 99, 107}
    IntersecTable [] is the same as the one in the first set
Table can be replaced by a multiplication-free calculation
  m = ( SlopeIdx << 2 ) – 32
  n = ( IntersecIdx << 3 ) – 13

## Slide 6: Simulation (1): first set of tables
 | All Intra HE |  |  | Random Access HE |  |  | Low delay B HE |  |  | Low delay P HE |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Class A | 0.0% | 0.0% | 0.0% | -0.2% | 0.1% | 0.0% |  |  |  |  |  | 
Class B | 0.0% | 0.0% | 0.0% | -0.2% | 0.1% | 0.1% | -0.2% | 0.4% | -0.2% | -0.2% | 0.5% | 0.3%
Class C | 0.0% | -0.1% | -0.4% | -0.3% | 0.0% | -0.2% | -0.4% | 0.3% | -0.1% | -0.3% | 0.3% | 0.3%
Class D | 0.0% | -0.6% | -1.1% | -0.5% | -0.1% | -0.9% | -0.7% | 0.4% | -0.7% | -0.4% | 1.3% | 0.7%
Class E | -0.1% | -0.3% | -0.1% |  |  |  | -1.0% | -0.8% | 0.8% | -0.7% | -0.8% | 0.0%
Class F |  |  |  |  |  |  |  |  |  |  |  | 
Overall | 0.0% | -0.2% | -0.3% | -0.3% | 0.0% | -0.2% | -0.5% | 0.2% | -0.1% | -0.3% | 0.4% | 0.3%
 | 0.0% | -0.2% | -0.3% | -0.3% | 0.0% | -0.2% | -0.5% | 0.1% | -0.1% | -0.3% | 0.3% | 0.3%
Enc Time[%] | 99% |  |  | 100% |  |  | 99% |  |  | 97% |  | 
Dec Time[%] | 99% |  |  | 99% |  |  | 101% |  |  | 101% |  | 
Common test condition in JCTVC F900, anchor is HM4.0
Encoding performed on cluster with same CPU
Decoding was performed on a single PC
Thanks to Samsung (JCTVC-G913) for the cross-checking

## Slide 7: Simulation (2): second set of tables
 | All Intra HE |  |  | Random Access HE |  |  | Low delay B HE |  |  | Low delay P HE |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Class A | 0.0% | 0.0% | 0.0% | -0.1% | -0.1% | -0.4% |  |  |  |  |  | 
Class B | 0.0% | 0.0% | 0.0% | -0.2% | 0.2% | 0.1% | -0.2% | 0.3% | -0.3% | -0.2% | 0.2% | 0.1%
Class C | 0.0% | -0.2% | -0.4% | -0.3% | 0.0% | 0.0% | -0.3% | 0.3% | -0.1% | -0.2% | 0.3% | 0.1%
Class D | 0.0% | -0.9% | -1.1% | -0.4% | -0.3% | -0.5% | -0.7% | 0.3% | 0.2% | -0.5% | 0.9% | 0.3%
Class E | -0.1% | -0.3% | -0.1% |  |  |  | -0.8% | 0.1% | 0.8% | -0.6% | 0.0% | 0.5%
Class F |  |  |  |  |  |  |  |  |  |  |  | 
Overall | 0.0% | -0.3% | -0.3% | -0.2% | 0.0% | -0.2% | -0.4% | 0.3% | 0.1% | -0.3% | 0.4% | 0.2%
 | 0.0% | -0.3% | -0.3% | -0.2% | -0.1% | -0.2% | -0.4% | 0.2% | 0.1% | -0.3% | 0.3% | 0.2%
Enc Time[%] | 100% |  |  | 101% |  |  | 99% |  |  | 97% |  | 
Dec Time[%] | 101% |  |  | 94% |  |  | 100% |  |  | 99% |  | 
Common test condition in JCTVC F900, anchor is HM4.0
Encoding performed on cluster with same CPU
Decoding was performed on a single PC
Thanks to Samsung (JCTVC-G913) for the cross-checking

## Slide 8: Conclusions
8-bit InitIdx proposed for CABAC contexts initialization
Storage of initialization parameters reduced by at least 50%
Values can be obtained by means of tables or simple computations
Coding efficiency improvement observed with provided initIdx values
Recommend adoption of proposed 8-bit CABAC initialization

## Slide 9
Thank you!