## Slide 1: Coding and selection of SAO parameters (JCTVC-G915)
David Baylon and Koohyar Minoo
Motorola Mobility
11/23/11

## Slide 2
Encoder offset optimization
Increase in number of EO classes
Change in coding of BO type (HE case)
1/23/2011
© 2010 Motorola Mobility, Inc.
Proposed SAO Improvements

## Slide 3
HM4.0: offset computed based on distortion minimization only
Proposed: offset based on both distortion and bits (cost-minimization-based)
 RD selection of offset
1/23/2011
© 2010 Motorola Mobility, Inc.
Encoder offset optimization

## Slide 4
HM4.0: EO classes (excluding default)
HM4.0: EO type Index = sign(forward_jump) + sign(backward_jump)+2
Proposed: EO classes (excluding default)
 More classes (offsets) per EO type
Proposed: EO type Index = 3*sign(forward_jump) + sign(backward_jump)+4
1/23/2011
© 2011Motorola Mobility, Inc.
Increase in number of EO classes
1
2
3
4
1
2
3
4
5
6
7
8

## Slide 5
HM4.0 (HE): longer BO codeword in binarization
Proposed: shorter BO codeword in binarization
 less RD bias against BO types
  Justification: With recommended encoder optimization, BO classes are selected more
1/23/2011
© 2010 Motorola Mobility, Inc.
Change in coding of EO type (HE case)

## Slide 6
1/23/2011
© 2010 Motorola Mobility, Inc.
Simulation results
 | Intra HE |  |  | Intra LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.0% | -0.9% | -0.8% | 0.0% | -0.7% | -0.8%
Class B | 0.1% | -0.8% | -1.5% | 0.1% | -0.8% | -1.4%
Class C | 0.0% | -0.5% | -0.6% | 0.0% | -0.3% | -0.4%
Class D | 0.0% | -0.5% | -0.5% | 0.0% | -0.4% | -0.4%
Class E | 0.0% | -1.5% | -1.2% | 0.0% | -1.5% | -1.4%
Overall | 0.0% | -0.8% | -1.0% | 0.0% | -0.7% | -0.9%
 | 0.0% | -0.8% | -1.0% | 0.0% | -0.7% | -0.9%

## Slide 7
1/23/2011
© 2010 Motorola Mobility, Inc.
Simulation results
 | Random Access HE |  |  | Random Access LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.1% | -1.8% | -1.6% | 0.0% | -0.7% | -0.9%
Class B | -0.1% | -1.0% | -1.8% | 0.0% | -0.9% | -1.3%
Class C | 0.0% | -0.5% | -0.5% | 0.0% | -0.3% | -0.2%
Class D | 0.0% | -0.5% | -0.4% | 0.0% | -0.6% | -0.6%
Class E |  |  |  |  |  | 
Overall | 0.0% | -1.0% | -1.1% | 0.0% | -0.6% | -0.8%
 | 0.0% | -0.9% | -1.1% | 0.0% | -0.6% | -0.8%

## Slide 8
1/23/2011
© 2010 Motorola Mobility, Inc.
Simulation results
 | Low Delay B HE |  |  | Low Delay B LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | -0.1% | -1.2% | -1.7% | -0.1% | -1.5% | -1.7%
Class C | 0.0% | -0.4% | -0.7% | 0.0% | -0.5% | -0.7%
Class D | 0.0% | 0.1% | -0.1% | 0.0% | -0.1% | -0.6%
Class E | 0.0% | -2.6% | 0.0% | -0.1% | -1.3% | -1.4%
Overall | 0.0% | -1.0% | -0.7% | 0.0% | -0.9% | -1.1%
 | 0.0% | -1.0% | -0.8% | 0.0% | -0.9% | -1.1%

## Slide 9
1/23/2011
© 2010 Motorola Mobility, Inc.
Simulation results
 | Low Delay P HE |  |  | Low Delay P LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | 0.0% | -0.9% | -1.5% | 0.1% | -0.6% | -1.1%
Class C | 0.0% | -0.2% | -0.5% | 0.0% | -0.3% | -0.4%
Class D | 0.0% | -0.1% | -0.5% | 0.0% | 0.1% | -0.1%
Class E | 0.0% | -1.7% | 0.1% | 0.1% | -1.2% | 0.1%
Overall | 0.0% | -0.7% | -0.7% | 0.1% | -0.5% | -0.5%
 | 0.0% | -0.7% | -0.7% | 0.1% | -0.5% | -0.5%

## Slide 10
Adopting the non-normative part for encoder side optimization in the next HM (only a few lines of code)
Combination of changes reportedly provides savings of up to 1.1% for chroma without any loss in luma
  Consideration of adding 5 classes to EO types which are derived based on the same calculations but different mapping (With few lines of code change this can be supported)
  Further study of proposed Classification Type coding within CE
1/23/2011
© 2010 Motorola Mobility, Inc.
Summary

## Slide 11
1/23/2011
© 2010 Motorola Mobility, Inc.
Thank You