## Slide 1
JCTVC-G958
Non-CE11: Modified context selection for Significant Coefficient Flags with Diagonal sub-block scan
7th JCT-VC meeting, Nov 2011.

## Slide 2: G323 introduces unified sub-block scan pattern
Good for implementation, sub-blocks can be 4x4, 8x8 or 16x16 (we look at 4x4 case)
An 8x8 TU with 4x4 sub-blocks shown on right:
In HM-4.0, for 16x16 and 32x32 TUs, ctx for each significant coefficient flag calculated as below:
    Note: Xctx clipped at 4 in HM-4.0, G323 and G958 (note added to _r2 of contribution)

## Slide 3: Significance map throughput issue
Throughput issue when a previous significant coefficient flag is used to determine the context for a current significant coefficient flag.
  Can’t determine context until you decode the previous significant coefficient flag.
G323 excludes the previous significant coefficient flag in the following locations in each sub-block:

## Slide 4: Harmonise context selection
We propose to:
  Exclude the previous significant coefficient flag in same locations as G323.
  Estimate the excluded significant coefficient flag using nearby significant coefficient flags:
Small gain relative to G323
Minimal complexity impact

## Slide 5: Results relative to HM-4.0
 | All Intra HE |  | 
 | Y | U | V
Class A | -0.1% | -0.3% | -0.1%
Class B | 0.0% | 0.0% | 0.0%
Class C | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.0% | -0.1%
Class E | -0.1% | -0.2% | -0.2%
Class F | 0.0% | 0.0% | 0.0%
Overall (A-F) | 0.0% | -0.1% | -0.1%
 | 0.0% | -0.1% | -0.1%
Overall (A-E) | 0.0% | -0.1% | -0.1%
 | 0.0% | -0.1% | -0.1%
Enc Time[%] | 99% |  | 
Dec Time[%] | 100% |  | 
 | Random Access HE |  | 
 | Y | U | V
Class A | 0.1% | 0.3% | 0.5%
Class B | 0.0% | 0.0% | 0.1%
Class C | 0.0% | -0.1% | 0.1%
Class D | 0.0% | 0.0% | -0.3%
Class E |  |  | 
Class F | 0.0% | 0.1% | -0.2%
Overall (A-F) | 0.0% | 0.0% | 0.0%
 | 0.0% | 0.0% | 0.0%
Overall (A-E) | 0.0% | 0.0% | 0.1%
 | 0.0% | 0.0% | 0.1%
Enc Time[%] | 99% |  | 
Dec Time[%] | 99% |  | 
 | Low delay B HE |  | 
 | Y | U | V
Class A |  |  | 
Class B | 0.1% | -0.1% | -0.1%
Class C | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.1% | -0.3%
Class E | 0.1% | 0.0% | 0.4%
Class F | -0.2% | -0.5% | 0.1%
Overall (A-F) | 0.0% | -0.1% | 0.0%
 | 0.0% | -0.1% | 0.0%
Overall (A-E) | 0.0% | 0.0% | 0.0%
 | 0.0% | 0.0% | -0.1%
Enc Time[%] | 100% |  | 
Dec Time[%] | 101% |  | 
 | Low delay P HE |  | 
 | Y | U | V
Class A |  |  | 
Class B | 0.1% | 0.0% | -0.1%
Class C | 0.0% | 0.2% | 0.0%
Class D | 0.0% | -0.4% | -0.6%
Class E | 0.0% | -0.2% | -0.2%
Class F | 0.0% | 0.0% | -0.3%
Overall (A-F) | 0.0% | -0.1% | -0.2%
 | 0.0% | 0.0% | -0.3%
Overall (A-E) | 0.0% | -0.1% | -0.2%
 | 0.0% | 0.0% | -0.3%
Enc Time[%] | 100% |  | 
Dec Time[%] | 101% |  | 

## Slide 6: Results relative to G323 with 4x4 sub-block and parallel-friendly implementation
 | All Intra HE |  | 
 | Y | U | V
Class A | -0.06% | -0.07% | -0.10%
Class B | -0.05% | -0.09% | -0.08%
Class C | -0.03% | -0.01% | -0.03%
Class D | -0.01% | -0.06% | -0.09%
Class E | -0.06% | -0.07% | -0.11%
Class F | -0.02% | -0.01% | -0.09%
Overall (A-F) | -0.04% | -0.05% | -0.08%
 | -0.04% | -0.06% | -0.09%
Overall (A-E) | -0.04% | -0.06% | -0.08%
 | -0.04% | -0.07% | -0.09%
Enc Time[%] | 99% |  | 
Dec Time[%] | 100% |  | 
 | Random Access HE |  | 
 | Y | U | V
Class A | -0.03% | 0.16% | 0.42%
Class B | -0.03% | -0.03% | -0.05%
Class C | -0.03% | -0.09% | 0.11%
Class D | -0.06% | 0.05% | -0.18%
Class E |  |  | 
Class F | 0.03% | 0.00% | -0.02%
Overall (A-F) | -0.02% | 0.02% | 0.05%
 | -0.02% | 0.00% | 0.03%
Overall (A-E) | -0.04% | 0.02% | 0.07%
 | -0.04% | 0.01% | 0.03%
Enc Time[%] | 99% |  | 
Dec Time[%] | 100% |  | 
 | Low delay B HE |  | 
 | Y | U | V
Class A |  |  | 
Class B | 0.00% | -0.16% | 0.21%
Class C | -0.05% | -0.15% | 0.03%
Class D | 0.02% | 0.48% | -0.08%
Class E | -0.06% | 0.10% | -0.22%
Class F | -0.15% | -0.38% | 0.22%
Overall (A-F) | -0.04% | -0.04% | 0.05%
 | -0.04% | -0.03% | 0.05%
Overall (A-E) | -0.02% | 0.05% | 0.01%
 | -0.02% | 0.06% | 0.00%
Enc Time[%] | 101% |  | 
Dec Time[%] | 102% |  | 
 | Low delay P HE |  | 
 | Y | U | V
Class A |  |  | 
Class B | -0.01% | -0.15% | 0.02%
Class C | 0.02% | 0.28% | -0.03%
Class D | -0.01% | -0.58% | -0.36%
Class E | -0.05% | -0.17% | -0.44%
Class F | -0.01% | -0.04% | -0.22%
Overall (A-F) | -0.01% | -0.13% | -0.18%
 | -0.01% | -0.08% | -0.19%
Overall (A-E) | -0.01% | -0.15% | -0.17%
 | -0.01% | -0.12% | -0.20%
Enc Time[%] | 101% |  | 
Dec Time[%] | 101% |  |