## Slide 1: Context Simplification on coeff_abs_level_greater1_flag
JCTVC-H0062
Wenpeng Ding, Yunhui shi and Baocai Yin
Beijing University of Technology

## Slide 2: Summary
The number of Context for coeff_abs_level_greater1_flag is reduced from 32 to 24
BDRate increase 0.03 for Intra, -0.02 for Random access and -0.09 for Low delay .(Normal QP)
0.01 for Intra, 0.00 for Random access and -0.02 for Low delay(Low QP)
Same runtime complexity as that of HM5.0

## Slide 3: Proposed scheme
we propose to select the context as follows
ctxIdxInc = ( ctxSet * 3) + (Min( 3, greater1Ctx )+1)>>1
Similar scheme as jctvc-g121
HM4 | 0 | 1 | 2 | 3 | 4
HM5-G121 | 0 | 1 | 2 | 3 | 3
Proposed | 0 | 1 | 1 | 2 | 2
Notes: <number>

## Slide 4: Working draft modification
Derivation process of ctxIdxInc for the syntax element coeff_abs_level_greater1_flag
ctxIdxInc = ( ctxSet * 3) + (Min( 3, greater1Ctx )+1)>>1

## Slide 5: Results
 | All Intra HE |  |  | All Intra LC |  |  | All Intra HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A (8bit) | 0.05% | 0.02% | 0.03% | 0.11% | 0.06% | 0.05% |  |  | 
Class B | 0.03% | -0.01% | 0.01% | 0.07% | 0.06% | 0.06% |  |  | 
Class C | 0.02% | -0.01% | 0.01% | 0.06% | 0.04% | 0.02% |  |  | 
Class D | 0.01% | 0.04% | 0.03% | 0.05% | 0.03% | 0.02% |  |  | 
Class E | 0.07% | 0.00% | 0.07% | 0.11% | 0.09% | 0.08% |  |  | 
Overall | 0.03% | 0.01% | 0.03% | 0.07% | 0.05% | 0.05% |  |  | 
 | 0.03% | 0.00% | 0.03% | 0.07% | 0.05% | 0.04% |  |  | 
Class F | 0.00% | -0.05% | 0.04% | 0.03% | 0.28% | 0.02% |  |  | 
Enc Time[%] | 101% |  |  | 100% |  |  |  |  | 
Dec Time[%] | 101% |  |  | 101% |  |  |  |  | 
 | Random Access HE |  |  | Random Access LC |  |  | Random Access HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A (8bit) | -0.01% | 0.02% | -0.25% | 0.08% | 0.15% | -0.11% | -0.01% | 0.04% | 0.24%
Class B | -0.02% | -0.11% | -0.01% | 0.07% | 0.17% | 0.16% | 0.01% | -0.07% | 0.00%
Class C | -0.06% | -0.11% | 0.03% | 0.08% | 0.05% | -0.08% |  |  | 
Class D | 0.03% | -0.26% | 0.02% | 0.00% | 0.36% | -0.04% |  |  | 
Class E |  |  |  |  |  |  |  |  | 
Overall | -0.02% | -0.13% | -0.02% | 0.05% | 0.19% | 0.01% | 0.00% | -0.02% | 0.10%
 | -0.01% | -0.17% | -0.02% | 0.05% | 0.16% | -0.02% | 0.00% | -0.03% | 0.12%
Class F | -0.05% | -0.05% | -0.14% | 0.05% | -0.04% | 0.06% |  |  | 
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 101% |  |  | 101% |  |  | 100% |  | 
 | Low delay B HE |  |  | Low delay B LC |  |  | Low delay B HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A |  |  |  |  |  |  |  |  | 
Class B | -0.11% | -0.14% | 0.12% | 0.01% | -0.15% | 0.07% |  |  | 
Class C | -0.11% | -0.26% | -0.09% | 0.02% | 0.19% | 0.04% |  |  | 
Class D | -0.06% | -0.31% | -0.33% | 0.01% | 0.50% | -0.43% |  |  | 
Class E | -0.06% | 1.51% | -0.45% | -0.09% | -1.01% | -0.11% |  |  | 
Overall | -0.09% | 0.10% | -0.15% | -0.01% | -0.06% | -0.10% |  |  | 
 | -0.09% | 0.11% | -0.20% | -0.01% | -0.08% | -0.09% |  |  | 
Class F | -0.17% | -0.16% | -0.79% | 0.09% | -0.69% | -0.23% |  |  | 
Enc Time[%] | 100% |  |  | 100% |  |  |  |  | 
Dec Time[%] | 100% |  |  | 101% |  |  |  |  | 

## Slide 6: Results
 | All Intra HE |  | 
 | Y | U | V
Class A (8bit) | 0.03% | 0.01% | 0.01%
Class B | 0.01% | -0.01% | 0.02%
Class C | 0.00% | 0.00% | 0.02%
Class D | 0.00% | 0.01% | -0.01%
Class E | 0.03% | 0.01% | 0.05%
Overall | 0.01% | 0.00% | 0.02%
 | 0.01% | 0.00% | 0.02%
Class F | -0.01% | -0.01% | -0.03%
Enc Time[%] | 101% |  | 
Dec Time[%] | 102% |  | 
 | Random Access HE |  | 
 | Y | U | V
Class A (8bit) | 0.03% | 0.01% | -0.07%
Class B | 0.02% | -0.05% | 0.05%
Class C | -0.01% | -0.06% | -0.08%
Class D | -0.01% | -0.10% | 0.00%
Class E |  |  | 
Overall | 0.00% | -0.06% | -0.01%
 | 0.01% | -0.06% | -0.01%
Class F | -0.06% | -0.04% | -0.05%
Enc Time[%] | 100% |  | 
Dec Time[%] | 98% |  | 
 | Low delay B HE |  | 
 | Y | U | V
Class A |  |  | 
Class B | 0.01% | -0.01% | -0.04%
Class C | -0.03% | -0.08% | 0.01%
Class D | -0.02% | -0.08% | -0.04%
Class E | -0.04% | 0.18% | -0.28%
Overall | -0.02% | -0.01% | -0.07%
 | -0.01% | 0.00% | -0.09%
Class F | -0.05% | -0.19% | -0.20%
Enc Time[%] | 100% |  | 
Dec Time[%] | 99% |  | 

## Slide 7: Cross-checking Results
Thanks Huawei for cross-checking our results.

## Slide 8: Conclusion
coeff_abs_level_greater1_flag is reduced from 32 to 24
Same coding performance compared with HM5.0
Same runtime complexity as HM5.0.
Recommend to adopt.