## Slide 1: JCTVC-H0069 APS Update
Li Ming and Ping Wu, ZTE Stephan Wenger and Jill Boyce, Vidyo
David Flynn, BBC

## Slide 2: Design Principles
Design is a merger of
  Parameter set referencing (earlier version of H0069)
  Conditional Replacement (E309 and H0070)
  “Invalidation” trick, allowing to “undefine” an APS
Parameter set referencing allows update of parts of an APS while retaining previous information
Conditional replacement allows update of parts of an APS, without retaining information, and without adding references to linked list
Together, the two allow flexible updating while the depth of the linked list can be kept low.
“Invalidation” helps if “undefined” values of an APS carry a semantic (such as currently in the scaling_list)

## Slide 3: In the draft… NOTE: this is specification space, not implementation space.
Concept: class of parameters (COP): block of parameters gated by a flag indicating their presence: alf_param_present_flag and alf_params()
Conditional replacement: when COP data is present in an APS RBSP, it overwrites the corresponding COP data previously present.
We are no more activating one or more APS RBSPs. We are activating a logical data structure called activeAPS.
activeAPS is constructed using a recursive process for the linked-list walk
When aps_ref_flag && aps_id = = aps_ref_idx then invalidate (discard previous knowledge) of APS referenced by aps_id.

## Slide 4: Recursion NOTE: this is specification space, not implementation space.
coalesceAPS(apsId, recursionLimit) {
if( recursionLimit > 0 && APS[ apsId ].aps_ref_flag )
coalesceAPS( APS[ apsId ].aps_ref_id, recursionLimit – 1 );
mergeAPS( activeAPS, APS[ apsId ] )
}
Where:
  activeAPS is the active adaptation parameter set being constructed; and,
  mergeAPS( a, b ) is a function that combines the contents of APS a and APS b, such that the contents of APS b overwrites that of APS a for those classes of parameters marked by data presence flags in APS b.

## Slide 5: Activation NOTE: this is specification space, not implementation space.
Each adaptation parameter set may be updated using a partial update procedure specified in XXX, forming the array APS[apsId].
A construction process is performed at the start of each coded picture to populate the active adaptation parameter set from a list of adaptation parameter set structures that have been previously received.
The resulting active adaptation parameter set is only considered active for a single coded picture.
Depending on our decision in this regard, activation could also be slice-based.

## Slide 14: Outlook
Parameter set activation language can likely be simplified by using the coalesce mechanism for all parameter sets
activePS would be put together using all PPS, SPS, and APS data. Update mechanism could be enabled for all PPS SPS, and APS if so desired.
Further study