## Slide 1: AHG7: Controllable memory bandwidth reduction with bi-pred to uni-pred conversion (JCTVC-H0096)
JCT-VC 8th Meeting: San José, CA, USA, 1–10 February, 2012
Tomohiro Ikai
SHARP Corporation

## Slide 2: Overall summary
Controllable memory bandwidth reduction
  HM5
    inter_4x4_enable_flag is nothing if SCU size = 16.
    Bi-prediction cannot be restricted explicitly
  Proposal
    Replace inter_4x4_enable_flag with inter_predction_restriction_flag
      Disable 4x4 PU and 4x8/8x4 bi-pred (SCUSize = 8, inter_prediction_restriction_flag = 1)
      Disable 4x4, 8x4, 4x8 PU (SCUSize = 16, inter_prediction_restriction_flag = 0)
      Disable 4x4, 8x4, 4x8 PU and 8x8 bi-pred (SCUSize = 16, inter_prediction_restriction_flag = 1)
Bi-pred to uni-pred conversion in merge mode
  Convert bi-prediction to uni-prediction when the derived merge mode is bi-prediction and the bi-prediction is restricted.
Results
<number>
 |  | RA-HE | LB-HE | RA-LC | LB-LC | RA-HE10
4x8, 8x4 bi-pred and 4x4 PU restriction (8x8 SCU size) | proposal | 0.1 % | 0.1 % | 0.2 % | 0.3 % | 0.1 %
 | encoder only | 0.4 % | 0.5 % | 0.5 % | 0.8 % | 0.2 %
8x8 bi-pred restriction and less than 8x8 PU restriction (16x16 SCU emulation) | proposal | 1.8 % | 2.0 % | 3.0 % | 3.7 % | 0.9 %
 | encoder only | 2.2 % | 2.7 % | 3.5 % | 4.6 % | 1.2 %

## Slide 3: Motivation
inter_4x4_enable_flag is nothing if SCU size is not 8x8.
  We’d like to change Inter_4x4_enable_flag to more productive one.
Practical encoder restricts bi-prediction to reduce bandwidth reduction and other complexity.
  Over HD, 4x8 and 8x4 bi-pred restriction is required. 8x8 bi-pred restriction is also used.
  Besides, practical encoders might always not use 4x8, 8x4 bi-pred for small sequences too.
  HM’s merge mode has a problem if bi-pred is restricted.
<number>
When the derived merge mode candidate is bi-pred, the candidate cannot be selected in bi-pred restriction case

## Slide 4: Controllable PU size and Bi-pred restriction
<number>
uni-pred / bipred
HM5.0
(if inter_4x4_enable_flag = 0)
Proposal
uni-pred
(if inter_prediction_restriction_flag = 1)
bi-pred
SCU = 8x8
uni-pred
(if inter_prediction_restriction_flag = 1)
bi-pred
SCU = 16x16
8x8
8x4
4x8
4x4
16x16
16x8
8x16
8x8
8x8
8x4
4x8
4x4

## Slide 5: inter_prediction_restriction_flag
Restrict both PU size and bi-pred PU size
  depend on SCU size (MinCUSize)
  Bipred is restricted when the NoBipredFlag is false
inter_pred_flag is not present in the syntax if NoBipredFlag is true
The flag is renamed from inter_4x4_enable_flag is SPS
<number>
NoBipredFlag = inter_prediction_restriction_flag is true && ((log2MinCUSize == 3 && log2CUSize == 3 && PartMode != PART_2Nx2N) || (log2MinCUSize > 3 && log2CUSize == log2MinCUSize && PartMode == PART_NxN))

## Slide 6: Bi-pred to uni-pred conversion in merge mode
Bi-pred to uni-pred conversion
The conversion is used after each merge mode candidate derivation
<number>
  If both predFlagL0[ xN, yN ] and predFlagL1[ xN, yN ] is 1, predFlagL0[ xN, yN ] is set to 0 and refIdxL0 is set to -1
predFlagL0[ xN, yN ] = 1
refIdxL0 = x
predFlagL1[ xN, yN ] = 1
refIdxL0 = y
predFlagL0[ xN, yN ] = 0
refIdxL0 = -1
predFlagL1[ xN, yN ] = 1
refIdxL0 = y

## Slide 7: Summary of simulation results
 |  | RA-HE | LB-HE | RA-LC | LB-LC | RA-HE10
4x8, 8x4 bi-pred and 4x4 PU restriction (8x8 SCU size) | proposal | 0.1 % | 0.1 % | 0.2 % | 0.3 % | 0.1 %
 | encoder only | 0.4 % | 0.5 % | 0.5 % | 0.8 % | 0.2 %
8x8 bi-pred restriction and less than 8x8 PU restriction (16x16 SCU emulation) | proposal | 1.8 % | 2.0 % | 3.0 % | 3.7 % | 0.9 %
 | encoder only | 2.2 % | 2.7 % | 3.5 % | 4.6 % | 1.2 %
<number>
 |  | RA-HE | LB-HE | RA-LC | LB-LC | RA-HE10
8x8 bi-pred restriction and less than 8x8 PU restriction (16x16 SCU emulation) | proposal | 1.1 % / 1.0 % | / 1.0 % | 2.0%/ 1.7 % | / 2.1 % | 0.6 % / 1.0 %
 | encoder only | 1.8 % / 1.4 % | / 1.7 % | 2.9%/ 2.1 % | / 2.9 % | 0.9 % / 1.4 %
Table 1 Summary of the results.
Table 2 Summary of the results of Class A / B

## Slide 8: 4x8 and 8x4 bi-prediction restriction (proposed)
 | Random Access HE |  |  | Random Access LC |  |  | Random Access HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A (8bit) | 0.0% | 0.0% | -0.1% | 0.1% | 0.2% | 0.1% | 0.0% | 0.1% | 0.1%
Class B | 0.1% | 0.0% | 0.0% | 0.2% | 0.2% | 0.1% | 0.1% | 0.1% | 0.1%
Class C | 0.1% | 0.2% | 0.3% | 0.3% | 0.3% | 0.3% |  |  | 
Class D | 0.3% | 0.2% | 0.2% | 0.3% | 0.1% | 0.1% |  |  | 
Class E |  |  |  |  |  |  |  |  | 
Overall | 0.1% | 0.1% | 0.1% | 0.2% | 0.2% | 0.2% | 0.1% | 0.1% | 0.1%
 | 0.1% | 0.1% | 0.1% | 0.2% | 0.2% | 0.2% | 0.1% | 0.1% | 0.1%
Class F | -0.3% | -0.1% | -0.2% | -0.2% | -0.1% | -0.2% | 0.0% | 0.1% | 0.1%
Enc Time[%] | 94% |  |  | 91% |  |  | 94% |  | 
Dec Time[%] | 99% |  |  | 99% |  |  | 100% |  | 
 | Low delay B HE |  |  | Low delay B LC |  |  | Low delay B HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A |  |  |  |  |  |  |  |  | 
Class B | 0.1% | 0.1% | 0.3% | 0.2% | 0.0% | 0.0% |  |  | 
Class C | 0.2% | 0.2% | 0.1% | 0.4% | 0.5% | 0.2% |  |  | 
Class D | 0.3% | -0.2% | 0.1% | 0.4% | 1.0% | 0.8% |  |  | 
Class E | 0.0% | -0.2% | -0.3% | 0.3% | -0.1% | 0.2% |  |  | 
Overall | 0.1% | 0.0% | 0.1% | 0.3% | 0.3% | 0.3% |  |  | 
 | 0.1% | 0.0% | 0.0% | 0.3% | 0.3% | 0.3% |  |  | 
Class F | -0.5% | -0.3% | -0.6% | -0.6% | -1.2% | -0.7% |  |  | 
Enc Time[%] | 92% |  |  | 90% |  |  |  |  | 
Dec Time[%] | 100% |  |  | 98% |  |  |  |  | 
<number>

## Slide 9: 4x8 and 8x4 bi-prediction restriction (encoder only)
<number>
 | Random Access HE |  |  | Random Access LC |  |  | Random Access HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A (8bit) | 0.3% | 0.3% | 0.2% | 0.5% | 0.5% | 0.4% | 0.2% | 0.3% | 0.2%
Class B | 0.2% | 0.2% | 0.1% | 0.4% | 0.3% | 0.2% | 0.2% | 0.2% | 0.1%
Class C | 0.4% | 0.5% | 0.4% | 0.6% | 0.6% | 0.5% |  |  | 
Class D | 0.6% | 0.5% | 0.5% | 0.7% | 0.5% | 0.4% |  |  | 
Class E |  |  |  |  |  |  |  |  | 
Overall | 0.4% | 0.4% | 0.3% | 0.5% | 0.4% | 0.4% | 0.2% | 0.2% | 0.2%
 | 0.4% | 0.4% | 0.3% | 0.5% | 0.4% | 0.4% | 0.2% | 0.2% | 0.2%
Class F | -0.2% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] | 93% |  |  | 91% |  |  | 93% |  | 
Dec Time[%] | 99% |  |  | 99% |  |  | 100% |  | 
 | Low delay B HE |  |  | Low delay B LC |  |  | Low delay B HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A |  |  |  |  |  |  |  |  | 
Class B | 0.3% | 0.2% | 0.3% | 0.5% | 0.3% | 0.2% |  |  | 
Class C | 0.6% | 0.4% | 0.4% | 0.9% | 0.8% | 0.9% |  |  | 
Class D | 0.9% | 0.6% | 0.8% | 1.1% | 1.1% | 0.6% |  |  | 
Class E | 0.3% | 0.4% | 0.2% | 0.7% | 0.1% | 0.8% |  |  | 
Overall | 0.5% | 0.4% | 0.4% | 0.8% | 0.6% | 0.6% |  |  | 
 | 0.5% | 0.4% | 0.4% | 0.8% | 0.6% | 0.6% |  |  | 
Class F | -0.2% | -0.3% | -0.5% | 0.0% | 0.3% | -0.5% |  |  | 
Enc Time[%] | 92% |  |  | 89% |  |  |  |  | 
Dec Time[%] | 100% |  |  | 98% |  |  |  |  | 

## Slide 10: 8x8 bi-prediction restriction (proposed)
<number>
 | Random Access HE |  |  | Random Access LC |  |  | Random Access HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A (8bit) | 1.1% | 1.9% | 1.6% | 2.0% | 3.1% | 2.8% | 0.6% | 1.1% | 1.0%
Class B | 1.0% | 0.7% | 0.7% | 1.7% | 1.4% | 1.5% | 1.0% | 0.8% | 0.8%
Class C | 1.9% | 2.2% | 2.4% | 3.3% | 3.6% | 3.9% |  |  | 
Class D | 3.1% | 3.1% | 3.3% | 4.8% | 5.1% | 5.1% |  |  | 
Class E |  |  |  |  |  |  |  |  | 
Overall | 1.8% | 1.9% | 2.0% | 3.0% | 3.2% | 3.3% | 0.9% | 0.9% | 0.9%
 | 1.8% | 1.9% | 2.0% | 3.0% | 3.2% | 3.3% | 0.9% | 0.9% | 0.8%
Class F | 1.7% | 2.0% | 2.0% | 2.7% | 3.2% | 3.1% | 0.6% | 1.1% | 1.0%
Enc Time[%] | 79% |  |  | 71% |  |  | 79% |  | 
Dec Time[%] | 97% |  |  | 95% |  |  | 100% |  | 
 | Low delay B HE |  |  | Low delay B LC |  |  | Low delay B HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A |  |  |  |  |  |  |  |  | 
Class B | 1.0% | 0.2% | 0.4% | 2.1% | 1.0% | 1.2% |  |  | 
Class C | 2.4% | 2.2% | 2.5% | 4.2% | 4.1% | 4.0% |  |  | 
Class D | 3.7% | 2.9% | 4.3% | 6.3% | 6.5% | 6.4% |  |  | 
Class E | 0.8% | 0.5% | 0.0% | 2.1% | 1.1% | 1.4% |  |  | 
Overall | 2.0% | 1.5% | 1.8% | 3.7% | 3.2% | 3.2% |  |  | 
 | 2.0% | 1.5% | 1.8% | 3.7% | 3.1% | 3.2% |  |  | 
Class F | 2.9% | 3.0% | 2.9% | 4.7% | 4.3% | 4.2% |  |  | 
Enc Time[%] | 78% |  |  | 69% |  |  |  |  | 
Dec Time[%] | 98% |  |  | 95% |  |  |  |  | 

## Slide 11: 8x8 bi-prediction restriction (encoder only)
<number>
 | Random Access HE |  |  | Random Access LC |  |  | Random Access HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A (8bit) | 1.8% | 2.3% | 2.0% | 2.9% | 3.7% | 3.5% | 0.9% | 1.1% | 1.3%
Class B | 1.4% | 1.0% | 1.0% | 2.1% | 1.8% | 1.8% | 1.4% | 1.1% | 1.0%
Class C | 2.2% | 2.5% | 3.0% | 3.8% | 4.2% | 4.6% |  |  | 
Class D | 3.4% | 3.4% | 3.7% | 5.3% | 5.7% | 5.7% |  |  | 
Class E |  |  |  |  |  |  |  |  | 
Overall | 2.2% | 2.2% | 2.4% | 3.5% | 3.8% | 3.8% | 1.2% | 1.1% | 1.1%
 | 2.2% | 2.2% | 2.4% | 3.5% | 3.8% | 3.8% | 1.2% | 1.1% | 1.1%
Class F | 2.1% | 2.3% | 2.3% | 3.1% | 3.6% | 3.5% |  |  | 
Enc Time[%] | 77% |  |  | 69% |  |  | 77% |  | 
Dec Time[%] | 98% |  |  | 96% |  |  | 99% |  | 
 | Low delay B HE |  |  | Low delay B LC |  |  | Low delay B HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A |  |  |  |  |  |  |  |  | 
Class B | 1.7% | 0.7% | 0.8% | 2.9% | 1.7% | 1.9% |  |  | 
Class C | 3.2% | 3.0% | 3.7% | 5.3% | 5.5% | 5.8% |  |  | 
Class D | 4.5% | 4.0% | 5.2% | 7.4% | 8.1% | 8.0% |  |  | 
Class E | 1.3% | 0.4% | 0.1% | 2.9% | 1.9% | 2.7% |  |  | 
Overall | 2.7% | 2.1% | 2.5% | 4.6% | 4.3% | 4.5% |  |  | 
 | 2.7% | 2.1% | 2.5% | 4.6% | 4.3% | 4.5% |  |  | 
Class F | 3.7% | 4.1% | 3.7% | 5.7% | 5.6% | 6.3% |  |  | 
Enc Time[%] | 75% |  |  | 67% |  |  |  |  | 
Dec Time[%] | 97% |  |  | 94% |  |  |  |  | 

## Slide 12: Conclusion
Controllable memory bandwidth reduction
  PU size and Bi-pred PU size is restricted based on SCU size
  Replace inter_4x4_enable_flag with inter_predction_restriction_flag
Include Bi-pred to uni-pred conversion in merge mode
  Convert bi-prediction to uni-prediction when the derived merge mode is bi-prediction and the bi-prediction is restricted.
Results
We recommend the proposed modification to adopt in HM / CD
<number>
 |  | RA-HE | LB-HE | RA-LC | LB-LC | RA-HE10
4x8, 8x4 bi-pred and 4x4 PU restriction (8x8 SCU size) | proposal | 0.1 % | 0.1 % | 0.2 % | 0.3 % | 0.1 %
 | encoder only | 0.4 % | 0.5 % | 0.5 % | 0.8 % | 0.2 %
8x8 bi-pred restriction and less than 8x8 PU restriction (16x16 SCU emulation) | proposal | 1.8 % | 2.0 % | 3.0 % | 3.7 % | 0.9 %
 | encoder only | 2.2 % | 2.7 % | 3.5 % | 4.6 % | 1.2 %
Thank you to TI for cross-check (JCTVC-H0421)