## Slide 1: Modified definitions of intra mode and most probable mode (JCTVC-H0098)
JCT-VC 8th Meeting: San José, CA, USA, 1–10 February, 2012
Tomoyuki Yamamoto
SHARP Corporation

## Slide 2: Overall summary
Two simplifications on intra mode coding
  New intra mode numbering
    reduce table for angular intra prediction
    simpler derivation of main direction
  Omit MPM candidate swap
    less decoding process whcn MPM is used
Motivation
  MPM or REM mode order is not important in terms of coding efficiency
    mpm_idx and rem_intra_luma_pred_mode are coded with bypass mode
Coding efficiency
  BD-rate change: 0.00% ~ -0.01% for each change and combination
    Results are cross checked by Sony (JCTVC-H0527)
Recommendation … adopt both modifications in HM/WD
<number>

## Slide 3: New intra mode numbering
<number>
intraPred Mode | HM-5.0 | Proposed
0 | Planar | Planar
1 | VER | VER
2 | HOR | HOR
3 | DC | VER-8
4 | VER-8 | DC
5 | VER-4 | VER+8
6 | VER+4 | HOR+8
7 | VER+8 | VER-2
8 | HOR-4 | HOR-2
9 | HOR+4 | VER+2
10 | HOR+8 | HOR+2
11 | VER-6 | VER-4
12 | VER-2 | HOR-4
13 | VER+2 | VER+4
14 | VER+6 | HOR+4
15 | HOR-6 | VER-6
16 | HOR-2 | HOR-6
17 | HOR+2 | VER+6
18 | HOR+6 | HOR+6
intraPred Mode | HM-5.0 | Proposed
19 | VER-7 | VER-1
20 | VER-5 | HOR-1
21 | VER-3 | VER+1
22 | VER-1 | HOR+1
23 | VER+1 | VER-3
24 | VER+3 | HOR-3
25 | VER+5 | VER+3
26 | VER+7 | HOR+3
27 | HOR-7 | VER-5
28 | HOR-5 | HOR-5
29 | HOR-3 | VER+5
30 | HOR-1 | HOR+5
31 | HOR+1 | VER-7
32 | HOR+3 | HOR-7
33 | HOR+5 | VER+7
34 | HOR+7 | HOR+7
35 | LM | LM
a) VER and HOR are interleaved
 main direction can be derived easily
b1) 4 successive modes share the same abs angle
 abs angle table is kept small
b2) first 2 modes have negative angle
 sign of angle can be derived easily
c) mode 0, 1, 2 are same as HM-5.0
 familiar to the algorithm where shorter bits are assigned to rem[0]

## Slide 4: Usage of intra modes
<number>
decode mode
order[m]
absAng[abs(k)]
invAng[abs(k)]
bVer ? (o-25) : (o-9)
o >= 18
sign(k)
Angular prediction
H_trans[m]
V_trans[m]
MDCS[m]
MDIS[m]
m
m
o
bVer
k
invAng
absAng
signAng
H_trans_type
V_trans_type
scan_dir
filter_idx
decode mode
absAng[(m'+1)>>2]
invAng[(m'+1)>>2]
m' & 1
(m'+1) & 2
Angular Prediction
H_trans[m']
V_trans[m']
MDCS[m']
MDIS[m']
m'
m'
bVer
m'
invAng
absAng
signAng
H_trans_type
V_trans_type
scan_dir
filter_idx
Pred
Pred
HM-5.0
Proposed

## Slide 5: Omit MPM candidate swap
<number>
derive MPM0 from Left
MPM?
NO
YES
decode MPM index
derive MPM1 from Above
construct list of rem modes
conditionally swap MPM0 and MPM1
decode MPM flag
decode REM index
derive MPM0 from Left
MPM?
NO
YES
decode MPM index
derive MPM1 from Above
construct list of rem modes
conditionally swap MPM0 and MPM1
decode MPM flag
decode REM index
HM-5.0
Proposed
MPM swap is omitted for Left path

## Slide 6: Experimental result
<number>
New intra mode numbering (vs HM-5.0)
Omit MPM swap (vs HM-5.0)

## Slide 7: Experimental result
<number>
New intra mode numbering + Omit MPM swap (vs HM-5.0)
- No significant coding efficiency impact is observed
- New mode numbering slightly decrease processing time

## Slide 8: Conclusion
Two simplifications on intra mode coding
  New intra mode numbering
    reduce table for angular intra prediction
    simpler derivation of main direction
  Omit MPM candidate swap
    less decoding process when MPM is used
Coding efficiency
  BD-rate change: 0.00% ~ -0.01% for each change and combination
    Results are cross checked by Sony (JCTVC-H0527)
Related proposals
  intra mode numbering: H0175 (Cannon), H0407 (Sony)
  MPM candidate swap: H0175 (Cannon), H0428 (Qualcomm)
Recommendation … adopt both modifications in HM/WD
<number>