## Slide 1: On CABAC context for partition mode (JCTVC-H0099)
JCT-VC 8th Meeting: San José, CA, USA, 1–10 February, 2012
Tomoyuki Yamamoto
SHARP Corporation

## Slide 2: Overall summary
Context for partition mode information (part_mode)
  Discrepancy in current WD/HM
Solution 1
  Fix WD text to align with HM  some context depends on previous bin value in the same syntax
Solution 2
  Remove context of binIdx 2 and 3 of part_mode
   No in-syntax dependency, simpler text
   No significant change in coding efficiency
  * cross check by Qualcomm [H0687]
  * related contribution .. Qualcomm [H0545], Huawei/USTC [H0327]
Recommendation … adopt solution2
<number>

## Slide 3: Binarization of part_mode
<number>

## Slide 4: Discrepancy of context for part_mode
<number>
Syntax element | ctxIdxTable, ctxIdxOffset |  | binIdx |  |  |  | 
 |  |  | 0 | 1 | 2 | 3 | >=4
part_mode | Table 9‑25 | 2 | 0 | na | na | na | na
 |  | 3 | 0 | 1 | 0 | 1 | na
 |  | 6 | 0 | 1 | 0 | 1 | na
part_mode (cLog2CUSize = = Log2MinCUSize && cLog2CUSize > 3 ¦ ¦ inter_4x4_enabled_flag) | Table 9‑25 | 3 | 0 | 1 | 2 | na | na
 |  | 6 | 0 | 1 | 2 | na | na
Syntax element | ctxIdxTable, ctxIdxOffset |  | binIdx |  |  |  | 
 |  |  | 0 | 1 | 2 | 3 | >=4
part_mode | Table 9‑25 | 2 | 0 | na | na | na | na
 |  | 3 | 0 | 1 | 3 (bin1 is 1) 4 (bin1 is 0) | 5 (bin1 is 1) 6 (bin1 is 0) | na
 |  | 10 | 0 | 1 | 3 (bin1 is 1) 4 (bin1 is 0) | 5 (bin1 is 1) 6 (bin1 is 0) | na
part_mode (cLog2CUSize = = Log2MinCUSize && cLog2CUSize > 3 ¦ ¦ inter_4x4_enabled_flag) | Table 9‑25 | 3 | 0 | 1 | 2 | na | na
 |  | 10 | 0 | 1 | 2 | na | na
WD (G1203 d8)
HM-5.0
 context of binIdx 2 and 3 depends on bin value of binIdx 1

## Slide 5: Possible solutions
Solution 1
  Fix WD text to be aligned with HM
Solution 2
  Remove context for binIdx 2 and 3
<number>
Syntax element | ctxIdxTable, ctxIdxOffset |  | binIdx |  |  |  | 
 |  |  | 0 | 1 | 2 | 3 | >=4
part_mode | Table 9‑25 | 2 | 0 | na | na | na | na
 |  | 3 | 0 | 1 | na | na | na
 |  | 6 | 0 | 1 | na | na | na
part_mode (cLog2CUSize = = Log2MinCUSize && cLog2CUSize > 3 ¦ ¦ inter_4x4_enabled_flag) | Table 9‑25 | 3 | 0 | 1 | 2 | na | na
 |  | 6 | 0 | 1 | 2 | na | na

## Slide 6: Coding efficiency of solution 2
<number>
Note: Changes only affect when AMP is enabled

## Slide 7: Conclusion
Context for partition mode information (part_mode)
  Discrepancy in current WD/HM
Solution 1
  Fix WD text to align with HM  some context depends on previous bin value in the same syntax
Solution 2
  Remove context of binIdx 2 and 3 of part_mode
   No in-syntax dependency, simpler text
   No significant change in coding efficiency
  * cross check by Qualcomm [H0687]
  * related contribution .. Qualcomm [H0545], Huawei/USTC [H0327]
Recommendation … adopt solution2
<number>