## Slide 1: Non-CE11.1: Context reduction of significance map coding (JCTVC-H0100)
JCT-VC 8th Meeting in San José, CA, 1-10 February , 2012
Takeshi Tsukuba, Tomohiro Ikai
SHARP Corporation
Vadim Seregin, Joel Sole, Marta Karczewicz
Qualcomm

## Slide 2: Overall summary
Motivation
  Desirable to unify/simplify context derivation for significance map
Proposal 1 : Unified context derivation for 4x4 and 8x8 significance map
  Apply a common context assignment table for 4x4 and 8x8 blocks of each color component
  Context reduction : 11
Proposal 2 : DC context sharing
  Share DC context with all block sizes from 4x4 to 32x32 of each color component
  In total context reduction :13
Experimental result
  Average luminance BD-rate change on common QP(QP=22,27,32,37)
  DC context sharing (Propsal2) was implemented on top of the Proposal 1.
  Cross-checked results are provided by Panasonic.
 | AI_HE | RA_HE | LB_HE | RA10-HE | AI_LC | RA_LC | LB_LC
Proposal 1 | 0.03% | 0.01% | 0.02% | 0.07% | 0.04% | 0.05% | 0.01%
Proposal 2 | 0.03% | -0.01% | 0.00% | 0.05% | 0.03% | 0.02% | -0.05%

## Slide 3: HM-5.0’s Context assignment for significance map
Use 37 contexts for 4x4 and 8x8 significance map
  9 for 4x4 luma, 6 for 4x4 chroma, 11 for 8x8 luma, 11 for 8x8 chroma
Use 2 different lookup tables for context assignment
  30 elements for 4x4, 16 elements for 8x8
Use 6 DC contexts
  2 for 4x4, 2 for 8x8, 2 for 16x16~32x32
→ It’s desirable to unify/simplify contexts derivation for significance map
(c) 8x8 Luma and Chroma context assignment
10
1
4
5
8
6
9
9
2
3
6
3
6
7
7
7
0
1
4
5
8
6
9
9
2
3
6
3
6
7
7
7
0
1
4
5
8
6
9
9
2
3
6
3
6
7
7
7
0
1
4
5
8
6
9
9
2
3
6
3
6
7
7
0
1
1
1
3
3
4
4
2
4
2
4
5
5
5
(b) 4x4 Chroma context assignment
0
1
2
3
6
6
7
7
4
5
4
5
8
8
8
(a) 4x4 Luma context assignment

## Slide 4: Proposal 1
Use a common context assignment table for 4x4 and 8x8
  Unify context derivation for 4x4 and 8x8 significance map
  Remove the 8x8 lookup table
  Reduce 11 contexts
8x8 Luma
0
1
1
1
4
4
5
5
2
3
2
3
6
6
6
6
0
1
1
1
4
4
5
5
2
3
2
3
6
6
6
6
0
1
1
1
4
4
5
5
2
3
2
3
6
6
6
6
0
1
1
1
4
4
5
5
2
3
2
3
6
6
6
8x8 Chroma
0
1
1
1
4
4
3
3
2
3
2
3
5
5
5
5
0
1
1
1
4
4
3
3
2
3
2
3
5
5
5
5
0
1
1
1
4
4
3
3
2
3
2
3
5
5
5
5
0
1
1
1
4
4
3
3
2
3
2
3
5
5
5
0
1
1
1
4
4
5
5
2
3
2
3
6
6
6
4x4 Luma
0
1
1
1
4
4
3
3
2
3
2
3
5
5
5
4x4 Chroma
Use a common lookup table for luma
Use a common lookup table for chroma

## Slide 5: Proposal 2
Share DC context with all block sizes from 4x4 to 32x32
  In the case of combination with proposal 1 : In total context reduction reaches 13
  In the case of DC context sharing alone : Reduce 4 contexts
Th = min( width, height)
4x4
8x8
16x16~ 32x32
16x16~ 32x32
8x8
4x4
Luma
Chroma
sharing
sharing

## Slide 6: Experimental result ( Proposal 1, normal QPs)
+ Proposal 1 was implemented on the HM-5.0
+ Average BD-rate loss: 0.01% ~ 0.07%(Y), -0.27% ~ 0.12%(U), -0.22% ~ 0.30%(V)
+ No encoding / decoding time increase

## Slide 7: Experimental result ( Proposal 1, low QPs)
+ Proposal 1 was implemented on the HM-5.0
+ Average BD-rate loss: -0.02% ~ 0.05%(Y), 0.01% ~ 0.08%(U), -0.08%~0.11%(V)
+ No encoding / decoding time increase

## Slide 8: Experimental result ( Proposal 2, normal QPs)
+DC context sharing with (Proposal2) was implemented on top of the Proposal 1.
+ Average BD-rate loss: -0.05% ~ 0.05%(Y), -0.32% ~ 0.17%(U), -0.11% ~ 0.11%(V)
+ No encoding / decoding time increase

## Slide 9: Experimental result ( Proposal 2, low QPs)
+DC context sharing( Proposal2) was implemented on top of the Proposal 1.
+ Average BD-rate loss: -0.04% ~ 0.03% (Y), -0.02% ~ 0.07%(U), -0.14% ~ 0.05%(V)
+ No encoding / decoding time increase

## Slide 10: Experimental result ( Only DC context sharing, normal QPs)
+In the case of applying DC context sharing alone +average BD-rate loss: -0.02% ~ 0.05% (Y), -0.16% ~ 0.19%(U), -0.29% ~ 0.16%(V)
+ No encoding / decoding time increase

## Slide 11: Experimental result ( Only DC context sharing, low QPs)
+In the case of applying DC context sharing alone +average BD-rate loss: -0.01% ~ 0.00% (Y), -0.05% ~ 0.06%(U), -0.07% ~ 0.11%(V)
+ No encoding / decoding time increase

## Slide 12: Conclusion
Proposal 1 : Unified context derivation for 4x4 and 8x8 significance map
  Apply a common context assignment table for 4x4 and 8x8 blocks of each color component
  Context reduction : 11
Proposal 2 : DC context sharing
  Share DC context with all block sizes from 4x4 to 32x32 of each color component
  In total context reduction : 13
Average BD-rate changes
  Proposal 1: 0.01%~0.07% ( normal QP ), -0.02%~0.05% ( low QP)
  Proposal 2: -0.05%~0.05% ( normal QP), -0.04%~0.03% ( low QP)
    DC context sharing (Propsal2) was implemented on top of the Proposal 1.
  Only DC context sharing : -0.02% ~ 0.05% ( normal QP), -0.01% ~ 0.00% ( low QP)
Recommendation … adopt both modifications in HM/WD
Many thanks to Panasonic for cross-checking this contribution (JCTVC-H0100)

## Slide 13: Additional information
Results of combination of H0443 and proposal 1 on common condition
Average BD-rate change: 0.01%~0.09% (Y)

## Slide 14: Additional information
Results of combination of H0443 and proposal 1 on low QP condition
Average BD-rate change: 0.00%~0.15%(Y)