## Slide 1: JCTVC-H0112 CE1, subtest C4: Multi-parameter probability estimation for CABAC
Elena Alshina, Alexander Alshin, JeongHoon Park
Samsung Electronics Ltd

## Slide 2: Why 2 models for PE perform better than 1?
Short distance prediction (B) quickly converges to true value ¾ ; but this model is subject to fluctuations in a large measure.
“Semi-sum” (C) tends to optimal value slowly but later reaction for small perturbations is not so noticeable
stabilization
JCTVC-H0112 CE1, subtest C4: Multi-parameter probability estimation for CABAC

## Slide 3: Summary of proposed changes
HM5.0 | JCTVC-H0112
Memory usage of each context model | 
UChar m_ucState; | UShort iP0,iP1; char uiIndex;
State up-date | 
UChar m_aucNextStateMPS[ 128 ]; UChar m_aucNextStateLPS[ 128 ]; | iP0=iP0 +(((Y==1?32768 :0)- iP0)>>4); iP1=iP1 +(((Y==1?32768 :0)- iP1)>>7); if (uiIndex<50) return iP0; else return (iP0+iP1+1)>>1;
Interval sub-division | 
UChar sm_aucLPSTable[64][4]; UChar sm_aucRenormTable[32]; | UShort sm_aucLPSTable[64][64]; UChar sm_aucRenormTable[64];
CABAC Initialization | 
 | +UShort uiConvertProbability[64];
JCTVC-H0112 CE1, subtest C4: Multi-parameter probability estimation for CABAC

## Slide 4: Test results summary
Conclusion:
Based on reported performance improvement
0.7% (Luma) and 0.4% (Chroma) BD-rate gain
Samsung proposes to adopt multi-parameter CABAC probability up-date model to WD and HM6.0.
JCTVC-H0112 CE1, subtest C4: Multi-parameter probability estimation for CABAC
Test | One parameter | 2-parameters
AI | -0.4% | -0.8%
RA | -0.3% | -0.7%
LB | -0.2% | -0.6%
All | -0.3% | -0.7%
Avg Enc Time | 100% | 103%
Avg Dec Time | 100% | 101%
BD-rate difference is averaged across AI, RA, LD(B) for HE, LC and HE-10, class F is not included