## Slide 1: Objective and subjective evaluation of HM5.0 JCTVC-H0116, 8th JCTVC meeting
TK Tan, A. Fujibayashi, Y. Suzuki & J. Takiue
NTT DOCOMO, Inc.
1 – 10 February 2012.

## Slide 2: Summary
Objective and subjective evaluation of HM5.0 was conducted.
  To evaluate the performance of HM5.0 compared to JM.
  To find a minimum tool set
The following steps were performed.
  Objective evaluation of tools combinations
    Simulation was conducted for the common conditions in JCTVC-G1200
    Additional combinations of LC + tools enabled in HE but not in LC were also simulated.
    BD-rate vs. Encoding / Decoding time were plotted.
  Subjective evaluation of tools combinations
    The visual quality of the decoded sequences in the simulation were checked to see if the BD-rate improvements were observable.
  Clustering of tools  selection of minimum tool set for comparison to JM.
    Based on the objective and subjective evaluation of tools combinations, a clustering of the tools were made
    A minimum tool set of LC tools + RDOQ and SAO was selected as a good trade-off between coding performance and complexity.
  Subjective comparison between HM and JM
    Informal subjective testing (preliminary screening)
    Formal subjective testing.

## Slide 3: 1) Objective Measure – Common conditions
HM5.0 coding structure and corresponding JM18.0 reference
The luma BD-rate gains of HM5.0 HE & LC compared to the JM18.0 for the following coding conditions are:
HM coding structure | JM configuration
Random Access (RA) | Alpha anchor (IbBbBbBbP)
Low Delay B (LB) | Beta* anchor (IPPP)
Low Delay P (LP) | Beta* anchor (IPPP)
All Intra (AI) | Alpha anchor with all I only.
Alpha and Beta anchors are the JM references used in the HVC call for proposal.
Beta* anchor, represent the Beta anchor with the exception that there is no longer temporal nesting and all frames are reference frames.
 | Random Access | Low Delay B | Low Delay P | All Intra
High efficiency (HE) | -35.9% | -41.2% | -37.4% | -22.9%
Low delay (LC) | -28.5% | -34.7% | -26.2% | -16.5%

## Slide 4: 1) Objective Measure - Summary of combination of tools
When various tools are added to the LC common conditions, the effects on BD-Rate (+ve is gains) are as follows.
  The objective gains are mostly contributed by RDOQ, ALF and to a lesser extent SAO.
    Random access (cf. alpha): RDOQ (3.5%), ALF (2.6%) and SAO (0.8%)
    Low delay B (cf. beta): RDOQ (2.3%), ALF (2.0%) and SAO (1.3%)
    Low delay P (cf. beta): ALF (6.4%), SAO (5.4%) and RDOQ (1.4%)
    Intra only (cf AI alpha): RDOQ (4.2%) and ALF (1.7%)
  Together ALF and SAO account for most of the difference in decoding time between HE and LC.
  AMP increases encoding time, but contribute marginally to the coding gains.
    Random access: Enc Time: +8%, BD-Rate gains: 0.6%
    Low delay B: Enc Time: +14%, BD-Rate gains: 0.7%
    Low delay P: Enc Time: +10%, BD-Rate gains: 0.6%
  NSQT has negligible impact on encoding and decoding time, but contribute coding gains as follows
    Random access: BD-Rate gains: 0.2%
    Low delay B: BD-Rate gains: 0.6%
    Low delay P: BD-Rate gains: 0.5%
Note that the BD-rate reported here are BD-rate LC+X – BD-rate LC with JM as the reference and X is one of {RDOQ, SAO, ALF, AMP or NSQT}.

## Slide 5: 1) Objective Measure - RA encoding with LC + Tools
Various tools are added to LC to see what their effects on BD-Rate (+ve is gains) and encoding time (100% = JM18.0 encoding time).
Top gains come from RDOQ (3.5%), ALF (2.6%) and SAO (0.8%)

## Slide 6: 1) Objective Measure - RA decoding with LC + Tools
Various tools are added to LC to see what their effects on BD-Rate (+ve is gains) and decoding time (100% = JM18.0 decoding time).
Decoding time increase is mostly due to ALF and SAO

## Slide 7: 2) Subjective evaluation of tools combinations
The observations on the subjective quality.
The main observations found in this comparison are as follows:
  Enabling RDOQ can sometimes cause some noisiness in the subjective quality of the video.
  Enabling SAO results in the visible improvement for some sequences especially BasketballDrill and Kimono1.
Tools | Observations - Random Access | Observations – Low Delay B
LC | Some colour bleeding, aliasing, wobbling were observed. | Some colour bleeding, aliasing, blockiness were observed.
LC+RDOQ | Similar quality to LC. But artifact seems more pronounced. | Similar problems but seems to be worse than LC
LC+ALF | Similar quality to LC. Some colour bleedings were slightly reduced but impact seems small. | Similar quality to LC.
LC+SAO | Same quality as HE. | Same quality as HE.
LC+ALF+SAO | Same quality as HE. | Same quality as HE
LC+RDOQ+ALF | Similar quality to LC + RDOQ | Similar quality to LC or LC + RDOQ
LC+RDOQ+SAO | Same quality as HE. | Same quality as HE

## Slide 8: 3) Clustering of tools
Tool cluster | Cluster 0: RDOQ | Cluster 1: LMChroma | Cluster 2: AMP NSQT | Cluster 3: SAO | Cluster 4: ALF
Impact on decoding time | None | Negligible | Negligible | Low to medium | High
Objective Gains (BD-rate relative to BD-rate LC) | 1.4% to 4.2% | Mostly chroma only 1.9% to 5.6% | Small (less than 1.0% BD-rate) | 0.5% to 5.4% | 1.7% to 6.4%
Subjective improvements | Can sometime cause some noisiness in the subjective quality |  |  | Visible on some sequences: BasketballDrill and Kimono1 | Not visible

## Slide 9: 4) Subjective comparison between HM and JM
Objective
  To verify if the HM5.0 has achieved the 50% bitrate savings target compared to JM18.
Codecs are tested
  1) JM 18.2* high profile (modified JM18.2 described in JCTVC-H360)
  2) HM5.0 high efficiency (HM5.0 HE)
  3) HM5.0 low complexity with RDOQ and SAO (HM5.0 LC+RDOQ+SAO)
Coding structure
  The random access coding structure was used for all codecs as this was found to be the most efficient coding structure.
Test bitrates (QP selection)
  The JM 18.2* bitstreams are coded at QP = 27, 30, 33, 36
  The HM5.0 HE and HM5.0 LC+RDOQ+SAO bitstreams are coded at not more than half the bitrate of the JM 18.2* bitstreams. (QP = 31, 34, 37, 40)
9 test sequences used
  Class B and Class C
Acknowledgment
The authors wishes to thank University of Science and Technology of China and Microsoft Corp for providing the JM18.2*software

## Slide 10: 4) Informal subjective testing
The main indicative findings of the informal subjective test comparing HM5.0 HE, HM5.0 LC+RDOQ+SAO and JM18.2* are:
  Both HM5.0 HE and HM5.0 LC+RDOQ+SAO has achieved the target of 50% bitrate savings over JM18.2* and it is quite possible than the bitrate saving is even higher than 50%.
  HM5.0 HE and HM5.0 LC+RDOQ+SAO at the same bitrate have the same subjective quality.
# of observer votes received by a test case (combination of votes) |  |  | # of test cases where the combination of votes occurred | Cumulative % where majority voted that HM5.0 HE at half the bitrate has a quality better than or equal to JM 18.2*.
HM5.0 HE at half the bitrate is better than JM 18.2* | HM5.0 HE at half the bitrate and JM 18.2* are comparable | JM 18.2* is better than HM5.0 HE at half the bitrate |  | 
4 | 0 | 0 | 20 | 56%
3 | 1 | 0 | 2 | 61%
3 | 0 | 1 | 5 | 75%
2 | 2 | 0 | 1 | 78%
2 | 1 | 1 | 1 | 81%
1 | 3 | 0 | 1 | 83%
1 | 0 | 3 | 2 | 
0 | 2 | 2 | 2 | 
0 | 0 | 4 | 2 | 

## Slide 11: 4) Formal subjective testing.
The main findings of the formal subjective test comparing HM5.0 HE, HM5.0 LC+RDOQ+SAO and JM18.2* are:
  MOS vs. bitrate (see slides 20 to 28).
    For all the test cases, the MOS scores assigned to HM HE and HM LC+RDOQ+SAO coded at comparable bitrates are not statistically distinguishable.
    In comparison to the corresponding JM bitstreams, except for the lower 3 bitrate points of "PartyScene", HM at half the bitrate or less (52% to 36%) achieves similar subjective quality to JM. (33/36 test points).
  BD-rate calculations from MOS vs. bitrate plots
    The average BD-rate gains achieved by HM5.0 RA-HE and HM5.0 RA-LC+RDOQ+SAO compared to JM are 51.2% and 49.4%, respectively.
    The difference between HM5.0 RA-HE and HM5.0 RA-LC+RDOQ+RA is only 1.8%.
 | A) | B) | 
 | RAHE vs JM | RA LC+RDOQ+SAO vs. JM | A) - B)
BQTerrace | -68.4% | -62.5% | -5.9%
BasketballDrive | -69.8% | -67.2% | -2.6%
cactus | -52.4% | -50.6% | -1.8%
Kimono1 | -50.7% | -55.2% | 4.6%
ParkScene | -51.9% | -50.1% | -1.8%
BQMall | -46.1% | -42.2% | -3.9%
BasketballDrill | -46.4% | -45.9% | -0.5%
PartyScene | -25.2% | -29.0% | 3.9%
RaceHorses | -49.8% | -41.8% | -8.0%
Average | -51.2% | -49.4% | -1.8%

## Slide 12: Conclusion
The following are concluded in this contribution.
  BD-rate measures give a very rough indication of the actual performance gains achieved by HEVC.
    Sometimes, subjective gains are not visible despite significant objective gains and vice-versa.
    It is recommended that subjective assessment should be the norm rather than the exception when accessing the performance of the HEVC.
  For the random access coding structure, the formal subjective test confirmed that:
    HM5.0 HE and HM5.0 LC+RDOQ+SAO at the same bitrate have the same subjective quality.
    HM5.0 at half the bitrate or less (52% to 36%) has the same subjective quality compared to JM18.2*.

## Slide 13: Additional Slides

## Slide 14: Low delay B encoding with LC + Tools
Various tools are added to LC to see what their effects on BD-Rate (+ve is gains) and encoding time (100% = JM18.0 encoding time)..
Top gains come from RDOQ (2.3%), ALF (2.0%) and SAO (1.3%)

## Slide 15: Low delay B decoding with LC + Tools
Various tools are added to LC to see what their effects on BD-Rate (+ve is gains) and decoding time (100% = JM18.0 decoding time)..
Decoding time increase is mostly due to ALF and SAO

## Slide 16: Low delay P encoding with LC + Tools
Various tools are added to LC to see what their effects on BD-Rate (+ve is gains) and encoding time (100% = JM18.0 encoding time).
Top gains come from ALF (6.5%), SAO (5.5%) and RDOQ (1.3%) out of 11.2% HE gain.

## Slide 17: Low delay P decoding with LC + Tools
Various tools are added to LC to see what their effects on BD-Rate (+ve is gains) and decoding time (100% = JM18.0 decoding time).
Decoding time increase is mostly due to ALF and SAO

## Slide 18: Intra only encoding with LC + Tools
Various tools are added to LC to see what their effects on BD-Rate (+ve is gains) and encoding time (100% = JM18.0 encoding time).
Top gains come from RDOQ (3.0%) and ALF (1.8%) out of 6.4% HE gain.

## Slide 19: Intra only decoding with LC + Tools
Various tools are added to LC to see what their effects on BD-Rate (+ve is gains) and decoding time (100% = JM18.0 decoding time).
Decoding time increase is mostly due to ALF.

## Slide 20: Formal subjective test

## Slide 21: Formal subjective test

## Slide 22: Formal subjective test

## Slide 23: Formal subjective test

## Slide 24: Formal subjective test

## Slide 25: Formal subjective test

## Slide 26: Formal subjective test

## Slide 27: Formal subjective test

## Slide 28: Formal subjective test