## Slide 1: Improvement of Intra DC prediction for cases without neighbouring samples JCTVC-H0120
Alberto Dueñas, Francisco Javier Roncero, Oscar Patino and Adam Malamy

## Slide 2: Problem Statement
On the current WD5 in the cases where intra prediction is required for a CU where no neighbouring samples are available, value of 128 for all neighbors is used to perform the intra prediction
We define this as a 128-value prediction
The usage of the current 128-value prediction may cause a large error in some occasions leading to:
  Noticeable visually artifact
  Noticeable coding efficiency lost

## Slide 3: Problem Statement (2)
Original WD5:
Propose Contribution:
QP 40 in Low Delay P Low complexity

## Slide 4: Algorithm description
The current contribution proposed is to add an intra_DC_X_value parameter to the syntax (where X = luminance, Cb and Cr) that could be used on the cases where the current 128-value prediction is currently utilized to perform intra prediction (where no neighbouring samples are available)
This proposal implies the following new main tasks in the bitstream generation process:
  Adding the new syntax elements – intra_DC_X_value – to the bitstream for the cases described
  The calculation of the value for intra_DC_X_value during the prediction process
Assumed to have a low implementation cost

## Slide 5: Algorithm description (2)
Using the “currently not used” Intra prediction mode 35 for luma to signal the special Intra_DC prediction proposed enables new syntax elements intra_DC_X_value that must be expected in the bit-stream.
No signaling is required when intra_DC_X_value it is not used and will have no cost when not used
Intra prediction mode | Associated names
0 | Intra_Planar
1 | Intra_Vertical
2 | Intra_Horizontal
3 | Intra_DC
Otherwise (4..34) | Intra_Angular
35 | Intra_FromLuma (used only for chroma)

## Slide 6: Algorithm description (3)
When the new special Intra_DC prediction proposed is used
  New intra_DC_Cx_value syntax elements if special Intra_DC prediction is signaled
DC value calculated as usual if special Intra_DC is not signaled
Current implementation calculates DCVal as:
The proposal will use the new syntax elements: DCVal = intra_DC_X_value (X = luma, Cb and Cr)

## Slide 7: Experimental results
Two new configurations are being tested:
  Low delay P LC + Force Intra Refresh + Constrained Intra.
    HM has been modified to enforce the usage of Intra LCUs (10% of total LCUs in a frame) in a regular partern, one every 10 and enabling “ConstrainedIntraPred”
  All Intra LC + Slices.
    HM has been modified to force slices boundaries (slices of 10 LCUs in size are used in this case)
No significant changes on the standard configurations

## Slide 8: Experimental results (2)
 | Low Delay P LC +Force Intra |  | 
 | Y | U | V
Class A | - | - | -
Class B | -0.8 | -3.8 | -2.7
Class C | -2.3 | -7.0 | -8.0
Class D | 0.7 | -1.1 | -2.0
Class E | 0.6 | 0.3 | -0.5
Overall | -0.6 | -3.1 | -3.4
Enc Time[%] | 100% |  | 
Dec Time[%] | -- |  | 
 | All Intra LC + Slices |  | 
 | Y | U | V
Class A | - | - | -
Class B | -0.3 | -0.4 | -0.5
Class C | -0.2 | -0.1 | -0.3
Class D | -0.1 | -0.3 | 0.8
Class E | -0.2 | -1.2 | -0.6
Overall | -0.1 | -0.5 | -0.2
Enc Time[%] | 100% |  | 
Dec Time[%] | -- |  | 

## Slide 9: Conclusions
The proposed algorithm deals with an issue that is producing both noticeable visual degradation and coding efficiency degradation
Simple encoding/decoding process modifications
In case where no neighbouring samples are available:
  Visual improvement are produced
  BD-Rate improvement is produced
No cost when it is not used, using unused signaling

## Slide 10: Thank You