## Slide 1
CE11 : Level Context Reduction
(JCTVC-H130)
Yinji Piao

## Slide 2: Summary
Propose to simplify luma context model of level coding
  More consistent context sets for luma and chroma
  25% context reduction for level coding
Coding performance
  0.0% / AI_HE, 0.0% / RA_HE, 0.0% / LD_HE
  0.0% / AI_LC, 0.0% / RA_LC, -0.0% / LD_LC
  0.0% / RA_HE10

## Slide 3: Level coding in HM5.0
Context for GreaterT1 flag and GreaterT2 flag
  32 contexts for GreaterT1 flag: 6x4 (luma) + 2x4 (chroma)
  24 contexts for GreaterT2 flag: 6x3 (luma) + 2x3 (chroma)
  Context_idx = [contextset_idx, modelbin]
    Subset of large transform: 4x4 subblock
    Subset of 4x4 & 8x8 : Every 16 coefficients in reverse scan order
Context Set_Luma (previous subset) |  | 
0 | Sub-set 0 | 0 LargerT1
1 |  | 1-3 LargerT1
2 |  | >3 LargerT1
3 | Other sub-sets | 0 LargerT1
4 |  | 1-3 LargerT1
5 |  | >3 LargerT1
Luma
Context Set_Chroma (previous subset) | 
0 1 | No LargerT1
 | At least one LargerT1
Chroma
Model bin 1 (current subset) | 
0 | 1 or more LargerT1
1 | Initial - no trailing ones
2 | 1 trailing one
3 | 2 or more trailing ones
Model bin 2 (current subset) | 
0 | Initial - no LargerT1
1 | 1 LargerT1
2 | 2 or more LargerT1
GreaterT1 flag
GreaterT2 flag
Context set
Modelbin

## Slide 4: Simplified luma context set
Context for GreaterT1 flag and GreaterT2 flag
  Remove 8 luma contexts of GreaterT1 flag: 6x4  4x4
  Remove 6 luma contexts of GreaterT2 flag: 6x3  4x3
Context Set_Luma (previous subset) |  | 
0 | Sub-set 0 | No LargerT1
1 |  | At least one LargerT1
2 | Other sub-sets | No LargerT1
3 |  | At least one LargerT1
Luma
Context Set_Chroma (previous subset) | 
0 1 | No LargerT1
 | At least one LargerT1
Chroma
Context set
Modelbin
Model bin 1 (current subset) | 
0 | 1 or more LargerT1
1 | Initial - no trailing ones
2 | 1 trailing one
3 | 2 or more trailing ones
Model bin 2 (current subset) | 
0 | Initial - no LargerT1
1 | 1 LargerT1
2 | 2 or more LargerT1
GreaterT1 flag
GreaterT2 flag

## Slide 5: Experimental results
Common test condition
 | All Intra HE |  |  | Random Access HE |  |  | Low delay B HE |  |  | Random Access HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Class A | 0.1 | 0.1 | 0.1 | 0.0 | 0.0 | -0.1 |  |  |  | 0.0 | 0.2 | -0.2
Class B | 0.0 | 0.1 | 0.1 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.2 | 0.1 | 0.1 | -0.1
Class C | 0.0 | 0.0 | 0.0 | 0.0 | -0.1 | 0.1 | 0.0 | -0.1 | 0.2 |  |  | 
Class D | 0.0 | 0.0 | 0.0 | 0.0 | -0.4 | -0.2 | 0.0 | 0.1 | -0.1 |  |  | 
Class E | 0.0 | 0.0 | 0.1 |  |  |  | 0.0 | 0.5 | -0.1 |  |  | 
Overall | 0.0 | 0.0 | 0.0 | 0.0 | -0.2 | 0.0 | 0.0 | 0.1 | 0.0 | 0.0 | 0.1 | -0.1
Enc Time | 100% |  |  | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time | 100% |  |  | 100% |  |  | 99% |  |  | 102% |  | 
 | All Intra LC |  |  | Random Access LC |  |  | Low delay B LC |  |  |  |  | 
 | Y | U | V | Y | U | V | Y | U | V |  |  | 
Class A | 0.0 | 0.1 | 0.1 | 0.0 | 0.1 | 0.0 |  |  |  |  |  | 
Class B | 0.0 | 0.1 | 0.1 | 0.0 | 0.2 | 0.2 | 0.0 | -0.3 | 0.0 |  |  | 
Class C | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 |  |  | 
Class D | 0.0 | 0.0 | 0.0 | 0.0 | 0.5 | -0.2 | 0.0 | 0.7 | -0.1 |  |  | 
Class E | 0.0 | 0.1 | 0.0 |  |  |  | -0.1 | -0.6 | -1.5 |  |  | 
Overall | 0.0 | 0.0 | 0.0 | 0.0 | 0.2 | 0.0 | 0.0 | 0.0 | -0.3 |  |  | 
Enc Time | 99% |  |  | 100% |  |  | 100% |  |  |  |  | 
Dec Time | 100% |  |  | 100% |  |  | 100% |  |  |  |  | 

## Slide 6: Conclusion
Number of removed context: 25%
Coding performance
  0.0% / AI_HE, 0.0% / RA_HE, 0.0% / LD_HE
  0.0% / AI_LC, 0.0% / RA_LC, -0.0% / LD_LC
  0.0% / RA_HE10
 | HM5.0 |  | Proposed | 
 | Luma | Chroma | Luma | Chroma
coeff_abs_level_greater1_flag | 24 | 8 | 16 | 8
coeff_abs_leve2_greater1_flag | 18 | 6 | 12 | 6

## Slide 7
Thank you !

## Slide 8: Experimental results
Low QP test
 | All Intra HE |  |  | Random Access HE |  |  | Low delay B HE |  |  | Random Access HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Class A | 0.1 | 0.1 | 0.1 | 0.1 | 0.0 | 0.1 |  |  |  | 0.1 | 0.1 | 0.0
Class B | 0.1 | 0.1 | 0.1 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.1 | 0.0
Class C | 0.0 | 0.0 | 0.1 | 0.0 | 0.0 | 0.0 | 0.0 | -0.1 | 0.1 |  |  | 
Class D | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.1 | 0.0 | 0.0 | 0.0 |  |  | 
Class E | 0.1 | 0.1 | 0.1 |  |  |  | 0.0 | 0.1 | -0.2 |  |  | 
Overall | 0.1 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.1 | 0.1 | 0.0
Enc Time | 100% |  |  | 101% |  |  | 101% |  |  | 100% |  | 
Dec Time | 100% |  |  | 101% |  |  | 101% |  |  | 102% |  | 
 | All Intra LC |  |  | Random Access LC |  |  | Low delay B LC |  |  |  |  | 
 | Y | U | V | Y | U | V | Y | U | V |  |  | 
Class A | 0.0 | 0.1 | 0.1 | 0.0 | 0.0 | 0.0 |  |  |  |  |  | 
Class B | 0.1 | 0.1 | 0.1 | 0.0 | 0.0 | 0.1 | 0.0 | 0.0 | 0.1 |  |  | 
Class C | 0.0 | 0.1 | 0.1 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.1 |  |  | 
Class D | 0.0 | 0.0 | 0.0 | 0.0 | 0.1 | 0.0 | 0.0 | 0.1 | 0.0 |  |  | 
Class E | 0.1 | 0.1 | 0.1 |  |  |  | 0.0 | -0.8 | -0.2 |  |  | 
Overall | 0.0 | 0.1 | 0.1 | 0.0 | 0.0 | 0.0 | 0.0 | -0.1 | 0.0 |  |  | 
Enc Time | 100% |  |  | 100% |  |  | 100% |  |  |  |  | 
Dec Time | 100% |  |  | 101% |  |  | 100% |  |  |  |  | 

## Slide 9: Experimental results
RDOQ off
 | All Intra HE |  |  | Random Access HE |  |  | Low delay B HE |  |  | Random Access HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Class A | 0.0 | 0.1 | 0.0 | 0.0 | 0.0 | 0.1 |  |  |  | 0.0 | 0.2 | 0.0
Class B | 0.0 | 0.1 | 0.0 | 0.0 | 0.1 | 0.0 | 0.0 | 0.1 | -0.1 | 0.0 | 0.0 | -0.1
Class C | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | -0.2 | 0.0 | -0.1 | 0.1 |  |  | 
Class D | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.1 | -0.1 | -0.1 | 0.0 |  |  | 
Class E | 0.0 | 0.1 | 0.0 |  |  |  | 0.1 | 0.0 | -0.7 |  |  | 
Overall | 0.0 | 0.1 | 0.1 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | -0.2 | 0.0 | 0.1 | -0.1
Enc Time | 100% |  |  | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time | 100% |  |  | 100% |  |  | 100% |  |  | 101% |  | 
 | All Intra LC |  |  | Random Access LC |  |  | Low delay B LC |  |  |  |  | 
 | Y | U | V | Y | U | V | Y | U | V |  |  | 
Class A | 0.0 | 0.1 | 0.1 | 0.0 | 0.1 | 0.0 |  |  |  |  |  | 
Class B | 0.0 | 0.1 | 0.1 | 0.0 | 0.2 | 0.2 | 0.0 | -0.3 | 0.0 |  |  | 
Class C | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 |  |  | 
Class D | 0.0 | 0.0 | 0.0 | 0.0 | 0.5 | -0.2 | 0.0 | 0.7 | -0.1 |  |  | 
Class E | 0.0 | 0.1 | 0.0 |  |  |  | -0.1 | -0.6 | -1.5 |  |  | 
Overall | 0.0 | 0.0 | 0.0 | 0.0 | 0.2 | 0.0 | 0.0 | 0.0 | -0.3 |  |  | 
Enc Time | 99% |  |  | 100% |  |  | 100% |  |  |  |  | 
Dec Time | 100% |  |  | 99% |  |  | 99% |  |  |  |  |