## Slide 1
JCTVC-H0140
CE1: Modified probability update and table removal for multi-parameter CABAC update
(Sub-test C2)
8th JCT-VC meeting, Feb 2012.

## Slide 2: Background: H0112/G764 (studied in CE1)
Either one or two 15-bit probability estimates exist for each context (iP0, iP1).
  iP0 and iP1 are averaged to create a combined probability estimate.
  iP0 and iP1 evenly cover the [0, 1] probability space (no more ‘valMPS’).
The CABAC offset (“uiLPS”) is determined by performing a table look-up on a 2D table.
  The first dimension index is created by truncating the combined probability estimate from 15-bits to 6-bits.
  The second dimension index is created by truncating the 9-bit range value to 6-bits (the MSB is required to always be ‘1’ and is ignored).
  The table contains 9-bit entries, resulting in an overall table size of 36Kb (reduced from 288Kb in G764).
Problem: A 36Kb (64x64x9-bit) look-up table is introduced in H0112.

## Slide 3: H0140 solution
36Kb LUT is removed and updateLPS() is modified:
  Note: updateLPS() refers to bin = 0 case.
H0112/G764 36Kb LUT replaced with the following steps:
  A 15-bit combined probability estimate (either iP0 or average of iP0 and iP1) is right shifted by 6 bits, producing a 9-bit truncated probability estimate (we retain the 9-bit truncation of G764).
  The truncated probability estimate is inverted.
  The 9-bit range value is masked by 0x1fc to produce a 7-bit value.
  Multiply the truncated probability estimate (9-bits) with the 7-bit value to produce a 16 bit value (note that MSB of 7-bit value is always 1, so multiplication logic is a bit simplified).
  Right shift the product by 9-bits to produce a 7-bit offset.
  Clip the offset to a minimum value.

## Slide 4: H0140 solution
updateLPS() modification:
  The H0112/G764 updateLPS() is defined as:
    iP0 -= iP0 >> ALPHA0
    iP1 -= iP1 >> ALPHA1
  The proposed updateLPS() is defined as:
    iP0 = max(iP0 – iP0 >> ALPHA0, 2<<6)
    iP0 = max(iP1 – iP1 >> ALPHA1, 2<<6)
  (ALPHA1 and ALPHA2 are constants which set the rate of adaptation 0 and 1 bin values.)

## Slide 5: Results relative to HM-5.0

## Slide 6: Results relative to HM-5.0 (continued)