## Slide 1
JCTVC-H0145
Non-CE11: Harmonisation of 8x8 TU residual scan
8th JCT-VC meeting, Feb 2012.

## Slide 2: Background information: G1038 ‘straw man’ solution
Summary of residual coding in HM-5.0:
Transform size | Sub-block | Upper scan | Ctx selection dependency | Scan pattern: Sub-block | Scan pattern: Upper layer
4x4 | 4x4 | N/A | Position | H,V, D (MDCS) | N/A
8x8 | 8x8 | N/A | Position | H,V, D (MDCS) | N/A
16x16 | 4x4 | 4x4 | Neighbours | D | D
32x32 | 4x4 | 8x8 | Neighbours | D | D
4x16 | 4x4 | 1x4 | Neighbours | D | D
16x4 | 4x4 | 4x1 | Neighbours | D | D
8x32 | 4x4 | 2x8 | Neighbours | D | D
32x8 | 4x4 | 8x2 | Neighbours | D | D

## Slide 3: Proposal
Harmonise the 8x8 TU scan with other TU sizes:
  Split 8x8 TU into four 4x4 sub-blocks.
    Scan within each sub-block according to MDCS.
  Two options for the order of scanning sub-blocks (upper layer):
    1. Scan the upper layer also according to MDCS.
    2. Always use diagonal scan.
      This can be considered a further level of harmonisation.
  Benefit:
    All TU sizes now use 4x4 sub-block as the smallest entity.
  (Note: 4x4 case is effectively one sub-block and therefore trivial.)

## Slide 4: Results – Upper layer MDCS

## Slide 5: Results – Upper layer diagonal only