## Slide 1: CE10 Subtest 4: Deblocking filter using adaptive weighting factors
Ann-Kathrin Seifert,Thomas Wedi, Matthias Narroschke
Panasonic Corporation
8th JCT-VC meeting, San José, 01.-10. February 2012

## Slide 2: Outline
Introduction
Deblocking filter using adaptive weighting factors
Estimation of weighting factors
Experiments and results
Conclusion

## Slide 3: Deblocking filter according to HM4.0
Deblocking of a reconstructed sample :
: Value by which a sample value is modified
Problem:
is generated by a fixed filter
=> No adaptation to varying signal statistics possible

## Slide 4: Deblocking filter using adaptive weighting factors
Adaptation to varying signal statistics by adaptive weighting factor :
Luminance: Individual weighting factors
  Strong and weak filtering
  Distance to block boundary
Chrominances: No weighting factors
Total: 5 weighting factors

## Slide 5: Estimation of weighting factors
Minimization of MSE for subjectively important samples:
Subjectively important samples are defined by:
=> Considered as subjectively important

## Slide 6: Coding of estimated weighting factors
Quantization with step size of 1/64
Coding of the 5 quantized weighting factors:
  Slice header
  No arithmetic coding

## Slide 7: Objective Results
Configuration | BD-Bit rate [%] |  | Encoder run time ratio [%] | Decoder run time ratio [%]
 | Classes A-E | Class F |  | 
I HE | -0.1 | -0.2 | 101 | 101
I LC | -0.1 | -0.2 | 99 | 100
RA HE | 0.0 | -0.2 | 101 | 101
RA LC | 0.0 | -0.1 | 99 | 102
RA HE 10bit | -0.2 | - | 100 | 101
LDB HE | 0.0 | 0.0 | 102 | 102
LDB LC | 0.1 | -0.4 | 99 | 101
LDP HE | 0.1 | 0.0 | 100 | 102
LDP LC | 0.2 | -0.2 | 100 | 100

## Slide 8: Subjective results
HM5.0
JCTVC-H0148
Cactus, LD HE, QP42, Frame 269

## Slide 9: Subjective results
HM5.0
JCTVC-H0148
RaceHorses, LD HE, QP42, Frame 218

## Slide 10: Subjective results
HM5.0
JCTVC-H0148
BasketballDrill, RA HE, QP42, Frame 107

## Slide 11: Conclusion
Introduction of adaptive weighting factors in the deblocking filter to adapt to varying signal statistics
Estimation of weighting factors by minimization of mean squared reconstruction error for subjective important samples
Coding and transmission of estimated weighting factors
Results compared to HM5.0:
  Visibly improved subjective quality
  Same objective quality
  Same run times
Proposal: Inclusion into CD/WD and HM