## Slide 1: JCTVC-H0177: Use of chroma phase in LM mode
C.Gisquet, E.Francois
JCT-VC 8th Meeting, San Jose, Feb, 2012

## Slide 2: Chroma phase in current HM design
LM mode explicitly links chroma samples to luma samples
  chroma samples position (chroma phase) related to luma samples should be taken into account
Definition for 4:2:0:
  Cx,Cy indicate the grid position
  Nominal case: Cx=0,Cy=1
In current HM design
  Syntax element chroma_format_idc indicating the chroma format (i.e. YUV4:2:0, …)
  Left samples: RecL’[-1,y] = ( RecL[-1,2y] + RecL[-1,2y+1] ) >> 1
  Inner samples: RecL’[x,y] = ( RecL[2x,2y] + RecL[2x,2y+1] ) >> 1
  Top samples: RecL’[x,-1] = ( RecL[2x-1,-1] + 2RecL[2x,-1] + RecL[2x+1,-1] + 2 ) >> 2

## Slide 3: Proposal : generalize LM mode for other chroma phase
SPS/PPS syntax change: signal horizontal/vertical chroma phase
  Possibly insert other information
    Such as those defined in AVC Video usability information, resolution ratio luma/chroma …
New RecL’ samples interpolation depending on the chroma phase
  several filters experimented – following filters are recommended
 | Top | Left | Inner | comments
Cx=0, Cy=0 | [1,2,1]/4 horiz | [1,2,1]/4 vertic | [1,2,1]/4 horiz | 
Cx=0.5, Cy=0 | [1,1]/2 horiz | [1,2,1]/4 vertic | [1,1]/2 horiz | symmetrical version of the current HM filter
Cx=0.5, Cy=0.5 | [1,1,1,1]/4 horiz | [1,1,1,1]/4 vertic |  | 

## Slide 4: Syntax
seq_parameter_set_rbsp( ) { | Descriptor
profile_idc | u(8)
reserved_zero_8bits /* equal to 0 */ | u(8)
level_idc | u(8)
seq_parameter_set_id | ue(v)
chroma_format_idc | ue(v)
if( chroma_format_idc = = 1 ¦ ¦ chroma_format_idc = = 2 ) { | 
chroma_phase_x | u(1)
chroma_phase_y | u(1)
} | 
max_temporal_layers_minus1 | u(3)
… | 
rbsp_trailing_bits( ) | 
} | 

## Slide 5: Evaluation
2 sets of 4:4:4 RGB sequences considered, converted to 4:4:4 YUV
  Class P: 1080p sequences used for the AVC professional extension
  Class S: 2 1080p sequences, 2 2160p (3940x2160) sequences from SVT
Each sequence converted into 8 different YUV 4:2:0 versions, corresponding to 8 different horizontal/vertical chroma phases
  Using non-normative downsampling filters from JSVM
4 HM versions used:
  HM_V0 : default HM5.0 Cx=0, Cy=0.5
  HM_V1 : LM adapted for Cx=0, Cy=0
  HM_V2 : LM adapted for Cx=0.5, Cy=0
  HM_V3 : LM adapted for Cx=0.5, Cy=0.5
Conversion tools and modified HM provided with the contribution

## Slide 6: Results
 |  | Reference HM_V0: Cx=0, Cy=0.5 |  |  |  |  |  |  |  |  | 
Phase of input sequences |  | HM_V1 Cx=0, Cy=0 |  |  | HM_V2 Cx=0.5, Cy=0 |  |  | HM_V3 Cx=0.5, Cy=0.5 |  |  | 
Cx | Cy | Y | U | V | Y | U | V | Y | U | V | Best version
0 | 0 | -0.1 | -1.1 | -1.5 | 0.0 | 0.3 | 0.3 | 0.1 | 1.5 | 1.0 | HM_V1
0.25 | 0 | -0.1 | -1.4 | -1.5 | 0.0 | -1.1 | -1.4 | 0.0 | -0.3 | 0.0 | HM_V1
0.5 | 0 | -0.1 | -1.3 | -1.2 | -0.1 | -2.8 | -2.7 | -0.1 | -2.0 | -1.4 | HM_V2
0.75 | 0 | -0.1 | -1.2 | -1.0 | -0.2 | -4.2 | -3.5 | -0.2 | -3.4 | -2.3 | HM_V2
0 | 0.5 | 0.3 | 4.9 | 2.6 | 0.4 | 7.3 | 3.8 | 0.1 | 1.5 | 1.4 | HM_V0
0.25 | 0.5 | 0.3 | 5.0 | 2.6 | 0.3 | 5.2 | 2.6 | 0.0 | -0.6 | -0.2 | HM_V3
0.5 | 0.5 | 0.3 | 4.8 | 2.5 | 0.2 | 3.0 | 1.1 | -0.1 | -2.6 | -1.9 | HM_V3
0.75 | 0.5 | 0.3 | 4.2 | 2.1 | 0.2 | 0.9 | -0.2 | -0.2 | -4.2 | -2.8 | HM_V3

## Slide 7: Conclusions
Natural extension of LM mode to take into account chroma phase
  Insert chroma format information signaling in SPS/PPS
  Adapt Luma samples interpolation based on these chroma format information
  Current proposal handles 4:2:0 content
  Can be generalized to other formats (4:2:2, interlaced with ¼ chroma phase)
  Chroma Gain using the right filters observed in all tested cases (up to -0.2% Y, -4.2% U, -3.5% V)