## Slide 1: JCTVC-H0200 AHG21: Comments on Signaling of LTRPs
LG Electronics

## Slide 2: Summary
Method for signaling of LTRPs seems can be further improved
Two main concerns:
  1st problem: inability to handle situation when there are more than one LTRPs in DPB with same delta POC LSB relative to that of current slice.
  2nd problem: bit count to send delta POC LSB is relatively big
    May not be easy to reduce this
We propose solution to both concerns above
Proposed items:
  Replace delta_poc_lsb_lt_minus1 [i] with delta_poc_lsb_lt [i]
    May solve 1st problem above
  Allow encoder to skip signaling delta poc lsb lt of LTRPs without making it removed from DPB
    May ease 2nd problem above

## Slide 3: Handling two LTRPs with same delta POC LSB
Situation:
  In DPB, there is already one LTRP with POC 21
  At POC 296, it is decided that pic with POC 280 should be an LTRP
According to current LTRP signaling scheme, POC 21 must be removed from DPB
ingThis can be solved by simply replace delta_poc_lsb_lt_minus1 [i] with delta_poc_lsb_lt [i]
With the proposed change:
  delta_poc_lsb_lt [0] = 16  correspond to LTRP with POC 280
  delta_poc_lsb_lt [1] = 0  correspond to LTRP with POC 21
21
280
296
MaxPocLsb = 256
Current Slice
1st LTRP
2nd LTRP
Delta POC LSB =16
Delta POC LSB % MaxPocLsb =16

## Slide 4: Handling two LTRPs with same delta POC LSB
Bit-count analysis:
  No significant bit increase for both agreed test cases (case 2.6 and case 3.3)
    For case 2.6: only 8 bits for over 4000 pictures and 12 bits for over 9000 pictures
    For case 3.3: only 1.7% for RTT 100 ms and 0.5% for RTT 200 ms
Error resilience analysis: No effect to error resilience feature of current signaling scheme
Case | Condition | Bits by current method |  | Bits by proposed method | 
 |  | 1st half | 2nd half | 1st half | 2nd half
Case 2.6 | 10s-20s-10s-20s | 31199 | 40628 | 31199 | 40636
Case 2.6 | 20s-60s-20s-60s | 62493 | 81676 | 62495 | 81686
Case 3.3 | RTT 100ms | 5191 | 5332 | 5283 | 5424
Case 3.3 | RTT 200ms | 6795 | 7580 | 6835 | 7620

## Slide 5: Reducing bit-count for sending delta POC LSB
Fact 1: Once selected / decided, LTRP usually does not change frequently
Fact 2: Delta POC LSB of all LTRP in DPB must always be signaled in slice header, otherwise they will be removed.
--Situation--
Given the following situation:
  Encoder knows that previous transmitted picture was safely received by decoder
  There is no changes in the LTRPs status in the DPB
--Question—
  Can we not send delta POC LSB of all LTRPs in DPB and ask decoder to not to remove them from DPB?

## Slide 6: Reducing bit-count for sending delta POC LSB
In the given situation, we can provide a feature to skip signaling delta POC LSB
21
150
151
LTRP
Set POC 140
as new LTRP
22
140
…
…
Confirmed safely received!
Confirmed safely received!
Skip signaling delta POC LSB
23
…

## Slide 7: Reducing bit-count for sending delta POC LSB
Bit-count analysis:
  Significant bit-count reduction is all agreed cases to be tested
Error resilience analysis
  Best use in the given situation
  Otherwise, may have some risk!
  Encoder has option whether or not to use this feature.
    Cost only 1 bit if encoder does not want to enable this feature
Case | Condition | Bits by current method |  | Bits by proposed method | 
 |  | 1st half | 2nd half | 1st half | 2nd half
Case 2.6 | 10s-20s-10s-20s | 31199 | 40628 | 9570 | 11978
Case 2.6 | 20s-60s-20s-60s | 62493 | 81676 | 19170 | 23978
Case 3.3 | RTT 100ms | 5191 | 5332 | 1999 | 2030
Case 3.3 | RTT 200ms | 6795 | 7580 | 1787 | 1870

## Slide 8: Conclusion
Proposed item 1:
  Simple change. Only removing ‘minus1’ term from current delta_poc_lsb_lt_minus1 [i]
  Can allow LTRP signaling to handle situation where there are more than one LTRPs with same delta POC LSB.
Proposed item 2:
  Provide a non-mandatory feature for skipping signaling delta POC LSB when there is no change to LTRP status and last transmitted picture is confirmed to be received safely.
Ask the JCTVC group to adopt the proposed changes