## Slide 1: Non-CE8: Method of removing boundary artifacts for SAO
<number>
JCTVC-H0201
Toru Matsunobu
Hisao Sasai
Takahiro Nishi
Panasonic Corporation
Notes: <number>

## Slide 2
<number>
Introduction
Motivation
  Visual artifacts are observed with some sequences by HM5.0.
(a) Original image
(b) Decoded image
of HM5.0
(c) Decoded image
of HM5.0 without SAO
(d) Difference of
(b) and (c)
BasketballDrill
6th frame
Al-HE
QP37

## Slide 3
<number>
Problems
BO(1) | EO(2) | EO(1) | 
BO(2) | BO(1) |  | 
EO(4) |  | OFF | EO(2)
 |  | OFF | OFF
Category(8)
Category(9)
Category(7)
Category 9
Category 8
Partition boundary
Category of BO
Intensity
SAO adds offset values to reconstructed samples at each partition and category individually.
Partitioning by SAO
Clustering by band offset of SAO
The difference between neighboring samples on the partition boundary is increased by addition of very different offset values.
Increased difference is visible as artifact

## Slide 4
<number>
Solutions
Proposal 1. weak offset for partition boundary
Proposal 2. weak offset for category boundary
Offset values are reduced
by using weight coefficients.
Weak offset values
near category boundary of band offset

## Slide 5
<number>
Results of simulation
BD-rate performance
 | All Intra HE |  |  | Random Access HE |  |  | Low delay B HE |  |  | Random Access HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Proposal 1. weak offset for partition boundary | 0.0% | 0.0% | 0.1% | 0.0% | 0.1% | 0.1% | 0.1% | 0.0% | 0.2% | 0.0% | 0.0% | 0.1%
Proposal 2. weak offset for category boundary | 0.1% | 0.3% | 0.5% | 0.1% | 0.3% | 0.5% | 0.3% | 0.5% | 0.8% | 0.1% | 1.4% | 2.0%
combination of proposal 1 and 2 | 0.1% | 0.3% | 0.5% | 0.1% | 0.4% | 0.6% | 0.3% | 0.9% | 1.1% | 0.1% | 1.5% | 2.2%
Anchor: HM5.0
Not significant loss (0.0~0.3%)
Similar to run time

## Slide 6
<number>
Results of simulation
Subjective quality
HM5.0
Combination of
proposal 1 and 2
Kimono1, 162nd B-Slice, LD-HE, QP37
Original
HM5.0 without SAO
Difference of
SAO on and off
proposal 1
proposal 2

## Slide 7
<number>
Results of simulation
Subjective quality
HM5.0
Combination of
proposal 1 and 2
SlideEditing, 97th I-Slice, RA-HE, QP37
Original
HM5.0 without SAO
Difference of
SAO on and off
proposal 1
proposal 2

## Slide 8
<number>
Results of simulation
Subjective quality
HM5.0
Combination of
proposal 1 and 2
Spincalendar, 386th b-Slice, RA-HE, QP37
Original
HM5.0 without SAO
Difference of
SAO on and off
proposal 1
proposal 2

## Slide 9
<number>
Results of simulation
Subjective quality
HM5.0
Combination of
proposal 1 and 2
BasketballDrill, 455th B-Slice, RA-HE, QP37
Original
HM5.0 without SAO
Difference of
SAO on and off
proposal 1
proposal 2

## Slide 10
<number>
Results of simulation
Subjective quality
HM5.0
Combination of
proposal 1 and 2
BasketballDrill, 6th I-Slice, AI-HE, QP37
Original
HM5.0 without SAO
Difference of
SAO on and off
proposal 1
proposal 2

## Slide 11
<number>
Results of simulation
Subjective quality
HM5.0
Combination of
proposal 1 and 2
BasketballDrive, 305th B-Slice, LD-HE, QP37
Original
HM5.0 without SAO
Difference of
SAO on and off
proposal 1
proposal 2

## Slide 12
<number>
Results of simulation
Subjective quality
HM5.0
Combination of
proposal 1 and 2
Spincalendar, 1st I-Slice, AI-HE, QP37
Original
HM5.0 without SAO
Difference of
SAO on and off
proposal 1
proposal 2

## Slide 13
<number>
Conclusion
We confirmed that the artifact was removed by our proposal on top of HM5.0.
Considering the good trade-off between the noticeable subjective quality improvement and the not significant BR-rate loss.
Recommendation
Inclusion of our proposed changes in the HM/CD
or further study of this subjective issue in CE/AHG toward DIS
Many thanks to TI for cross-check (JCTVC-H0439)