## Slide 1: JCTVC-H0203 AHG4: Further latency reduction of CABAC init for dependent tiles
LG Electronics

## Slide 2: Summary
In the 7th JCTVC meeting in Geneva, G197 was proposed and adopted
  Suggest to init CABAC prob table of the first LCU of the non-first dependent tiles from adjacent-left LCU
  Adv 1: lower processing latency
  Adv 2: remove requirement for column line buffer
CABAC init of the 1st LCU in first column, non-first row dependent tiles seems not covered yet by G197
Proposal: to complete method proposed in G197, apply the following CABAC init rule, for the 1st LCU of dependent tile:
  If neighboring-left LCU is available, init from adjacent-left LCU
  Else if neighboring-upper tile is available, init from adjacent-upper LCU
  Else, reset CABAC prob table.

## Slide 3: Summary
In the 7th JCTVC meeting in Geneva, G197 was proposed and adopted
  Suggest to init CABAC prob table of the first LCU of the non-first dependent tiles from adjacent-left LCU
  Adv 1: lower processing latency
  Adv 2: remove requirement for column line buffer
CABAC init of the 1st LCU in first column, non-first row dependent tiles seems not covered yet by G197
Proposal: to complete method proposed in G197, apply the following CABAC init rule, for the 1st LCU of dependent tile:
  If neighboring-left LCU is available, init from adjacent-left LCU
  Else if neighboring-upper tile is available, init from adjacent-upper LCU
  Else, reset CABAC prob table.

## Slide 4: CABAC Init of 1st LCU in dependent tile
Before the 7th JCTVC meeting
After the 7th JCTVC meeting
We think that it is a nice change
But, what about LCU #40?

## Slide 5: CABAC Init of 1st LCU in dependent tile

## Slide 6: CABAC Init of 1st LCU in dependent tile
Proposed
Improve latency processing
It can be implemented without requiring additional buffer
Would be nicely combined with what have been adopted from G197

## Slide 7: CABAC Init of 1st LCU in dependent tile

## Slide 8: Effect to coding performance
 | 4 tiles (2 rows -- 2 columns) |  |  | 16 tiles (4 rows -- 4 columns) |  | 
 | Y | U | V | Y | U | V
INHE | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0%
INLC | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | -0.1%
RAHE | 0.0% | 0.2% | 0.1% | 0.2% | 0.3% | 0.3%
RALC | 0.0% | 0.1% | 0.0% | 0.1% | 0.0% | 0.0%
LBHE | 0.0% | 0.1% | -0.1% | 0.3% | 0.4% | 0.3%
LBLC | 0.0% | 0.1% | -0.2% | 0.3% | 0.3% | 0.3%
LPHE | 0.0% | 0.1% | -0.1% | 0.3% | 0.4% | 0.3%
LPLC | 0.0% | 0.0% | 0.1% | 0.2% | -0.1% | 0.4%

## Slide 9: Conclusion
Method to further lower processing latency for dependent tiles is proposed.
Complement the adopted method proposed by G197
Small impact to coding performance
  More or less the same as performance reported by G197
Ask the JCTVC group to adopt the proposed changes