## Slide 1
Market needs and practicality of sub-picture based CPB operation
(JCTVC-H0215, m23090)
K.Kazui, J.Koyama, S.Shimada and A.Nakagawa
FUJITSU LABORATORIES LTD.
A.Duenas
CAVIUM
Copyright 2012 FUJITSU LIMITED
Notes: <number>

## Slide 2: Summary
This contribution provides information which confirms the needs and the practicality of the sub-picture based operation of CPB for interoperable ultra low delay video transmission.
  Original contribution: JCTVC-G188 at 7th meeting
Information includes
  AVC-based ultra-low delay codec in the market
  Ultra low delay video monitor
  Schemes to limit CABAC’s delay
<number>

## Slide 3: AVC-based ultra-low delay codecs
Vendor/Product | End to end Latency
CAVIUM CNW5302 | 2 ms
NEC VC-7710/VD-7710 | 10 ms
Hitachi HU-200EI/DI | 8-10 ms
IBEX HLD-3000 | 10 ms
HHI | 3 ms
Note: end to end latency cannot be achieved when following the method described on the Annex C (HRD) of AVC.
<number>

## Slide 4: Ultra low delay display
In the LCD monitor market, there are many monitors from several display vendors which have so-called "through mode" (or "instant mode" or "game mode") for gaming users.
The "through mode" provides low latency less than 1 frame period by skipping the storage of a picture in a frame buffer.
Example: Toshiba 32ZP2
  3ms delay for 2D video
<number>

## Slide 5: Proposed operation in JCTVC-G188
A picture is conceptually divided into M groups of treeblocks.
  Each group contains equal number of treeblocks.
  Example：1 Treeblock line
  The variable M is signaled in Buffering period SEI.
  Amount of bits of each group can be averaged by existing schemes such as the vertical intra line refresh scheme.
tr( n, i ): removal time of i-th group in picture n.
  tr( n, i ) = tr ( n - 1 ) + ( tr ( n ) - tr ( n - 1 ) ) * i / M
New buffer model
Decoding delay can be reduced to 1ms.
1920x1080/60Hz
1 group per 1 treeblock line
<number>

## Slide 6: CABAC’s delay (1/2)
Worst case latency is infinite.
  Outstanding bits in the encoder BAC
  Problematic for a encoder operating in ultra low delay mode since it is difficult to know in prior when bits corresponding to the last bin of a sub-picture are output from a CABAC engine.
MediaTek’s proposal
  The coding interval is adjusted when the number of outstanding bits reaches to the threshold.
  Originally proposed in JCTVC-F059
  JCTVC-G0271 at this meeting
  When this proposal is accepted, above problem is removed.
<number>

## Slide 7: CABAC’s delay (2/2)
There are other ways to set the upper bound of the BAC latency by proper control at an encoder side with minimal loss in coding efficiency and small complexity increase.
<number>

## Slide 8: Conclusion
There are the needs and the practicality of the sub-picture based operation of CPB for interoperable ultra low delay video transmission.
  AVC-based ultra-low delay codec in the market
  Ultra low delay video monitor
  Schemes to limit CABAC’s delay
We recommend to adopt new CPB operation described in JCTVC-G188.
<number>

## Slide 9
<number>