## Slide 1: JCTVC-H0216 Non-CE9: Modification of derivation process for MVP candidate in AMVP/Merge
<number>

## Slide 2
<number>
In MPEG4/AVC, the ranges of MV are restricted based on profiles and level in Annex A
  Ex) Horizontal motion vector range does not exceed the range of -2048 to 2047.75, inclusive, in units of luma samples
 Based on this restriction, a scaled MV range for temporal direct is also restricted with NOTE,
  NOTE4 – mvL0 and mvL1 cannot exceed the ranges specified in Annex A.
In HM5.0, there is no restriction of the ranges for a scaled MVP candidate  A mismatch might be happened in the decoded pictures due to the difference of the supported MV bit precision between encoder and decoder
  Ex) Encoder supports 32 bit precision for MV  scaled MVP can become 32 bit precision Decoder supports only 16 bit precision for MV  scaled MVP may become wrong due to overflow after scaling
To avoid such a mismatch, one approach is to add a NOTE such as below like MPEG4/AVC
  NOTE – mvLXCol cannot exceed the ranges specified in Annex X
This method does not affect a normative decoding process. However, an encoder has to take care of it by using some special tricks. For example,
  If a scaled MVP exceeds the specified ranges, encoder controls to select Intra mode, even though in the case of Inter mode is effective
  Encoder traces a scaled MVP candidate during 1st pruning and creating the additional candidate, and it controls not to select the candidate which is related to a scaled MVP candidate, which exceeds the specified ranges after scaling
These methods are too complicated so that there’re some possibilities to confuse encoder designers
Introduction

## Slide 3
<number>
Two methods are proposed to avoid mismatch due to the difference of the supported MV bit precision between encoder and decoder
Solution1 : Not appending MVP candidate which exceeds the specified ranges
  If mvLXCol exceeds the ranges specified in Annex X, it is not appended into MVP candidate list
Solution2 : Clipping MVP candidate into the specified ranges
  If mvLXCol exceeds the ranges specified in Annex X, it is clipped into the ranges
These methods affect a normative decoding process, however, it is not needed for an encoder to use any tricks for the mode decision to avoid mismatch
Proposed method

## Slide 4
<number>
Simulation Result of solution1 and solution2
Anchor: HM5.0
The proposed methods were implemented to HM5.0 software
MV bit precision was restricted to 16 bit, which can sufficiently cover the MV range for 8Kx4K images
No loss was observed for all test condition in both cases
In HM5.0, it’s considered that MV, which exceeds 16 bit precision, is not used

## Slide 5
<number>
Two modified method were proposed to avoid a mismatch due to the difference of the supported MV bit precision between encoder and decoder
It show no loss for all test conditions relative to HM5.0
We suggest one of proposed methods be adopted in the HM/CD of HEVC
Conclusion