## Slide 1
Introduction of AVC’s derivation process of chroma motion vector for interlace support
(JCTVC-H0222, m23097)
K.Kazui, J.Koyama, S.Shimada and A.Nakagawa
FUJITSU LABORATORIES LTD.
Copyright 2012 FUJITSU LIMITED
Notes: <number>

## Slide 2: Summary
We propose to introduce the chroma MV adjustment scheme of AVC for 4:2:0 interlace format.
  Significant improvement: +0.4 dB on average, up to +1.0 dB for chroma components
  Simple: No increase in computational complexity
  No delay of schedule: Well verified through AVC standardization
We also propose to introduce interlaced video related parameters into SPS and slice header similarly as in AVC.
<number>

## Slide 3: Introduction
Need for support of interlaced video
  Interlace is still the major video format in a broadcasting studio.
  Hot discussion at the 7th meeting
Chroma MV adjustment
  Adopted in AVC
  Proposed by 4 organizations
  A chroma MV is shifted according to the parities of a current picture and a reference picture.
  Activated only for 4:2:0 interlace format
  JCTVC-G196 reports +0.4 dB on average, up to +1.0 dB BD-PSNR improvement of chroma components.
<number>

## Slide 4: Chroma MV adjustment of AVC
if( progressive_frame == 0 && chroma_format_idc == 1 )
{
if ( ref_pic is top field and curr_pic is bottom field)
mvCLX[ 1 ] = mvLX[ 1 ] + 2;
else if (ref_pic is bottom field and curr_pic is top field )
mvCLX[ 1 ] = mvLX[ 1 ] - 2;
else
mvCLX[ 1 ] = mvLX[ 1 ];
}
else
{
mvCLX[ 1 ] = mvLX[ 1 ];
}
<number>

## Slide 5: Example of Chroma MV adjustment
Top
Top
Bottom
Bottom
Luma
Chroma
Y
Correct position
Y component of luma MV:
mvLX[ 1 ]= 1.0
<number>
shift
in units of 1/8 chroma line
Y component of chroma MV
(without adjustment)
mvCLX[ 1 ]= 1.0
Y component of chroma MV
(without adjustment)
mvCLX[ 1 ]= 0.75

## Slide 6: BD-PSNR (as shown in JCTVC-G196)
Random Access HE |  | BD-PSNR (dB) |  | 
 |  | Y | U | V
1920x1080 | Church | 0.00 | 0.09 | 0.06
 | Marching | 0.00 | 0.33 | 0.52
 | Walk | 0.00 | 0.46 | 0.48
 | WhaleShow | 0.00 | 0.23 | 0.29
832x480 | Flower | 0.02 | 1.01 | 0.38
 | Football | 0.00 | 0.38 | 0.18
 | Mobile | 0.06 | 1.05 | 1.16
 | TableTennis | −0.01 | 0.24 | 0.35
Overall 1920x1080 |  | 0.00 | 0.28 | 0.34
Overall 832x480 |  | 0.02 | 0.67 | 0.52
Overall |  | 0.01 | 0.48 | 0.43
Average coding gain of Cr: +0.48dB (RA_HE) +0.43dB (RA_LC) +0.27dB (LD_HE) +0.23dB (LD_LC)
Up to 1dB coding gain in chroma components on RA_HE condition
  “Flower garden”
  “Mobile and calendar”
Data is shown in BD-PSNR since evaluation of chroma performance in BD-bitrate may cause misleading
<number>
VS. HM4.0
Notes: This is the result obtained by chroma modification.
Average coding gains are from 0.48 to 0.23 dB.
And in some sequences, up to 1 dB coding gain is achieved in chroma components.
<number>

## Slide 7: Proposed syntax for field indication
  progressive_sequence in SPS
  Originally introduced in sequence extension of MPEG-2
  progressive_sequence equal to 0 indicates the coded video sequence contains field pictures only.
  When progressive_sequence does not appear in SPS, it is inferred to 1.
bottom_field_flag in slice header
  Originally introduced in slice header of AVC
  bottom_field_flag appears only when progressive_sequence is equal to 0.
  When bottom_field_flag does not appear in slice header, it is inferred to 0.
<number>

## Slide 8: Conclusion
We recommend to adopt AVC’s chroma MV adjustment in HEVC.
  Significant coding gain
  Negligible complexity increase
  No delay of schedule
We also recommend to adopt proposed syntax changes for field indication.
  SPS and slice header
<number>

## Slide 9
<number>