## Slide 1: Non-CE11: Sign Data Hiding without RDOQ JCTVC-H0227
Gordon Clare, Félix Henry, Joël Jung, Stéphane Pateux – ORANGE LABS
Notes: presentation title
<number>

## Slide 2: Purpose of this contribution
Decoder is identical to JCTVC-H0224 « CE11: Sign Data Hiding »
  Embedding the sign of the first coefficent in the parity of the residue
This proposal aims at showing the behaviour of Sign Data Hiding without using RDOQ (low complexity configuration)
The software was sent to CE11 members
JCTVC-H0227
Notes: presentation title
<number>

## Slide 3: How the encoder works
When the parity of the residue has to be changed, the quantized coefficent whose original value that is the closest to its nearest quantization interval frontier is changed by on in this direction.
Example
  ai is smaller than bi, ai becomes the cost of xi
  xi with the smallest cost is shifted by one
  here, xi is quantized to 1 instead of 2
JCTVC-H0227

0
1
2
3
4
ai
bi
xi
Notes: presentation title
<number>

## Slide 4: Performance
Remarks
  Homogenous gains across configs, luma/chroma, and QPs
  Higher gains without Class E
  All sequences were examined (and compared with reference ones) and no specific artefacts due to the use of Sign Data Hiding could be detected
 | AVE-RAGE | Intra LC | RA LC | LDB LC
BD Rate (no F) | -0.7% | -0.7% | -0.7% | -0.8%
Encoder runtime | 103% | 106% | 101% | 101%
Decoding runtime | 102% | 102% | 101% | 102%
JCTVC-H0227
Notes: presentation title
<number>

## Slide 5: Support slides
JCTVC-E196

## Slide 6: Data Hiding for compression
What do we call Data Hiding for compression?
  Avoid explicit transmission of a given syntax element
    (typically, a binary element)
  At decoding, derive its value from other elements
    (typically, their parity)
[1] JCTVC-A114, “Video coding technology proposal by France Telecom, NTT, NTT DoCoMo, Panasonic and Technicolor”, I. Amonou et AL, 1st JCTVC meeting, Dresden, April 2010
[2] J-M. Thiesse, J. Jung, and M. Antonini, “Data hiding of Intra prediction information in chroma samples for video compression,” Proc. IEEE International Conference on Image Processing, ICIP 2010, pp. 2861-2864, Hong Kong, September 2010.
[3] JCTVC-E428, “Low Complexity Embedding of Information in Transform Coefficients”, R. Cohen, S. Rane, A. Vetro, H. Sun, 5th JCTVC meeting, Geneva, March 2011
JCTVC-H0227
Notes: presentation title
<number>

## Slide 7: What is the purpose of Data Hiding here?
Sometimes, we are spending bits to distinguish between coding choices, while their RD cost is similar!
  This situation creates a « communication channel »
  Data Hiding attempts to use this channel
R
D
-
R
This is bad!
JCTVC-H0227

## Slide 8: Proposal
Modification of the residual block encoding and decoding
Can be summarized by:
  If there is enough “space”, hide the sign of the first non-zero coefficient into the parity of the sum of the residue
Convention
Parity | Sign
Even | +
Odd | -
JCTVC-H0227
Notes: presentation title
<number>

## Slide 9: Encoder
Checks whether the number of modifiable coefficients is larger than syntax element TSIG
  If no, normal encoding of the signs
  If yes,
    first sign is not encoded
    if the parity of the sum of the coefficients does not match the sign, modify amplitude to get a match
0
+3
-2
+2
0
0
+1
0
0
+1
0
0
…
First
non-zero
Last
non-zero
N Modifiable coefficients,
N>TSIG?
Quantized
residual block
JCTVC-H0227
Notes: presentation title
<number>

## Slide 10: Decoder
Checks whether the number of modifiable coefficients is larger than syntax element TSIG
  If no, normal decoding of the signs
  If yes, first sign is inferred from the parity of the sum of the residue
0
3
2
2
0
0
1
0
0
1
0
0
…
First
non-zero
Last
non-zero
N Modifiable coefficients,
N>TSIG?
Quantized
residual block
JCTVC-H0227
Notes: presentation title
<number>

## Slide 11: Remarks
The decoder behaviour is very simple and specified
The way the encoder modifies the parity of the residue, when needed, is up to the encoder designer, provided that
  The first non-zero coefficent cannot become zero
  The number of modifiable coefficient become smaller than TSIG
The designer of the encoder can choose its own complexity/performance trade off
We present in the next slide our own approach
JCTVC-H0227
Notes: presentation title
<number>

## Slide 12: Encoder used in for the current proposal
Non normative
If a change of the parity is required, we will shift one coefficient by 1, among the modifiable coefficients
  based on RD cost minimization
We re-use the RD costs already computed during RDOQ
In order to increase the chances of finding a modification with a low RD cost, the following steps are implemented in the proposed encoder:
  Zero quantized coefficients can be shifted by one (in the direction of the original value of the coefficient)
  The quantized coefficients having an amplitude of one can be shifted by one in both directions
The above additionnal explorations are NOT used to improve RDOQ
JCTVC-H0227

## Slide 13: Tests conditions
HM5.0,
JCTVC-G1200 test conditions,
High Efficiency
  TSIG values:
JCTVC-H0227
Notes: presentation title
<number>

## Slide 14: Where does the gain come from?
R
D
-
R
D
-
R
D
-
50%
1 bit
50%
x
x
x
x
x
x
x
x
JCTVC-H0227

## Slide 15: Conclusion
Exploits a new source of rate reduction
  Transmission of equiprobable signs into an existing « channel »
  Additive to most other sources of improvement
Gains are homogenous
Almost no increase in decoder runtime
Small increase in encoder runtime
  Proposed encoder is just one straightforward implementation
  Certainly possible to improve
Proposed for adoption
  WD text is provided
  Crosscheck by RIM (JCTVC-H0XXX)
or
JCTVC-H0227