## Slide 1: JCTVC-H0264: Design considerations for Adaptive Resolution Coding (ARC)
Thomas Davies (Cisco)

## Slide 2: Background
Changing resolution is valuable
  - for reducing complexity
  - matching resolution to a display
  - bandwidth reduction
Simple resolution adaption proposed in JCTVC-F158 by reference frame resampling – no need for SPS and Intra frame
Coding gains, substantial for some sequences, reported at high QP in JCTVC-G264

## Slide 3: Issues
In principle resolution could change every frame:
  Number of reference frames resampled at once
  Frequency with which resolution is changed up and down
Complexity of filtering: how simple can the resampling filters be?

## Slide 4: Constraining resampling
Limit the number of resampling operations per frame period
  Level constraint max_ref_resamples_per_frame
Limit the frequency with which resolution can be changed:
  Level constraint min_ref_res_changes_interval

## Slide 5: Resolution change down

## Slide 6: Resolution change up

## Slide 7: Short-length filter test
Tested various short filters for normative reference resampling (green in figures)
Keeping picture resampling (red in figures) the same: h11/f7 filters from JCTVC-F618
Upsampling: tested 2 filters – zero phase linear interpolation; quarter-phase DCTIF
Down-sampling: tested 3 filters – 3 lobe filter (-1, 0, 9, 16, 9, 0, -1)/32; half-phase linear; half-phase 4 tap filter
Anchor: use the same h11/f7 filters

## Slide 8: Upsampling
No significant effect – linear results are:
BD-rate (%) | High Efficiency |  |  |  | 
Class | LB_HE | LP_HE | LB_HE10 | LB_LC | LP_LC
Class A | 0.1% | 0.4% | 0.1% | 0.0% | 0.3%
Class B | 0.0% | 0.1% | 0.0% | 0.0% | -0.1%
Class C | 0.0% | 0.1% | 0.1% | 0.0% | 0.0%
Class D | 0.0% | 0.1% | 0.0% | 0.1% | -0.1%
Class E | 0.1% | -0.2% | 0.0% | 0.0% | -0.8%
Average | 0.0% | 0.1% | 0.1% | 0.0% | -0.1%

## Slide 9: Downsampling
More dependency on filter type. Best is 3-lobe Lanczos:
BD-rate (%) | High Efficiency |  |  |  | 
Class | LB_HE | LP_HE | LB_HE10 | LB_LC | LP_LC
Class A | 0.2% | 0.9% | 0.1% | 0.2% | -1.3%
Class B | 0.2% | 0.8% | 0.2% | 0.3% | 0.1%
Class C | 0.2% | 0.8% | 0.2% | 0.3% | 0.6%
Class D | 0.2% | 0.6% | -0.1% | 0.5% | 0.4%
Class E | 0.2% | 1.9% | 0.1% | 0.4% | 1.6%
Average | 0.2% | 1.0% | 0.1% | 0.3% | 0.2%