## Slide 1
JCTVC-H0244
Non-CE6: Intra-mode bypass parallelism (IMBP)
8th JCT-VC meeting, Feb 2012.

## Slide 2: Background information:
Intra-prediction mode coding in HM-5.0
  Arithmetic coded: prev_intra_luma_pred_flag
  Bypass coded: mpm_flag or rem_intra_luma_pred_mode
Each intra-predicted PU has bypass coded data.
  Parsing throughput is an issue in intra-predicted frames.
  Concatenation of bypass coded data is used in transform coefficient coding to increase throughput.

## Slide 3: Proposal
Concatenate the bypass-coded portions of the intra_mode for each PU within an LCU.
Concatenate the bypass-coded portions of the intra_mode for each PU within an LCU.
  Firstly parse the CU structure and prev_intra_luma_pred_flag data for LCU
  Then parse mpm_flag/rem_intra_luma_pred_mode for LCU.
  Finally parse transform tree.
Benefit: Concatenated bypass-coded data may be fetched together for higher throughput.

## Slide 4: Benefit
~25% of all encoded bins in a stream are EP-coded;
~40% of all EP-coded bins (or about 10.5% of all stream bins) are optimized with IMBP;
IMBP groups relevant EP-bins, reducing the total number of EP-chunks in the stream by ~48%;
After IMBP grouping the average length of relevant EP-chunks increases from 2.5 bins per chunk to 151.6 bin per chunk;

## Slide 5: Results